## Slide 1: Design of metadata schemas for ion chromatography in applied plasma sciences
Robert Wagner
Leibniz Institute for Plasma Science and Technology
Greifswald, Germany

## Slide 2: Motivation
Many different scientific fields in applied plasma science
Analytics are often needed to evaluate the plasma application
Example:
Suitable analytic for this use-case is ion chromatography (IC)
IC data are mostly evaluated by manual means and often lack proper FAIRness (Findability, Accessibility, Interoperability and Reusability)
This talk addresses our approach of a “FAIRer” workflow

## Slide 3: What is ion chromatography (IC)
Physico-chemical analysis method
Used to determine the ion composition of liquid samples
Two major variants, anion chromatography and cation chromatography
Used in different fields such as environmental sciences, food technology and applied plasma sciences

## Slide 4: Challenges in IC
No modern norms available (ASTM norm from 1993 with reapproval in 2019)
No open metadata standard and ontology for IC available
Publications often do not mention all necessary information for method adaptation
  Related but more known analytics like LC-MS have similar problems

## Slide 5: Schema creation workflow

## Slide 6: The designed metadata schemas
Data citation Inform...
Insrument method
Processing method
Column properties
Sample properties
Quality assurance
Sequence name
Date of measurement
IC Schema
Pump settings
Eluent generator settings
Sampler settings
UV/VIS detector
Conductivity detector settin...
Suppressor settings
Standard detection windows
pH
Conductivity
Redox potential
Dilution factors
Guard column specs
Separation column specs
Background conductivity
System pressure at start
Capacity factor
Linear velocity of mobile ph...
HETP
Mandatory information accord...
condensed

## Slide 7: The IC metadata schema
JSON schema based on ASTM E 1151 and own measurement experience
Refined with user experience of scientist from different fields
Already integrated in the IC workflow in the INP along with other research data management (RDM) tools
A couple of months later …
X
X
X
Without RDM
With RDM

## Slide 8: Data composition of an “IC - Experiment”
report
raw data
metadata
Information about the labeled peaks, areas,
retention times and the audit trail (device specific and time stamped metadata)
Information about the measured conductivity over the measurement time, the used detector channel and some device metadata (more detailed in the report)
Metadata from the sample preparation, device setup, methodology, data processing method, quality assurance

## Slide 9: New data management supported workflow
 Already realised
 In development
Device software

## Slide 10: Outlook and current research
The design of a proper IC ontology for further FAIRification is in progress
The visualization of the experimental data structure via graph database (Neo4J) is in development to increase the findability and accessibility of experimental data
  Planned incorporation of ELN experiments, stored metadata and the INPTDat repository
The last step in the planned workflow is the transition of manual data evaluation to (semi-)automated data evaluation to further increase the interoperability and reusability

## Slide 11: Example use-case

## Slide 12
Thank you for your attention!