## Slide 1
Luis Velasco (Universidad Politécnica de Catalunya, Spain),
Roberto Proietti (PoliTo, Italy)
7th of May 2024.
Workshop
Security in Classical Optical Communications and Quantuum Technologies
QKD endpoint software security: A talk to better grasp attacks plausibility and their remediations.
Vincent Lefebvre, sarl TAGES SOLIDSHIELD
vincent@solidshield.com
Grant Agreement number: 101096466

## Slide 2
ETSI QKD SECURITY WG

## Slide 3
ETSI QKD API specs
“SAE and KME software shall be protected while this is outside the scope of the specifications”
Secure Application Entity (SAE)
use the Quantum channel Keys for Encrypting the data channel. These keys are generated and delivered by the Key Management Entities (KME)

## Slide 4
THREAT MODELS ON SAE/KME
SAE impersonation
SAE tampering
Data Channel Link Break
DoS on KMEs and SAEs
SAE vulnerable variant

## Slide 5
SAE vulnerability exploit
Objectives:
Priviledge escalation,
code njection,
ROP, ...
Security Boundery
Conditions:
Code or dependency static analysis
Overflow-based, exception-based, backdoors
On main or dependencies
Data input channel
SAE SW
Dependency

## Slide 6
SAE Impersonation
Objective: Get out of the security boundary
Conditions:
Get access to SAE SW
Get access to SAE ID
SAE to KME link security
SAE to KME link is based on HTTPS (authentication + encryption)
SAEs, KMEs are identified with their unique ID (MAC)
The security of the ID is out of the scope of the specifications
Security Boundary
SAE A SW

## Slide 7
SAE Tampering
Objective: Modify SAE
Security Boundary
Conditions:
Get access to the SAE .exe file or to the SAE DRAM memory pages
SAE SW
Key export
Key tamper for (secure) Data Channel break

## Slide 8
DoS attacks on KMEs
Objectives:
Generate large volume of HTTP or HTTPS requests (HTTP flood
Generate SSL/TLS exhaustion
Saturate KMEs with fake GetKey Requests
Conditions:
Access to KMEs API (and URL)
Replicate SAE with ID
KME SW
SAE SW
SAE SW
SAE SW
SAE SW
SAE SW
SAE SW
SAE SW
SAE SW
GetKey!
GetKey!
GetKey!
GetKey!
GetKey!
GetKey!
GetKey!
GetKey!

## Slide 9
DoS attacks on SAE
Objective: SAE Ressource exhaustion
Conditions:
-Install Resource Burner as a sibling on the same platform
SAE SW
Resource Burner

## Slide 10
PLAUSIBLE ATTACKS?
Vulnerability exploit: To be analysed with input channel, maintenance channel, dependencies, SBOM, on both side KME and SAE
SAE impersonation: Depends on SAE’s ID security and protocole to exchange the ID (MACsec, ...)
SAE tampering: Depends on reality of:
  Code accessibility
  Remote attestation, runtime verification, placement in TEE, code encryption
DoS on KME:
  No need to break HTTPs authentication to spawn the DoS attack
  Flood legitimate requests requires the connection of multiple SAE on a single KME (as is specified by ETSI)
DoS on SAE: Depends on white listing enforcement.
An high-level attack plausibility analysis:
QKD are supposedly used for highly secured communications...
Motivation is HIGH to break the weak link

## Slide 11
Attack vector | TEE remediation | Information
SAE Vulnerability | Obscurity | Pro: TEE protects the confidentiality of SAE once inside the TEE and if encrypted before reaching it. Cons: Evil TEE attack.
SAE Impersonation | Through Machine binding | Reminder: TEE remote attestation attests that the code is inside a TEE, without specifying which precise TEE (ie, host) Machine binding requires a secret to be provisionned on the machine.
SAE tampering | If TEE remote attestation is produced | Integrity assurance at the highest trustworthiness
DoS on KME | None | TEE are exposed to availability attack due to integrity hard locking policy (ie, raw hammering attack on DRAM). This attack can be circumvented with white listing
DoS on SAE | None | TEE are exposed to availability attack due to integrity hard locking policy (ie, raw hammering attack on DRAM). This attack can be circumvented with white listing
TEE inherent costs
Vendor-specific, Performance and Memory consumption.
TEE remediation table
IEEE Security and Privacy Journal May 2023, SWOT of TEE for the Telecom Industry. Lacoste Marc, Lefebvre Vincent

## Slide 12
Hardening inherent costs: Latency, performance
Hardening techniques
Attack vector | Hardening remediation | Requirements
SAE or KME Vulnerability | Obscurity SBOM enforcement | Text section encryption SBOM enforcement with lib verification prior call jumps
SAE Impersonation | Singularization Machine binding | Software singularization for unique identification Software-to-Platform binding: Create an artificial semantic link to a secret Provision the secret on the platform, inside or outside a TEE
SAE tampering | Attestation at load time, runtime verifications | Self-attestation, remote attestation, possible leverage of DLT Runtime verification (partial / complete footprint measurements) with the trade-off (security/penalty)
DoS on KME (by SAE replication, legit request) | SAE execution control by sparing OTTs | Create a semantic dependence of the program modified bootstrap phase, based on process launch-dependent elements. At program start, the modified bootstrap transfers of these elements to OTT server which retutrns corresponding unforgeable OTT, with adhoc rate-limiting policy.
DoS on SAE (by sibling attrition) | CPU resource governance | Runtime heartbeats Root priviledge for resource priotization

## Slide 13
Takeaways
Must- and Best-Haves
Better-Do
ETSI QKD WG is well-advised.
Attack plausibility must be defined in consideration of the ultra-high data confidentiality promises of QKD, attack-exposed at its weak point. (i.e., software components).
MUST-HAVEs:
  Standard vulnerability removal and/or code confidentiality preservation, secure SBOM, remote attestation and white listing are ground zero requirements.
  SAE runtime integrity (by TEE or runtime permanant verification)
BEST-HAVEs:
  SAE and KME trustworthy identity by hardware anchoring (e.g., PUF, in-TEE anchor, in-EE anchor).
  Against KME DoS. Application-level request flood can be remediated by One-Time execution Tokens delivered per instance (per SAE ID)
  Singularization of SAE/KME instances for accurate trailing with runtime heartbeats reflecting correct functioning states.
  DLT perpetual security logs for RCA and efficient and shared dynamic security
BETTER-DOs:
  Apprehend the possible conflict between Availability and Integrity.
  Comprehend the hidden costs of security (performance, memory consumption, deployment restrictions).

## Slide 14
Thanks for your attention.
Gracias. Grazie.
QKD endpoint software security: A talk to better grasp attacks plausibility and their remediations.
Vincent Lefebvre, sarl TAGES SOLIDSHIELD
vincent@solidshield.com