## Slide 1: Quick introduction to GRID2DEMAND
Notes: Hi everyone! Thanks for the invitation!
I’m so happy to share with you about the quick demand generation tool, Grid2demand.

## Slide 2
INPUT files
Network files in GMNS format can automatically generated by OSM2GMNS tool.
POI data may need manual modification, because building types extracted from OpenStreetMap do not follow a land use type standard.
(Optional) Users can give a customized trip rates table in advance or edit the default table.
Output demand and agent files are aligned with standard travel models for static and dynamic transportation management and planning.
Notes: Let’s look at the framework.
Firstly, network files including POI data are prepared by osm2gmns. The network files and poi trip rate table are the input. It’s OK if there’s no trip rate table.
Then based on four-step travel model, 1) we partition zones by grid, 2) forecast production and attraction for each POI node, boundary node and residential node, 3) and calculate zone-to-zone accessibility.
Finally, apply a classical gravity model to perform trip distribution and randomly get node-to-node demand for assignment.
The output demand and agent files are aligned with standard travel models for static and dynamic transportation management and planning.

## Slide 3
Export a network file from OpenStreetMap.
Use OSM2GMNS tool to convert the network from OpenStreetMap to a routable transportation network with .csv files in standard GMNS format. (https://github.com/asu-trans-ai-lab/OSM2GMNS)
Step 1: Network preparation
Road network
Road network with Point Of Interest (POI)
Notes: The first step to apply grid2demand is network preparation.
The .osm file of the area of interest can directly exported from OpenStreetMap. And use osm2gmns to convert the network into a routable .csv files in GMNS format.
POI data may need manual modification, because building types extracted from OpenStreetMap do not follow a land use type standard.

## Slide 4
Step 2: Import GRID2DEMAND and read the network data
Step 3: Partition Grid into cells
Grids can be automatically generated by a given number of grid cells or cell's width and height in meters.
Notes: Then, import grid2demand. Input the number of grid cells or cell size you’d like. Grids can be automatically generated.

## Slide 5: Why grid zones?
TAZ based on census tracts
Grid zones
Land use is ignored in TAZs. The spatial biases may deteriorate the accuracy of travel demand.
Trip generation directly comes from activity nodes, which is aggregated in grid zones. Smaller grid, more accurate demand.
Census tract
Grid cell
Zones partitioned by grids could reduce spatial biases.
Notes: You may ask why we partition zones by grid.
Let’s see the left side first. The red boundary is a census tract. If we directly regard it as a traffic analysis zone, most travel demand come from the north side. And TAZs have different shapes and sizes. Such spatial biases may deteriorate the accuracy of travel demand.
However, zones partitioned by grids with same size could reduce the spatial biases. Trip generation directly comes from activity nodes aggregating in each grid.

## Slide 6
Step 4: Get production/attraction rates of each land use type with a specific trip purpose
Users can customize trip purpose and poi_trip_rate.csv. Default trip rates are collected according to ITE trip generation rates tables.
The values of production and attraction of each POI node are calculated according to land use type, trip purpose and the area of the building (or other unit of measurement).
A sample of poi_trip_rate.csv
Notes: In the fourth step, we’re going to get POI production and attraction rates of each land use type with a specific trip purpose.
Users can customize trip purpose and trip rate table. Default trip rates are collected according to ITE trip generation rates table.

## Slide 7
Step 5: Define production/attraction values of each node according to the node’s activity type
Three kinds of nodes in the network can generate travel demand: 1) POI nodes, 2) residential nodes, and 3) boundary nodes.
Users can customize production and attraction values of residential nodes and boundary nodes.
A sample of updated node.csv
Notes: There are three kinds of nodes can generate travel demand.
The values of production and attraction of each POI node are calculated according to land use type, trip purpose and the area of the building (or other unit of measurement).
For residential nodes and boundary nodes, users can directly customize the production and attraction values.
In step 5, the values of production and attraction of each node are obtained.

## Slide 8
Step 6: Calculate zone-to-zone accessibility
A degree at different latitudes represents different lengths on a flat surface. Users need to input the latitude of the area of interest for converting x/y coordinates into
lengths on a flat surface.
A sample of accessibility.csv
Currently, accessibility is measured by straight-line distance between zone centroids.
Notes: Next step is to calculate accessibility. A degree at different latitudes represents different lengths on a flat surface. We need to convert x/y coordinates into lengths on a flat surface. According to the input latitude of the area of interest, equivalent length will be used in the tool.
Currently, accessibility is measured by straight-line distance between zone centroids. Later, we’ll calculate realistic travel distance with a Shortest Path Algorithm.

## Slide 9
Step 7: Apply gravity model to perform trip distribution
For each OD pair, a typical gravity model is applied to calculate zone-to-zone demand volume.
Default values of friction factor coefficients under a specific trip purposes
where,
: Trips from zone to zone ; : Productions in zone ; : Attractions in zone
: Friction factor for travel from zone to zone ;
: Correction factor for travel from zone to zone . Default value equals to 1;
: Accessibility from zone to zone ;
: Friction factor coefficients.
Trip Purpose | a | b | c
1 (HBW) | 28507 | -0.02 | -0.123
2 (HBO) | 139173 | -1.285 | -0.094
3 (NHB) | 219113 | -1.332 | -0.1
Notes: Finally, a typical gravity model is utilized to get zone-to-zone demand volume.

## Slide 10
Step 7: Apply gravity model to perform trip distribution
Users can specify a trip purpose to use default coefficients or customize friction factor coefficients.
A sample of output demand.csv
Notes: The coefficients of friction factor function can use the default values under a specific trip purpose or customize as well.

## Slide 11
Step 8: Generate Agent
Based on zone-to-zone demand volume, agent-based node-to-node demand will be generated randomly.
A sample of output input_agent.csv
Notes: Based on zone-to-zone demand volume, agent-based node-to-node demand will be generated randomly, which is ready for assignment.

## Slide 12
All features are stored with geometry (i.e. x/y coordinates). It’s readily to visualize the output demand.csv and other features in QGIS.
Visualization
https://colab.research.google.com/github/asu-trans-ai-lab/grid2demand/blob/main/osm2gmns.ipynb
Notes: Due to all features stored in .csv format with geometry field, so it’s easy to visualize the output demand and other features in QGIS.
OK, this is a quick introduction to Grid2demand. Let me show you with an online demo now.