## Slide 1
DA SS
V.Egorov DLNP JINR, Dubna
(on behalf of the DANSS collaboration)
JINR
Dubna
Detector of the reactor AntiNeutrino based on Solid-state Scintillator
ITEP
Moscow

## Slide 2
Neutrino experiments at the Kalinin NPP
(Tver region, 285 km NW from Dubna)
GEMMA
(Neutrino Magnetic Moment)
DANSS
(reactor monitoring and search for sterile neutrino oscillations)
GeN
(Coherent -Ge scattering)
Pressurised Water Reactor (ВВЭР-1000)
Thermal Power: 3 100 MW
Neutrino Flux: / 4 / day
Campaign: 18 months
4
3
2
Notes: For more than 15 years we perform neutrino experiments at the Kalinin NPP located in Russia, between Moscow and SPb. The plant used 4 Pressurised Water Reactors of 3.1 GW thermal power each.

## Slide 3
Core of
ВВЭР-1000
room А336
Cooling Pond
Reactor building of the B-320 project
Overburden
(reactor, building, shielding, cooling pond, etc.):
~50 m of W.E.
Technological room A336
just under reactor
9 m only!
5 1013 /cm2/s
Notes: Two of four reactor units belong to the project B-320 and there exists a room just under the reactor cauldron which is partly available for us. Being there, we are at 9 meter from the center of the core and exposed to a huge neutrino flux. Moreover, big amount of hydrogen-containing material above the room shields perfectly against fast cosmic neutrons (which is the main source of background). Such a close vicinity to the industrial reactor provides not only good experimental conditions, but some problems also.

## Slide 4
Normally, to detect neutrino one needs
at least 1 ton of (liquid) scintillator
Flammable
Explosive
Caustic
Toxic
Volatile
…

LS ≡ Persona non grata

## Slide 5
Instead, we use polystyrene-based plastic scintillator
highly segmented
interlayed with Gd

## Slide 6
25 X-Modules
25 Y-Modules
2500 independent scintillator strips
coupled to 2500 SiPM and 50 PMT
Modular structure provides 3d space pattern of each event
1m
1m
1m
1.1 tonne of PS = 5.1×1028 Hydrogen atoms
Basic element: polystyrene-based scintillator strip
JINST 11 (2016) no.11, P11011; arXiv:1606.02896 [physics.ins-det]
Notes: The detector consists of 2500 independent scintillator strips based on polystyrene. Each of them is coupled to individual photosensor. Each 50 strips are combined to intercrossing modules coupled to a small PMT. Such modular structure provides 3-dimensial space pattern of each event. So that we could see separately energy deposit of positron and that of annihilation photons. It helps a lot for the background suppression during analysis.

## Slide 7
Composite shielding against gamma-rays, muons and neutrons

## Slide 8: There are several ways to demonstrate neutrino oscillations:
Observe deficit or excess of counts with respect to theor. expectation
Observe deviation of the predicted spectrum shape
Observe evolution of the neutrino flux with distance
(model-independent, free of main systematic errors and therefore the most reliable)

## Slide 9
Dn
L=12.7 m
2.7 days
Up
L=10.7 m
2.0 days
Md
L=11.7 m
2.3 days
2 min
2 min
Dn
L=12.7 m
2.7 days
20 tn

## Slide 10
Aug 2015
V.Egorov
V.Belov
V.Brudanin

## Slide 11
Sep 2015

## Slide 12
Oct 2015
I.Zhitnikov

## Slide 13
Nov 2015

## Slide 14
Mar 2016

## Slide 16: Background monitoring
Permanent monitoring of gamma-BG with four NaI (3’x3’): 1 inside + 3 outside the DANSS shield
no (ON – OFF) visible difference
Permanent monitoring of neutron flux with three 3He neutron counters: 1 inside +2 outside the shield
Episodic measurements with HPGe and “MuMeter”
Φn = 0.57 outside (OFF)
Φn = 300.4 outside (ON)
Φn = 0.03 inside (OFF)
Φn = 0.04 inside (ON)
Φn = 6.0 en plein air

## Slide 17: Energy calibration with cosmic muons (see also poster #162 and arXiv:1804.04046[hep-ex] describing calibration and analysis details)

## Slide 18: Calibration with 22Na, 60Co, 137Cs, 248Cm (few Bq)
Teflon capillary
H(n,γ)
Gd(n,γ)

## Slide 19
Up , Md , Dn
m= 4.01  0.07
c =13.68  0.23
Off
N =1.52  0.05
N =3.20  0.02
248Cm
T (P-D), μs
Events / 200 ns / day
50 PMT only
An example of time distributions

## Slide 20
4051 Up ev / day
3476 Md ev / day
3022 Dn ev / day
333 Off ev / day
50 PMT only
An example of energy spectra (partial segmentation)

## Slide 21
50 PMT and
2500 SiPM
4910 Up ev / day
4101 Md ev / day
3490 Dn ev / day
133 Off ev / day
An example of energy spectra (full segmentation)

## Slide 22: IBD total rate vs effective distance
IBD intensity follows reasonably the 1 / L2 dependence.
Effective distance L takes into account real spatial distribution of the detection efficiency and the reactor core burning profile (monitored permanently by the KNPP staff) .
The time variation of reactor core burning profile is taken into account with a precision of 30 min and ~10 cm.
UP
MIDDLE
DOWN
Time evolution of the core burning profile
Reactor core center

## Slide 24: DANSS data taking
Variable distance to the reactor core: 10.7m (Up), 11.7m (Md), 12.7m (Dn)
Detector movement: 3 times per week (Down -> Up -> Middle -> Down…)
Raw DANSS data
The DANSS data
“fuel-corrected”
(except of the 1st month)

## Slide 30
Significance of the best regions
Results are preliminary:
more syst. effects are under study
BF: 2.8 σ
“ 3 σ means not a discovery, but just a cause of thinking”
A. Serebrov
Notes: ~

## Slide 31: Summary
DANSS is taking data since Apr 2016 (data available for analysis – since Oct 2016).
4910 IBD events/day are detected in the closest position
Background: 133 μ-induced events/day (2.7% for Up pos.)
Spectrum dependence on the fuel composition within the campaign is clearly visible and agrees with HM-prediction
A large fraction of allowed sterile oscillation parameters region is excluded in a model-independent way. The RAA point (Δm2=2.3 eV2, sin2(2)=0.14) is excluded at 5σ level.
The best point at (Δm2=1.4 eV2, sin2(2)=0.05) has 2.8σ significance.
DANSS data taking and analyses: on-going

## Slide 32
Thank you for attention

## Slide 33: Benchwarmers

## Slide 34
MC description of Gd(n,) spectrum (high-E part)