## Slide 1: Commissioning and calibration of the SoLid experiment
Nick van Remortel
University of Antwerp, Belgium
On behalf of the SoLid Collab.
Neutrino 2018, Heidelberg
June 8, 2018

## Slide 2
2
PI A. Vacheret CoG 682474 SOLID

## Slide 3: Motivation
Establish or disprove new neutrino eigenstates at m2O(1 eV2), see also reactor- and gallium anomaly
[Gariazzo et al., JHEP06(2017)135]

## Slide 4: Motivation
Establish or disprove new neutrino eigenstates at m2O(1 eV2), see also reactor- and gallium anomaly
Resolve discussion on spectral features observed by long baseline reactor expts using common fuels (235U, 238U, 239Pu, 241Pu)
[G. Mention et al., Phys. Lett. B773(2017)307]

## Slide 5: Motivation
Establish or disprove new neutrino eigenstates at m2O(1 eV2), see also reactor- and gallium anomaly
Resolve discussion on spectral features observed by long baseline reactor expts using common fuels (235U, 238U, 239Pu, 241Pu)
Several experiments taking data since 2018!
SoLid approach:
  energy measurement with plastic scintillator: Linear energy response (see eg. ESCAPE 2018)
  Very small segmentation:
    Topological event information & Bg reduction
    2D Oscillometry in E and L
  Using highy enriched 235U reactor fuel
[Gariazzo et al., JHEP06(2017)135]

## Slide 6: BR2 nuclear site
Compact research reactor
   50 cm and height 90 cm
  Fuel 93.5% 235U
  Thermal power 50-80 MW
  Duty cycle 150 days/year (~ 1 month cycles)
  SoLid at baseline 6-9 m
At ground level
  Overburden 10 mwe
  Muon rate: O(250 Hz)
  Cosmogenic neutrons
  Natural radioactivity

## Slide 7: SoLid detection principle
Anti-electron-neutrinos detected through inverse beta decay (IBD) in the composite (PVT + 6LiF:ZnS) scintillator element ( MeV)
Prompt positron signal
  Positron energy contained in one/two PVT cubes
  Allows precise localisation of IBD interaction
  Provides seed for anti-neutrino energy
Delayed neutron signal
  Neutron captured in 6LiF:ZnS close by + 4.78 MeV
  Capture time O(60 s)
Both signals
  Collected by WLS fibers in X and Y directions and transported to MPPC for readout
  Discrimination (ES – NS) based on pulse shape
JINST 12 (2017) no.04, P04024
JINST 13 (2018) no.05, P05005

## Slide 8: SoLid phase 1
SoLid detector cells: Cubes
  PVT cubes of 5x5x5 cm3 with 2 6LiF:ZnS neutron screens
  Optically isolated with Tyvek wrapping
arXiv:1806.02461

## Slide 9: SoLid phase 1
SoLid detector cells: Cubes
  PVT cubes of 5x5x5 cm3 with 2 6LiF:ZnS neutron screens
  Optically isolated with Tyvek wrapping
  Scintillation light extracted via 4 WLS fibers towards 2MPPC’s (SiPMs) in either direction

## Slide 10: SoLid phase 1
SoLid detector cells: Cubes
  PVT cubes of 5x5x5 cm3 with 2 6LiF:ZnS neutron screens
  Optically isolated with Tyvek wrapping
  Scintillation light extracted via 4 WLS fibers towards 2MPPC’s (SiPMs) in either direction
SoLid detection Modules
  5 modules of 10 planes each
  1.6 ton sensitive mass
SoLid detection planes
  Planes of 16x16 cubes = 64 RO channels give 3D topological information
  Plane readout & trigger:
    amplification& shaping
    Digitisation at 40 MHz - 2 Tb/s output for full detector
    Trigger logic in FPGA

## Slide 11: SoLid Phase 1
Container 2.4x2.6x3.8 m3
  Cooled to 10C to reduce MPPC dark count rate (1/3)
Shielding
  Water enclosure 50cm thick, 3.4 m high, 28ton
  Polyethylene ceiling 50cm thick, 6ton
  Cadmium lining
Automated calibration system for absolute efficiency and energy scale calibration at % level (207Bi, 60Co, 137Cs, 22Na, AmBe, 252Cf)  Full G4 simulation

## Slide 12: SoLid Phase 1
Container 2.4x2.6x3.8 m3
  Cooled to 10C to reduce MPPC dark count rate (1/3)
Shielding
  Water enclosure 50cm thick, 3.4 m high, 28ton
  Polyethylene ceiling 50cm thick, 6ton
  Cadmium lining
Automated calibration system for absolute efficiency and energy scale calibration at % level (207Bi, 60Co, 137Cs, 22Na, AmBe, 252Cf)  Full G4 simulation
Target sensitivity
  Energy resolution
  IBD efficiency 30%
  Signal-to-Background 3:1

## Slide 13: Quality control: CALIPSO
Automated scanner with active calibration head accommodating various neutron, electron/gamma sources:
  207Bi, 22Na, 137Cs, 60Co, …
  235Cf, AmBe
  16x16 cell plane in 4 hours
Employs same readout&DAQ as full detector
22Na Compton edge of 1270 keV gamma used for LY measurement
Poster: L. Manzanillas Monday #171 (Ballroom)

## Slide 14: Construction & Integration:
CROSS
Nov 2017

## Slide 15: Optical performance
99% of channel gains equalized to 1.4% spread
Linear energy response over wide range
Will add more sources/energies: Including conversion ’s from 207Bi
Exploit muons for real-time monitoring
Poster: L. Manzanillas Monday #171 (Ballroom)
And
arXiv:1806.02461

## Slide 16: Optical performance
Channel gains equalized to 1.4% spread
Linear energy response over wide range
Will add more sources/energies and exploit muons for real-time monitoring
Pre-integration calibration crosschecked & complemented by in-situ calibration
Light yield: 77 PA/MeV/cube (E)/E = 12% at 1 MeV
Very good consistency between 22Na and AmBe
SoLid Preliminary
Poster: L. Manzanillas Monday #171 (Ballroom)

## Slide 17: Trigger and DAQ
Dec 2017
Feb 2018
Construction & Quality Control
Commissioning at BR2
Installation
Nov 2017
Mar 2018
In-situ calibration
Physics

## Slide 18: Trigger and DAQ
Neutron trigger implemented in FPGA
  Based on scintillation signal induced in 6LiZnS: lots of secondary peaks
 Count number of peaks over treshold in sliding time window
  Read out long time buffer around NS: [-500 s, +200s]
See D. Saunders’ poster: #151 (Hölderlin-Room)

## Slide 19: Trigger and DAQ
Neutron trigger implemented in FPGA
  Based on scintillation signal induced in 6LiZnS: lots of secondary peaks
 Count number of peaks over treshold in sliding time window
  Read out long time buffer around NS: [-500 s, +200s]
Performance
  Trigger&PID efficiency 79  3 % (trig dominated)
  Trigger purity ~20%
  DAQ efficiency > 90%
purity
efficiency
Neutron trigger performance
See D. Saunders’ poster: Monday #151 (Hölderlin-Room)
SoLid Preliminary

## Slide 20: Neutron reconstruction
Validated in-situ with AmBe and 252Cf sources:  neutron detection efficiency per cube!
Average trigger  reconstruction efficiency: Improved from 75.8% to 79.4%  0.03% (stat)  3.1% (syst)
SoLid Preliminary
NS
ES
SoLid Preliminary

## Slide 21: Event Topologies: Muons
Exploit temporal AND spatial event information:
Muons: Tracking and dE/dx
Time Synchronisation Validation
Monitoring and pressure correction
SoLid Preliminary
SoLid Preliminary

## Slide 22: Event Topologies: IBD-like
Suppression of :
Accidentals:
  Distance prompt – NS: > 2 cubes
Fast neutrons:
  Recoils: high Energy & multiplicity
Muon induced NS:
  Muon veto time window
Intrinsic radio-contamination:
  214Bi->214Po and Rn:
    Energy
    timing
    Same-cube events
JINST 13 (2018) no.05, P05005

## Slide 23: NS-ES Time correlation
Reaction | Fitted capture time (s)
Spallation (NS after -track) | 65.3  1.3 (stat)
AmBe Calibration (NS after ) | 66.4  0.8 (stat)
IBD Simulation (NS after e+) | 63.3  0.1 (stat)
SoLid Preliminary
NS after 
NS after 4.4 MeV  from AmBe
NS after e+ from IBD
SoLid Preliminary
thermalised
epithermal

## Slide 24: IBD-like Rates
Preliminary rate monitoring, based on:
  Timing, Topology, Muon veto, Energy selection
Significantly higher IBD-like rate during reactor ON
Very low accidental rate
How does it behave?
SoLid Preliminary

## Slide 25: IBD-like Events
Preliminary rate monitoring based on:
  Timing, Topology, Muon veto, Energy selection
Significantly higher IBD-like rate during reactor ON
How does it behave?
  Spatially confined 
SoLid Preliminary
SoLid Preliminary

## Slide 26: IBD-like Events
Preliminary rate monitoring based on:
  Timing, Topology, Muon veto, Energy selection
Significantly higher IBD-like rate during reactor ON
How does it behave?
  Spatially confined 
  Time difference: consistent with thermalised n-capture 
SoLid Preliminary
SoLid Preliminary
SoLid Preliminary

## Slide 27: Conclusion
Solid improved design after evaluating performance of full scale prototype module in 2015-2016
Constructed a 1.6 ton detector (Phase1) in 2017 and commissioned it in Nov-Dec 2017
Validated performance with calibration & commissioning data
SoLid is now taking good quality physics data and observes IBD-like events
BR2 will provide us with 6 reactor cycles this year
Physics triggers and DAQ operations are being optimized
Object reconstruction under continuous development and being validated
Backgrounds being measured and IBD selection criteria optimized
First physics results coming real soon!

## Slide 28: SoLid Phase 1
Container 2.4x2.6x3.8 m3
  Cooled to 10C to reduce MPPC dark count rate (1/3)
Shielding
  Water enclosure 50cm thick, 3.4 m high, 28ton
  Polyethylene ceiling 50cm thick, 6ton
  Cadmium lining
Automated calibration system for absolute efficiency and energy scale calibration at % level (207Bi, 60Co, 137Cs, 22Na, AmBe, 252Cf)  Full G4 simulation