## Slide 1: IKPy
An Inverse Kinematics toolbox

## Slide 2: Outline
An inverse kinematics toolbox
IKPy functionnalities
Using IKPy
Live Demo

## Slide 3: Inverse Kinematics

## Slide 4: Inverse Kinematics (IK)
What you have : A robot where you can choose each motor’s angle
What you want to do : move the end effector to this position
How to do it : Find a combination of motor angles

## Slide 5: Desired functionnalities
Compatibility :
  Poppy Humanoid, Torso,
  Baxter
  Human
  Everything else…
Modularity
Plotting tools
Easy to use and setup
Fast enough

## Slide 6: IKPy at a glance

## Slide 7: Optimized computations
Almost based on C structures
Fast Forward-Kinematics
  Symbolic geometrical computations
Possibility to control the computation precision
  Tradeoff between precision and speed
Average computation time : 7 ms – 50 ms
Special optimisations :
  Multicore? (Work in progress)
  Dynamic IK

## Slide 8: Simple API
2 objects :
  Link ~= A motor
  Chain = Ordered list of Links

## Slide 9: Simple API (2)
2 functions :
  Chain.forward_kinematics
  Chain.inverse_kinematics
Additional features :
  Active links
  Smoothness control (very related to precision control)

## Slide 10: URDF Import
URDF : XML describing a Robot (as graph)
  Used by ROS, Poppy
  Compatible with 3D editors
Extract a chain from every URDF topology
Extreme precision : No limitation at the Software level

## Slide 11: 3D Plotting of the robot
Method plot() : Matplotlib 3D view
Standalone use

## Slide 12: Using IKPy

## Slide 13: A lightweight library
Easy to install : Pip or Conda
No compilation required
Compatibility with most systems :
  Python 2/3
Dependencies : Scipy / Numpy, Sympy
Fast enough for Embedded systems

## Slide 14: Developer API
API to customize IKPy behavior :
New representations
  URDF
  DH parameters
New Inverse Kinematics methods
  New constraints : effort, speed
  New solvers

## Slide 15: Last features (1)
Open source
Online documentation

## Slide 16: Last features (2)
Tutorials and notebooks

## Slide 17: Example : Pypot Integration
Fully integrated with Pypot
Chains = attributes of creatures
  Ex of Torso : torso.right_arm / torso.left_arm
IK = goto() method

## Slide 18: Demo

## Slide 19: Live Demo
Poppy torso : right hand must follow left hand.
IKPy features : Demo on ErgoJr.