## Slide 1: Permittivity Measurement of Brain Cancer Cell Solutions: towards the Characterization of Single Cancer Stem Cells
c.palego@bangor.ac.uk
W. Gamal1, R. Pinto2, M. Tanori2, A. Casciati2, M. Mancuso2, L. Persano3, G. Viola3, S. Saada4, F. Lalloue4, B. Bessette4, A. Pothier4, C. Palego1, C. Merla2
1: Bangor University, UK 2: ENEA, Italy
3: University of Padova Italy, 4: University of Limoges, France

## Slide 2: Outline
Need for cancer stem cells (CSCs) dielectric model
Dielectric study of human brain CSCs
Cell electrical parameters assessment
Measurement repeatability
Work in progress

## Slide 3: Need for CSCs dielectric model (1)
CSCs are thought to be crucial in solid tumour initiation, invasion and recurrence.
www.sumcastec.eu focuses on brain CSCs sensing, isolation and neutralization through a novel lab-on-chip technology

## Slide 4: Need for CSCs dielectric model (2)
Very few studies of brain cancer cells dielectric properties.
Growing human cancerous tissues studied applying xenograft model in mice by D. Yoo1
There are no dielectric models of human brain CSCs due to the difficulty in their isolation and culture.
[1] Bioelectromagnetics25:492-497(2004)

## Slide 5: Dielectric study of human brain cancer cells
Complex permittivity measurements performed for human glioblastoma (U87) and medulloblastoma (D283) cell lines.
Cell suspensions with a relatively pure population of CSCs measured in the frequency range of 0.5-3 GHz.
Complex permittivity measured using an open-ended coaxial probe (Keysight Technology 85070E dielectric probe kit) and a Keysight network analyser.
VNA
Coaxial Probe
Connecting Cable
A cell in suspension

## Slide 6: Cell electrical parameter assessment
Computing average of real and imaginary parts (AVGs)
- 3 independent experiments
- Each experiment has 5 repetitions
- Total file averaged for each condition=15
- Comparison of AVG for the different concentrations
Experimental Conditions
Buffer (PBS+H2O+ sucrose)
MEM
DMEM
D283 in MEM (5, 10, 20 mln)
D283 in buffer (5, 10, 20 mln)
U87 in DMEM (5, 10, 20 mln)
U87 in buffer (5, 10, 20 mln)
Evaluation of statistical significant differences for comparable conditions
- Fit AVG(medium), Fit AVG(20 mln), FitAVG(10mln), FitAVG(5mln)  p for each set of assessed parameters
Maximum Likelihood minimization of all fitted parameters (µ and 2)
- Weighted mean value and standard deviation of weighted mean
Merla et al., TMTT 58:3, 2010; Denzi et al., TBME 62:6, 2015
Fitting of AVGs using inverse EMT
15 different fitting for real and imaginary parts
Standard deviation of fitted parameters

## Slide 7: Permittivity measurements of Glioblastoma cell line (U87)

## Slide 8: Measurement Repeatability for Glioblastoma cell line (U87)

## Slide 9: Measurement Repeatability for Medulloblastoma cell line (D283)

## Slide 10: Work In Progress (1)
Experiment repeats.
Curve fitting and extraction of cell parameters (Effective Medium Theory).
Statistical analysis.

## Slide 11: Work In Progress (2)
Characterization by UHF dielectrophoresis in LOC
200ns, 8 pulses, 1kV
Electro-permeabilization in mesoscale planar structures
200µm, 50 Ωm
Manczak Et al., IMBioC, 2018

## Slide 12: Conclusions
Preliminary results of brain CSCs dielectric characterization presented
Established technique, but relatively novel target
Experimental work almost concluded, parameters extraction in progress
Relevant for sensing, isolation and treatment of CSCs

## Slide 13: Thank You

## Slide 14: On-chip neutralization of brain cancer stem cells
Method 3: on-chip EF exposure

## Slide 15: EF Exposure and membrane permeability
35 µm copper Shunt and series CPW structures were fabricated in Bangor on FR-4 and connected to the Creo generator to expose cells to 8 pulses of 200ns, 1kV, 1Hz.
Cells were cultured on cover slips which were put on top of the CPW structure for EF exposure.
Cell lines exposed were:
1- Daoy (medulloblastoma cell line that is isolated from the cerebellum).
2- D283 (Medulloblastoma cells, 95-97% stem cells).
3- U87 (glioblastoma cells).
Yo-pro, a green dye, was used to check the permeability of the membrane after pulse application.
Cells were fixed and mounted on a glass slide using a mounting gel with DAPI (to stain cell nuclei blue).

## Slide 16
Daoy, 200ns, 8 pulses, 1kV

## Slide 17: Daoy, 200ns, 8 pulses, 1kV

## Slide 18: Daoy, 200ns, 8 pulses, 1kV fixed in 4% PFA

## Slide 19: Work in Progress Moving from meso- to micro- scale
BiCMOS
Si Channels
Glass
~735 um
~65 um
300 um