## Slide 1
Workflow Diagrams PileGroup Tool Version 1.0
By
Peter Mackenzie-Helnwein

## Slide 2
Launch Application
The PileGroup Tool will launch with a fully functional initial
Three-layer soil system
A single pile
A reference load
Ready to explore …
Soil Configuration
Pile Configuration
Load control
Results

## Slide 3
Launch Application
The PileGroup Tool will launch with a fully functional initial
Three-layer soil system
A single pile
A reference load
Ready to explore …
Soil Configuration
Pile Configuration
Load control
Results

## Slide 4
Pile Configuration
Select pile by
ID in dialog (1,2, or 3), OR
Clicking on pile in System Plot
Add new Pile
no
yes
Clone last pile ?
Remove this pile
no
yes
Delete selected pile ?
Adjust pile parameters as desired.
(system will re-compute accordingly)

## Slide 5
Soil Configuration
Select soil by
Checking the desired layer, OR
Clicking on soil layer boundary in System Plot
Adjust position of the groundwater table s as desired.
(system will re-compute accordingly)
Adjust soil parameters as desired.
(system will re-compute accordingly)

## Slide 6
Load Control
The horizontal load on the pile or pile group can be varied from -10,000 kN to +10,000 kN.
no
yes
Like numeric control ?
no
yes
Prefer graphic control ?
Mode the slider to increase or decrease the horizontal load.
(the number field will show the current load value in kN)
Adjust numeric value in data entry field.
(the slider will be adjusted accordingly)

## Slide 7
Results
All Plots allow for
Zoom in and out (scroll)
Panning (click hold and drag)
Moment Tab
Shear Tab
Effective stress Tab
P_ult Tab
Y50 Tab
Displacement Tab
yes
See deformed piles?
yes
See moment diagrams ?
no
yes
See shear diagrams ?
yes
See soil vertical stress ?
yes
See soil capacity graph ?
yes
See soil characteristic displcement graph?
no
no
no
no
no