## Slide 1: DESIRE6G EU Project #1: Dynamic Slices #2: Cloud-native, hw-accelerated UP for better efficiency

## Slide 2
DESIRE6G EU Project: Deep Programmability and Secure Distributed Intelligence
Gergely Pongrácz
Attila Mihály
István Gódor

## Slide 3: Dynamic slices as user-network API
Slice: QoS policy + service graph
UE can connect to multiple services slices
  Either via simple API specifying e.g., ID or name …
  … or via an intent-based API
Dynamic service deployment: seconds timescale (see below)
  Services do not have to be deployed at each location
QoS separation between the slices is automatic, based on desired QoE (packet value)
 | Simple chain | Branching | Site-to-site
Generate k8s config | 0.0003 s | 0.0003 s | 0.0003 s
Saving config | 0.0153 s | 0.0270 s | 0.0261 s
Calling helm | 0.9250 s | 1.2556 s | 1.1069 s
Starting PODs | 2.4272 s | 2.2917 s | 2.2253 s
Configuring iNFs | 0.0972 s | 0. 1852 s | 0.1444 s
Total deployment | 3.465 s | 3.7598 s | 3.503 s
Total excl. k8s | 0.1128 s | 0.2125 s | 0.1708 s
Notes: QoE = throughput and latency requirements

## Slide 4: Load Optimizer in the data plane
Main features
  Optimized HW NF-DP load by packet markings (different markings for different flow volumes)
  Dynamic state migration between SW and HW NF-DP via state migration packets & no/minimal packet loss
  Fast up- and down-scaling of software NF instances
  Avoid packet re-ordering within a flow
Results
NF-CP
NF-DP-inst1
NF-DP-inst2
NF-DP-inst3
NF-DP
instances
Load Optimizer Data Plane
NF-CP
Logical NF-DP
P4Runtime
P4Runtime
P4Runtime
P4Runtime
Unified view:
P4Runtime with Optimization Annotations
Common CP-API, e.g,P4Runtime
LO-DP InfraNF on P4 switch
Implementing load balancing and heavy hitter offloading logic
Logical view
Physical view
HeavyHitter
offloading
Load Balancing
NF-DP-HW-inst1
NF-DP-HW-inst1
NF-DP-HW-instK
P4Runtime
NF-DP-SW-instN
IML Proxy
Load Optimizer Control Plane / Part of IML Proxy
Packet delays when a HH flow overloads the SW instance and is offloaded to the HW component
Packet losses when a HH flow overloads the SW instance and is offloaded to the HW component
Notes: Full migration in 45ms
Static migration takes long (green-yellow) Dynamic migration is very short (yellow-red)

## Slide 5: Multi-Tenant UP Deployment in IML
Goal: Running multiple P4 programs on a hardware data plane
    Isolated execution in both data and control planes
P4 program aggregation tool
    Different P4 implementation of NFs can be merged into a single P4 program
    Additional resource sharing elements in the pipeline
P4 Runtime control plane proxy
    Provides each NF control plane an isolated access to the corresponding data plane objects
Evaluation: 2 NFs of different complexity on Netronome SmartNIC (2x40G)
The effect of the complexity of the aggregated NFs on the experienced throughput and latency values