## Slide 1
Network Dynamics in EEG
Arnaud Delorme
(with contribution from Tim Mullen)

## Slide 2: Tim Mullen
Brain connectivity
Tim Mullen

## Slide 3
A toolbox for (source-space) electrophysiological information flow and causality analysis (single- or multi-subject) integrated into EEGLAB
Emphasis on vector autoregression and time-frequency domain approaches
Standard and novel interactive visualization methods for exploratory analysis of connectivity across time, frequency, and spatial location

## Slide 5: The Dynamic Brain
A key goal: To model temporal changes in neural dynamics and information flow that index and predict task-relevant changes in cognitive state and behavior
Open Challenges:
  Non-invasive measures (source inference)
  Robustness and Validity (constraints statistics)
  Scalability (multivariate)
  Temporal Specificity / Non­ stationarity / Single-trial (dynamics)
  Multi-subject Inference
  Usability and Data Visualization (software)

## Slide 6: Large-scale brain connectivity

## Slide 7
Bastos AM, Schoffelen J-M: A Tutorial Review of Functional Connectivity Analysis Methods and Their Interpretational Pitfalls. Front Sys Neurosci 2016, 9:413.

## Slide 8: The problem of spurious connectivity
Bivariate measures such as coherence (but also original GC), find spurious connections between nodes if they share a common input.

## Slide 9: Partial coherence
Coherence

## Slide 10: A deeper problem – unobserved nodes
With EEG, it's unavoidable that there will be contributing network nodes (e.g. thalamus) that we cannot observe.
We also can't be sure ICA will identify all important sources…

## Slide 11: Granger-causality
A measure of statistical causality based on prediction.
Widely used in time-series econometrics.
Nobel Prize in economics, 2003.
If a signal A causes a signal B, then knowledge of the past of both A and B should improve the predictability of B, as compared to knowledge of B alone.

## Slide 12
AR Models (prediction of future of a signal by its past)
X1
X1(t) = −0.5X1(t - 1) + 0.3X1(t - 2) + 0.1X1(t - 3) …

## Slide 13
AR Models (prediction of future of a signal by its past)
X1
X2

## Slide 14
AR Models (prediction of future of a signal by its past)
X1
X2
VAR Models (prediction of future of a signal by its past + the other signal's past)
X1
X2
Incorporating information about X1 improves the prediction of X2! We say "X1 granger causes X2"

## Slide 15
AR Models (prediction of future of a signal by its past)
X1
X2
VAR Models (prediction of future of a signal by its past + the other signal's past)
X1
X2
Incorporating information about X1 improves the prediction of X2! We say "X1 granger causes X2"
X1(t)= −0.5X1(t - 1) + 0.3X2(t - 1) + …
X2(t)= −5X1(t - 1) - 0.1X2(t - 1) + …

## Slide 16: Calculation of GC

## Slide 17: Vector Autoregressive (VAR / MAR / MVAR) Modeling
Granger Causality
Spectrum
Coherence
…

## Slide 18
Granger Causality
Does X4 granger-cause X1? (conditioned on X2, X3)

## Slide 19
1
X (t)= −0.5X (t - 1)
2
1
1
X (t)= 0.7 X (t - 1)
2
0.2 X (t - 1)
2
+ 0 X (t - 1) + E (t)
+ +
1
E (t)
2
Which causal structure does this model correspond to?
1 2
a) 1 2 b)
c) 1 2
X
Granger-causality quiz

## Slide 21: Selecting a VAR Model Order
Model order is typically determined by minimizing information criteria such as Akaike Information Criterion (AIC) for varying model order (p):
AIC(p) = 2log(det(V)) + M2p/N
Penalizes high model orders (parsimony)
entropy rate (amount of prediction error)
optimal order
model order
Error
  Optimal model order depends on sampling rate (higher sampling rate often requires higher model orders)

## Slide 23: Adapting to Non-Stationarity
The brain is a dynamic system and measured brain activity and coupling can change rapidly with time (non-stationarity)
  event-related perturbations (ERSP, ERP, etc)
  structural changes due to learning/feedback
How can we adapt to non-stationarity?
+
mV
time

## Slide 24: Segmentation-based VAR
(Jansen et al., 1981;Florian and Pfurtscheller, 1995; Ding et al,2000)
Analogous to short- time Fourier transform
Sliding window
From
time

## Slide 25: Segmentation-based VAR
(Jansen et al., 1981;Florian and Pfurtscheller, 1995; Ding et al,2000)
Analogous to short- time Fourier transform
Sliding window
From
time

## Slide 26: Important Choices
Model Order
  Determines complexity of spectrum you can model
  Larger orders need more data
Window Length
  Window must be long enough to contain sufficient data for your chosen model order
  Must be long enough to encompass the time-scale of interactions
  Yet not too long as to smear temporal dynamics or include non-stationary data
  If trials are present, can optimize AR model over trials
Notes: Trials added by me

## Slide 27
Too-large, windows may not be locally-stationary
Consideration: Local Stationarity

## Slide 28: How does brain plan visually guided movements?
Pointing Task (Park, et al. 2014, IEEE Trans Neural Syst Rehabil Eng)
vs.
Planning Execution
0
0.5 1.0
Time (s)
N=10 (right-handed, mean age=21) 70 channel EEG (Biosemi) 512 Hz; 128Hz for connectivity
John R. Iversen, Alejandro Ojeda, Tim Mullen, Markus Plank, Joseph Snider, Gert Cauwenberghs, Howard Poizner (2014) EMBC

## Slide 29: ICA source space analysis
ACC
Occ
Par
Mot
sup
ant
Cortical Regions of Interest
Independent Component Analysis
Group SIFT: Project ICs onto cortical surface using LORETA; extract ROI time series. Advantage: Same ROIs for all subjects enables statistical comparison. (Use BCILAB srcpot)

## Slide 30: Changed causal flow during reaching
c
a
a
d b b
FROM
L Mot
R Mot
L Occ
R Occ
ACC
L Par
R Par
TO
L Mot
R Mot
L Occ
R Occ
ACC
L Par
R Par
time [s] 0
50
13
3
0.5 10 0.5 1 0 0.5 1 0 0.5 1 0 0.5 1 0 0.5 1 0 0.5 1
50
13
3
50
13
3
50
13
3
50
13
3
50
13
3
50
13
3
freq [Hz]

## Slide 31
Occipital -> ACC
Planning
Execution

## Slide 32: Result discussion
SIFT is a capable toolkit for causal
dynamical analysis at source level
Parietal network expected for visually guided action (e.g. Heider, et al., 2010)
ACC more strongly driven by Occipital Motor. Locus for
translation of intention into action (Paus, 2001; Srinivasan, et al. 2013). ACC drives SMA (not shown).
Causal network results depend on the number of nodes
  E.g. Occipital " ACC could be mediated by region not included in model
  There will always be a tradeoff between network size and amount of data needed to fit the model.
  Regularization

## Slide 33
or
Scalp or Source?

## Slide 34
+
+
+
+
+
+
sensors
sources
ICA SBL
Beamforming Minimum-norm
...
Scalp or Source?

## Slide 35
A toolbox for (source-space) electrophysiological information flow and causality analysis (single- or multi-subject) integrated into EEGLAB
Emphasis on vector autoregression and time-frequency domain approaches
Standard and novel interactive visualization methods for exploratory analysis of connectivity across time, frequency, and spatial location

## Slide 36: SIFT Workflow

## Slide 39
ROI-based Connectivity analysis

## Slide 40
Align electrodes
with scalp model
Align atlas with
cortex model
EEGLAB ROI connectivity plugin
Distributed source
modeling
Group voxels in regions
and compute connectivity
Measures TRGC, GC, TRPDC,
PDC, TRDTF, DTF and CS
Haufe, S., Nikulin, V. V., Miller, K. R., & Nolte, G. (2013). A critical assessment of connectivity measures for EEG data: a simulation study. Neuroimage, 64, 120-133.

## Slide 41
Volumetric
atlases
Surface
atlases
Desikan Kiliany
Destrieux
PrAGMATiC
AFNI MNI
Schaefer 2018
Connectivity analysis using EEG
Brainnetome

## Slide 42
Cross-coherence amplitude and phase
2 areas, comparison on the same trials
Coherence amplitude 1
Phase coherence 0
Coherence amplitude 1
Phase coherence 90
Coherence amplitude 1
Phase coherence 180
Trial 1
Trial 2
Trial 3
COHERENCE = mean(phase vector)
Norm 0.33
Phase 90 degree
Notes: From 2 components at a definite time and definite frequency, we want to see if they are synchronized or if there is a latency shift or relationship between these two components. Let’s take 3 trials. For instance these 2 trials are synchronized. Here I represented their phase, and their difference is 0.
For two other trials, one being shifted by 90 ms in comparison to the other, their phase difference is 90 degrees. For the 3rd trial, the difference in phase in 180 degrees.
The coherence is the average of these 3 phase vector, so here the coherence phase is 90 degree and the amplitude is 0.33. If the two components always had the same relationship, then the coherence amplitude would be 1 and the phase would determine the latency difference between the components. For instance 90 degrees at 10hz represent a 25 ms advance for one of the components.
The cross-coherence help to determine how 2 processes are related. If one preceed the other, if they express the same frequency or pic at the time, if they are synchrosous. For instance, here the two components…. We can express the difference in term of angle but also in term of millisecond advance. For instance, 90 degree difference at 10 Hz represents 25 ms advance for one of the component.
Only the phase matters, not the amplitude of the waves

## Slide 43: Channel space (~100 dim)
Source space (~10,000)
N channels
M voxels x 3
Pairwise connectivity
TRGC, GC, TRPDC,
PDC, TRDTF, DTF and CS
First ROI
PCA
Dim ~ 2 to 4
Second ROI
PCA
Dim ~ 2 to 4
Compute connectivity between all ROI pairs

## Slide 44
Red regions are highly interacting
Connectivity matrix between 68 ROIs

## Slide 45
Inverse method

## Slide 46
Connectivity method

## Slide 47
Number of interactions
Delay between sources
Number of PCA comp.

## Slide 48
Stationary continuous data
About 100 Hz
2 second data chunks (or epochs)
Same length of data for each condition
No dynamics – static image
Data intake

## Slide 49
Change to the first model

## Slide 50
Note: Data is temporarily resampled at 100 Hz before computing connectivity

## Slide 53
Hands-on
Load .set file using menu item File > Load existing dataset
ds000117_pruned/derivatives/meg_derivatives/sub-01/ses-meg/meg/wh_S01_run_01_preprocessing_data_session_1_out.set
Select BEM model using menu item
Tools > Source localization using DIPFIT > Head model and settings
Compute Leadfield matrix using menu item
Source localization using DIPFIT > Compute Leadfield matrix
Compute ROI activity and connectivity
Tools > ROI connectivity analysis > Compute ROI activity
Tools > ROI connectivity analysis > Compute ROI connectivity
Tools > ROI connectivity analysis > Plot ROI connectivity

## Slide 54
The end