## Slide 1: Clustering of ICA components EEGLAB
Arnaud Delorme
Julie Onton
Romain Grandchamp
Nima Bigdely Shamlo
Scott Makeig
Practical MEEG 2025, Aix-Marseille Université, France, October, 2025

## Slide 2: Steps of clustering
Select ICA components for clustering
Precompute measures of interest
Cluster measures
Plot clusters and edit them if necessary

## Slide 3: Load an existing STUDY
ds002718_processed/Face_detection.study

## Slide 5: Study/Edit study info

## Slide 6: Edit dataset info
Notes: Next, 8 consonant letters (spanning approximately 2- of visual angle) were presented in succession at fixation. Of these, 3, 5 or 7 (colored black) were to be memorized, while the remaining 5, 3 or 1, respectively (colored green) were to be ignored. Letter stimulus duration was 1.2 s, with stimulus onset asynchrony (SOA) fixed at 1.4 s. (In a separate short-stimulus control condition, letter duration was 0.15 s.) In place of a ninth letter, a dash appeared on the screen to signal the beginning of a variable 2 – 4 s memory Maintenance period during which subjects silently rehearsed the identities of the memorized letters. A probe letter (colored red) then appeared, prompting the subject to respond by pressing one of two buttons (with the thumb or index finger of their dominant hand) to indicate whether or not the probe letter had been in the Memorize-letter set in that trial. An auditory feedback signal (a confirmatory beep or cautionary buzz), presented 400 ms after the button press, informed the subject whether his/her answer was correct or incorrect. After a self-selected, variable delay, the subject initiated the next trial by pressing either response button, triggering the reappearance of the fixation cross
(https://www.creact.co.jp/wp-content/uploads/2020/03/Frontal-midline-EEG-dynamics-during-working-memory.pdf#page=16&zoom=100,0,0)

## Slide 7
Actual IC map ()
Dipole projection ()
Computing residual variance (%)

## Slide 8
Notes: RELICA first computes IC “dipolarity” a measure of physiological plausibility, plus a measure of IC consistency across multiple decompositions of bootstrap versions of the input data. RELICA then uses these two measures to visualize and cluster the separated ICs, providing a within-subject measure of IC reliability that does not involve checking for its occurrence across subjects.
Authors demonstrated the use of RELICA on EEG data recorded from 14 subjects performing a working memory experiment and show that many brain and ocular artifact ICs are correctly classified as “stable” (highly repeatable across decompositions of bootstrapped versions of the input data). Many stable ICs appear to originate in the brain, while other stable ICs account for identifiable non-brain processes such as line noise. RELICA might be used with any linear blind source separation algorithm to reduce the risk of basing conclusions on unstable or physiologically uninterpretable component processes.

## Slide 11: ICs to cluster

## Slide 12: Precompute data measures

## Slide 13: Pre-compute measures

## Slide 14: Precompute data measures
TIP: Compute all measures so you can
test different combinations for clustering
Time-frequency options

## Slide 15: Cluster components

## Slide 16: Precluster schematic
ICs (all subj)
ERSP
(time/freq)
PCA
Mean ERSPs
PC
templates
# PCs
ICs (all subj)

## Slide 17: Precluster schematic
ICs (all subj)
ERSP
(time/freq)
PCA
Mean ERSPs
ICs (all subj)
Power
spectrum
*
PCA
Mean spectra
3D dipole position
PC
templates
# PCs
ICs (all subj)
PC
templates
# PCs
ICs (all subj)
x3
ICs (all subj)
*
ICs (all subj)
3D dipole moments
x3
ICs (all subj)
ICs (all subj)

## Slide 18: Precluster schematic
ICs (all subj)
ERSP
(time/freq)
PC weights
PCA
Mean ERSPs
ICs (all subj)
Power
spectrum
PC weights
*
PCA
Mean spectra
3D dipole position
PC
templates
# PCs
ICs (all subj)
PC
templates
# PCs
ICs (all subj)
x3
ICs (all subj)
PC weights
*
ICs (all subj)
3D dipole moments
x3
ICs (all subj)
PC weights
ICs (all subj)
ERSP
Spectrum
Dip. positions
Ics/PCs (all subj)
Dip. moments

## Slide 19: Precluster: Use singular values from PCA
10% of max singular value
~ relative variance of
principal components
ICs (all subj)
ERSP
(time/freq)
PC
templates
PCA
Mean ERSPs
ERSP
(time/freq)
# PCs

## Slide 20: Precluster schematic
ERSP
Spectrum
Dipoles
ICs (all subj)
Each component is a dot
Clustering will group these
dots

## Slide 21
1. k initial "means" (in this case k=3, (shown in color)) are randomly selected from the data set (shown in grey).
Standard Kmean Clustering
2. k clusters are created by associating every observation with the nearest mean.
3. The centroid of each of the k clusters becomes the new means
4. Steps 2 and 3 are repeated until convergence has been reached.

## Slide 22: Cluster components

## Slide 23
What measure(s) should you use?
It depends on your final cluster criteria…
- If for example, your priority is dipole location,
then cluster only based on dipole location…
But consider:
- What is the difference between these two components?
Choosing data measures

## Slide 24: Choosing data measures
Similar dipole location,
very different orientation.
Obvious dramatic effect on
scalp map topography:
But, do they
perform the
same functions?

## Slide 25: Results (Cluster 1 within subject)
100 % Sessions contribute

## Slide 26: Results (Cluster 2 within subject)
100 % Sessions contribute

## Slide 27: Results (Cluster 8 within subject)
100 % Sessions contribute

## Slide 28: Results (Cluster 13 within subject)
63.64% Sessions contribute

## Slide 29: Results (Cluster 14 within subject)
36.36% Sessions contribute

## Slide 30
Data
13 subjects performing a memory task
71 electrodes including EOGs
more than 300,000 data points/subject
Decomposition
23 ICA algorithms plus PCA and Promax
Analysis
Localization of all components with a single dipole
(4-shell spherical model)
Validation of the ICA algorithm for EEG

## Slide 31
Number of components with residual variance lower than a specific threshold
Notes: Data
13 subjects performing a memory task
71 electrodes including EOGs
more than 300,000 data points/subject
Decomposition
23 ICA algorithms plus PCA and Promax
Analysis
Localization of all components with a single dipole
(4-shell spherical model)

## Slide 32
More independence -> more biological components
Delorme, A., Palmer, J., Onton, J., Oostenveld, R., & Makeig, S. (2012). Independent EEG sources are dipolar. PLOS ONE, 7(2), e30135. https://doi.org/10.1371/journal.pone.0030135

## Slide 35
Left m cluster (across subjects)

## Slide 36
Right m cluster

## Slide 37
Occipital a cluster

## Slide 38
Frontal Midline q cluster
Delorme, A., Palmer, J., Onton, J., Oostenveld, R., & Makeig, S. (2012). Independent EEG sources are dipolar. PLOS ONE, 7(2), e30135. https://doi.org/10.1371/journal.pone.0030135

## Slide 40: ICA reliability across subjects
Different ICA algorithms return similar solutions
The ICA algorithms that return the most biologically plausible solutions are also the one that return the most independent decompositions

## Slide 41: View and edit clusters

## Slide 42: Plot/edit clusters

## Slide 43: Plot cluster data
Plot mean scalp
maps for easy
reference

## Slide 44: Plot cluster data
Choose
which
cluster
Choose which
components

## Slide 45: Plot cluster data

## Slide 46: Plot cluster data

## Slide 47: Plot cluster data
Familiar
Unfamiliar
Scrambled

## Slide 48
Familiar
Unfamiliar
Scrambled

## Slide 49: IC contributions to ERP envelope

## Slide 50: IC contributions to ERP envelope

## Slide 51: Hands on
Load the STUDY ds002718/Face_detection.study
(download ds002718 from NEMAR and run the script Session_5_ds002718_preproc.m if needed)
Precompute spectrum for components, scalp topo.
Precluster and cluster components using dipole locations and dipole moments (KMean)
Look at your clusters. Identify frontal midline theta cluster(s) and occipital alpha cluster(s)
Look for a cluster generating a N170 and check dipoles location
Remove outliers if any