## Slide 1: Sustainability assessment of packaging
Dimitris Ladakis, Anna Sadzik, Elisa Uhlig, Mara Strenger
Sustainable Packaging Institute of Albstadt-Sigmaringen University
online 27/02/2026
Demonstrative process for the production and enzymatic recycling of environmentally safe, superior and versatile PHA-based rigid packaging solutions by plasma integration in the value chain. H2020-BBI-JTI-2020
GA 101023685
Notes: I am pleased that you are interested in our workshop as part of the EU BioSupPack project (titel vorlesen).
Our task, among others, is the sustainability assessment and in the workshop today we will deal with „The next…“.

## Slide 2: Agenda
Introduction to BioSupPack and the institutes working on the sustainability assessment
Basics of sustainability assessments
Life Cycle Assessment (LCA)
Life Cycle Costing (LCC)
Social Life Cycle Assessment (sLCA)
Outlook
Questions

## Slide 3: Ongoing research project - BioSupPack
Goals:
Use of the bio-based raw material brewer's grains with up to >85 %, incl. upscaling of production
Integrating plasma technology throughout the value chain
Establishing a system for identifying and sorting the developed packaging solutions
Assess compliance with EU standards and sustainability aspects
Ensure recyclability
Investigating consumer perceptions
Establish new value chains
www.biosuppack.eu

## Slide 4: Ongoing research project - BioSupPack
Assessment of conformity and sustainability
www.plastikverarbeiter.de
www.biertreber.de
[1]
[2]
This project has received funding from the Bio Based Industries Joint Undertaking under the European Union’s Horizon 2020 research and innovation programme under grant agreement No. 101023685
Recycled PHA materials
Brewer's grains
PHA-selective enzymes
PHA
www.biosuppack.eu
[2]
[1]
PHA-based materials
Packaging
Waste management
Enzymatic recycling

## Slide 5
Notes: Update logos

## Slide 6
The Sustainable Packaging Institute (SPI) teaches & researches in six thematic areas
The institute has a research focus on „sustainable packaging concepts"
Forschungsfabrik
Startup - Zentrum
Akademie
www.innocamp-sigmaringen.de
Albstadt-Sigmaringen University‘s Sustainable Packaging institute

## Slide 7: Albstadt-Sigmaringen University‘s Sustainable Packaging institute
Notes: Unsere Arbeit wird abgerundet durch das 6. Themenfeld, die „Bioökonomie & Nachhaltigkeit“, was […]

## Slide 8: Agricultural University of Athens
Research interests
  Agricultural University of Athens
  Department of Food Science and Human Nutrition
  Group of Food Bioprocesses Engineering & Circular Bioeconomy
  https://becb.aua.gr/

## Slide 9
Shaping a more sustainable future together
Notes: We strive for a more sustainable future together. However, there are many challenges associated with this aim. And we believe that one step towards meeting these challenges is to have the necessary knowledge about alternative packaging materials. To assess the sustainability of packaging materials, we use sustainability assessments such as LCA.

## Slide 10: Sustainabilty assessment Basics

## Slide 11: Why are sustainability assessments important?
Sustainability dimensions:
Environmental sustainability,
Economic sustainability, and
Social sustainability
Generally:
Sustainability assessments can be done for existing and future packaging concepts, including all associated materials and processes across the entire life cycle.
This can include raw material extraction, production, distribution, use, and end-of-life treatment (reuse, recycling, recovery, disposal).
eLCA
sLCA
LCC
LCSA
Notes: Kloepffer (2008)

## Slide 12: Why are sustainbility assessments important?
Sustainability Assessments can help:
to identify opportunities for improving the environmental, economic or social performance of products at the various stages of their life cycle,
to provide information to decision-makers in industry, governmental or non-governmental organizations (e.g. for strategic planning, priority setting, product or process development, or corresponding new developments),
to support the selection of relevant indicators for environmental performance, including the associated measurement methods, and
to support marketing activities (e.g. the implementation of environmental labeling, the substantiation of environmental claims, or the preparation of an environmental product declaration).
Notes: ISO 14040

## Slide 13: Life Cycle assessment LCA

## Slide 14: How are sustainability assements done in general?
Data collection:
- Data collection
- Data categorization
- Allocation
2
Life Cycle Inventory
1
Goal and Scope
Definition:
- Goal
- Functional Unit
- System boundary(s)
- Data requirements
3
Impact assessment
Environmental impacts:
- Definition Impact
category
- Impact assessment
- Impact classification
- Impact characterization
4
Interpretation
Evaluation:
- Parameter evaluation
- Conclusions
- Sensitivity test
- Recommendations for
action
4 Phases of LCA according to DIN EN ISO 14040
Impact categories represent important environmental aspects and are assigned to the Life Cycle Inventory results (e.g. climate change, water use) (DIN EN ISO 14040:2021)
Crucial for the significance
Notes: The LCA consists of 4 phases and begins with the goal and scope. This is where the goal, … are defined. The first phase is crucial for the significance of the LCA.
Next is the life cycle inventory, which includes the collection of all relevant inputs and outputs.
In the impact assessment, the impact categories are defined. Impact categories represent important environmental aspects and are assigned to the Life Cycle Inventory results. An example of an impact category is climate change.
Finally, an interpretation is made. This phase includes a critical conclusion and the derivation of recommendations for action.
The LCA is an iterative method. The results of the other phases are used in the individual phases of a LCA.
INFO:
Allocation of life cycle inventory results to the selected impact categories (classification)
Calculation of the impact indicator values (characterization)
DIN ISO 14040, Environmental management - Life cycle assessment - Principles and framework (ISO 14040:2021-02)

## Slide 15: Goal and Scope
Goal Definition
The goal of the life cycle assessment is defined by specifying the intended application, the reasons for carrying out the study, and the target audience.
Functional Unit
The functional unit represents the quantified performance of a product system and serves as the reference unit for all input and output flows as well as for the assessment of environmental impacts. Only product systems that are functionally equivalent may be compared on the basis of the functional unit.
Examples:
Comparison of ketchup packaging systems → packaging containing 500 ml of ketchup

## Slide 16: Goal and Scope: Functional unit
LCA allows to compare the environmental sustainability of polymers / packaging
Material functionality must be included, as products often have higher resource consumption and consequently higher potential environmental impact than their packaging
Minimal
environmental impact
Packaging weight
Optimized packaging concept
Unfavorable
environmental impact
Oversized
Undersized
Minimum use of material
Figure: Optimized packaging concept (according to ISO 18602:2013)
Notes: LCA allows to compare the environmental sustainability of different polymers and/or packagings.
Functionality (product protection) must be included in order to obtain meaningful LCA results, as products often have a higher resource consumption and thus a greater potential environmental impact than packaging, so product wastage must be taken into account. The larger environmental impacts due to product loss are shown in the figure. Slight oversizing of packaging, on the other hand, has less of a negative impact.
DIN ISO 18602, Packaging and the environment - Optimization of the packaging system (ISO 18602:2013)

## Slide 17: Goal and Scope: Functional Unit
Requirements to packaging materials for sensitive food, pharmaceutical, and technical products are important
Protection as the primary function of packaging
0,01
0,1
1
10
100
1000
0,01
0,1
1
10
100
Water vapour permeability [g / m² d] 85% 0% RH
Oxygen permeability [cm³ (STP)/ m² d bar]
meat/MAP
ketchup,
sauces
nuts,
snacks
Edible oil
UHT milk
Vacuum coffee
beer
Special food,
infusions, baby food
Instant coffee
vacuum isolation panels, flexible displays
tablets
(blister)

## Slide 18: Goal and Scope: System boundries
Gate to Gate
Cradle to Gate
Raw material
Processing
Production
Gate to Grave
Use Phase
End-of-life
Recycling
.....
Cradle to Cradle
Cradle to Grave
Notes: Was schauen wir uns an was lassen wir raus
Systemgrenzen
2. Geografischer Bezug
  z.B. (lokale) Energiezusammensetzung, Abfallentsorgung, Ressourcenbezug
3. Zeitlicher Bezug (Untersuchungszeitraum)
  z.B. Bezugsjahr, definierter Bezugstag, Prozesszeitraum
4. Komplexität der Daten
  angemessene Wahl der zu betrachtenden & relevanten Prozess- und oder Produktdaten (Inputs, Outputs, Rest- und Nebenstoffe, etc.)
  in Anpassung an vorliegende Datenverfügbarkeit und - struktur

## Slide 19: Life Cycle Inventory: Template
Template for collecting data with inputs and outputs
Flow chart of the inputs and outputs

## Slide 20: Impact assessment: Categories on the example of the recipe method
Life cycle inventory results
Elementary flows like:
Midpoint Impact Categories
Global Warming Potential (GWP): Measures greenhouse gas emissions (kg CO2-eqk)
Damage Pathways
GHG emission increases GHG concentration: increases global mean temperature
〖"CH" 〗_4
〖"NO" 〗_𝑥
〖"SO" 〗_2
〖"NH" 〗_3
Endpoint area of protection
Ozone Formation, Human Health (HOFP): Ground-level ozone formation affecting health (𝑘𝑔 𝑁𝑂𝑥-eq)
Terrestrial Acidification (TAP): Acid deposition on land (𝑘𝑔 𝑆𝑂2-eq)
Freshwater Eutrophication (FEP): Nutrient pollution in freshwater (𝑘𝑔 𝑃-eq)
Human Toxicity: Potential health risk (𝑘𝑔 1,4−𝐷𝐶𝐵-eq)
Fossil Resource Scarcity (FFP): Depletion of fossil fuels (𝑘𝑔 𝑜𝑖𝑙-eq)
Water Consumption (WCP): Depletion of freshwater (m3)
Stratospheric Ozone Depletion Potential (ODP): Measures damage to the ozone layer (kg CFC−11-eqk)
Human Health: Measured in Disability-Adjusted Life Years (DALY).
Ecosystem Quality: Measured in species·year.
Resources: Measured in MJ surplus energy.
Change in disease distribution and flooding -> damage to human health
Change in biome distribution -> Disappeared terrestrial species
Change in river discharge -> disappeared freswater fish
…
…
…
Life cycle inventory results
Midpoint Impact Categories
Global Warming Potential (GWP): Measures greenhouse gas emissions (kg CO2-eqk)
Damage Pathways
GHG emission increases GHG concentration: increases global mean temperature
Endpoint area of protection
Ozone Formation, Human Health (HOFP): Ground-level ozone formation affecting health (𝑘𝑔 𝑁𝑂𝑥-eq)
Terrestrial Acidification (TAP): Acid deposition on land (𝑘𝑔 𝑆𝑂2-eq)
Freshwater Eutrophication (FEP): Nutrient pollution in freshwater (𝑘𝑔 𝑃-eq)
Human Toxicity: Potential health risk (𝑘𝑔 1,4−𝐷𝐶𝐵-eq)
Fossil Resource Scarcity (FFP): Depletion of fossil fuels (𝑘𝑔 𝑜𝑖𝑙-eq)
Water Consumption (WCP): Depletion of freshwater (m3)
Stratospheric Ozone Depletion Potential (ODP): Measures damage to the ozone layer (kg CFC−11-eqk)
Human Health: Measured in Disability-Adjusted Life Years (DALY).
Ecosystem Quality: Measured in species·year.
Resources: Measured in MJ surplus energy.
Change in disease distribution and flooding -> damage to human health
Change in biome distribution -> Disappeared terrestrial species
Change in river discharge -> disappeared freswater fish
…
…
Notes: https://www.researchgate.net/figure/Overview-of-damage-pathways-related-to-some-of-the-impact-categories-in-the-ReCipe2016_fig2_367001712
Recipe method

## Slide 21: Impact assessment: Downstream purification solvent
Chart: Total potential environmental impact [µPt]
| 1,3-dioxolane (wet biomass) | 1,3-dioxolane (dry biomass) | chloroform (dry biomass) | ammonium laurate (wet biomass)
Global warming | 0.00015668 | 0.00016313 | 0.00034922 | 9.5409e-05
Fine particulate matter formation | 3.6352e-05 | 3.639e-05 | 3.5877e-05 | 2.3014e-05
Terrestrial acidification | 0.00011673 | 0.00011982 | 0.00020694 | 7.1575e-05
Marine eutrophication | 1.7385e-05 | 1.7255e-05 | 1.2576e-05 | 1.1119e-05
Water consumption | -1.927e-05 | -1.6895e-05 | 6.9983e-05 | -1.8158e-05
Fossil resource scarcity | 0.00054291 | 0.00056581 | 0.0012262 | 0.00033056
Human toxicity | 0.0011793 | 0.0011922 | 0.0015264 | 0.00073889

## Slide 22: Impact assessment: Downstream purification solvent
Chart: Total potential environmental impact [µPt]
| 1,3-dioxolane (wet biomass) | 1,3-dioxolane (dry biomass) | chloroform (dry biomass) | ammonium laurate (wet biomass)
Global warming | 0.00015668 | 0.00016313 | 0.00034922 | 9.5409e-05
Fine particulate matter formation | 3.6352e-05 | 3.639e-05 | 3.5877e-05 | 2.3014e-05
Terrestrial acidification | 0.00011673 | 0.00011982 | 0.00020694 | 7.1575e-05
Marine eutrophication | 1.7385e-05 | 1.7255e-05 | 1.2576e-05 | 1.1119e-05
Water consumption | -1.927e-05 | -1.6895e-05 | 6.9983e-05 | -1.8158e-05
Fossil resource scarcity | 0.00054291 | 0.00056581 | 0.0012262 | 0.00033056
Human toxicity | 0.0011793 | 0.0011922 | 0.0015264 | 0.00073889
Notes: Farben anpassen – Obere farben passen aber die unter lila unterscheiden sich nicht gut genug

## Slide 23: Interpretation
In general:
The interpretation phase evaluates LCA results and assesses data quality
Environmental hot spots of solvents, processes, and packaging are identified
Focus on impact reduction potential and decision support
For the solvent example:
Green solvents/SAS (1,3-dioxolane, ammonium laurate) are environmentally preferable to chloroform
But: Both environmental and technical aspects must be considered
Ammonium laurate: environmentally more favourable
1,3-dioxolane: technically more favourable due to:
  Higher solubility and process performance
  Lower viscosity → easier handling
Notes: Key Impact Categories
All solvents/SAS show highest impacts in:
  Human toxicity
  Fossil resource scarcity
  Global warming potential
These categories offer the highest potential for impact reduction
Identification of hot spots supports targeted improvement strategies

## Slide 24: Life Cycle COsting assessment LCC
Dimitrios Ladakis
Agricultural University of Athens

## Slide 25: Methodological Framework for Life Cycle Costing (LCC)
Development of the Process Flow Diagram
(process design-Unisim, material and energy balance)
Sizing of all process equipment using standard chemical engineering techniques and widely acceptable rules of thumb
Estimation of purchased equipment cost (Cp) using relevant textbooks and reports
Conversion to todays prices by using the CEPCI (CHEMICAL ENGINEERING PLANT COST INDEX)
Economic evaluation by estimation of Fixed Capital Investment (FCI = 5×CP), Cost of manufacturing COM , Minimum selling price (MSP)
Estimation of externalities as environmental prices on the specific environmental indicator

## Slide 26: Process Design

## Slide 27: Process Design
PHB downstream
Green solvent
Pretreatment
Fermentation
Chloroform solvent
Ammonium laurate

## Slide 28: Aspen plus

## Slide 29: Equipment Sizing
Determination of the Characteristic Equipment Size per Plant Production Capacity
Definition of plant production capacity (e.g., ton/year, kg/h) and conversion to mass and volumetric flow rates under steady-state operation.
Identification of the governing design parameter for each unit (e.g., reactor volume, heat transfer area, pump flow rate, column diameter).
Application of fundamental design equations (residence time, heat transfer, mass transfer, hydraulic relations) to calculate the base equipment size.
Adjustment for scale-up constraints, including mixing efficiency, heat removal limitations, mass transfer performance, and safety margins.
Linking characteristic size to cost estimation, using scaling laws (e.g., six-tenths rule) for CAPEX and utility demand estimation in TEA.

## Slide 30: Purchased Equipment Cost
Equipment Type | Capacity Variable (Q) | Valid Range | Base Year (USD) | K₁ | K₂ | K₃ | Primary Reference
Stirred Tank Bioreactor / Reactor (CS) | Vessel Volume (m³) | 1 – 500 m³ | 2001 |  |  |  | Turton et al., 2018
Storage Tank (Carbon Steel, vertical) | Vessel Volume (m³) | 10 – 10,000 m³ | 2001 |  |  |  | Peters & Timmerhaus, 2003
Rotary Dryer | Heat Duty (kW) | 100 – 20,000 kW | 2001 |  |  |  | Towler & Sinnott, 2013
Spray Dryer | Evaporation Rate (kg/h) | 50 – 10,000 kg/h | 2001 |  |  |  | Towler & Sinnott, 2013
Agitated Vessel / Mixer | Vessel Volume (m³) | 0.5 – 200 m³ | 2001 |  |  |  | Turton et al., 2018
Shell & Tube Heat Exchanger (CS) | Heat Transfer Area (m²) | 10 – 1000 m² | 2001 |  |  |  | Towler & Sinnott, 2013
Centrifugal Pump | Flow Rate (m³/h) | 1 – 500 m³/h | 2001 |  |  |  | Turton et al., 2018
Distillation Column (tower shell only) | Column Diameter (m) | 0.5 – 4 m | 2001 |  |  |  | Peters & Timmerhaus, 2003
log10 (Cp )=K1 +K2 log10 (Q)+K3 [log10 (Q)]2
The general log-polynomial correlation is applied:
CEPCI Adjustment
Where CEPCI reflects:
Equipment index
Labor index
Structural steel index
Engineering services index
Source: Chemical Engineering Magazine (annual CEPCI report)

## Slide 31: Cost of Manufacturing (COM)
Fixed Capital Investment (FCI)
Lang Factor Method where: ≈ 3–5 depending on plant complexity.
Cost of Manufacturing (COM)
The Cost of Manufacturing is calculated (classical chemical engineering approach):
Where:
FCI = Fixed Capital Investment
COL = Cost of Labor
CUT = Cost of Utilities
CWT = Cost of Waste Treatment
CRM = Cost of Raw Materials

## Slide 32: Minimum Selling Price (MSP)
Minimum Selling Price (MSP)
MSP is defined such that:
Solving for product price yields:

## Slide 33: Total Life Cycle Cost LCC
Environmental Impacts→Monetized Environmental Externalities and integrate them with techno-economic outputs to determine the total life cycle cost.
The central equation of the integrated framework is:
or alternatively:
Where:
= Cost of Manufacturing (€/functional unit)
= Minimum Selling Price (€/functional unit)
= Environmental Externality Cost (€/functional unit)
Impact Category | Unit | Monetary Value
Climate Change | kg CO2-eq | 0.0566
Stratospheric Ozone Depletion | €/kg CFC-11 eq. | 30
Human Toxicity | €/kg DCB-eq | 0.0991
Photochemical oxidant formation | €/kg NMVOC-eq | 1.15
Fine Particulate Matter Formation | €/kg PM2.5 eq. or kg PM10 eq. | 39.2
Ionizing Radiation | €/Bq C-60 eq. to air or kBq U232 eq. | 0.0461
Acidification | €/kg SO2-eq | 4.970
Freshwater eutrophication | €/kg P-eq | 1.86
Marine eutrophication | €/kg N-eq | 3.11
Terrestrial ecotoxicity | €/kg 1,4-DB eq. | 8.69
Freshwater ecotoxicity | €/kg 1,4-DB eq. | 0.0361
Marine ecotoxicity | €/kg 1,4-DB eq. | 0.0074
Land use | €/Annual crop eq.·y or m2·y | 0.0845
Environmental Prices

## Slide 34: Sustainability assessments
Chart: Capacities (kt)
| 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100
Total COM | 4.6431 | 2.9948 | 2.289 | 1.8548 | 1.602 | 1.5479 | 1.5109 | 1.4905 | 1.4856 | 1.4616
Fermentation stage | 0.80134 | 0.64363 | 0.55475 | 0.52 | 0.5 | 0.48 | 0.46653 | 0.45398 | 0.45 | 0.4522
Enzyme & Hydrolysate production | 2.061 | 1.3554 | 1.0632 | 0.86506 | 0.78075 | 0.75992 | 0.73873 | 0.73224 | 0.72496 | 0.71897
Downstream 1,3-dioxolane | 1.7807 | 0.99578 | 0.67109 | 0.46972 | 0.32125 | 0.30795 | 0.30562 | 0.30429 | 0.31066 | 0.29038
Cost of manufacturing-Downstream
Total Cost of manufacturing
Chart: Capacities (kt)
| 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100
1,3-Dioxolane | 1.6382 | 0.91611 | 0.61741 | 0.43214 | 0.3312 | 0.2944 | 0.28117 | 0.27995 | 0.27995 | 0.27995
Ammonium laurate | 1.3761 | 0.76954 | 0.51862 | 0.363 | 0.27821 | 0.2473 | 0.23618 | 0.23516 | 0.23516 | 0.23516
Chloroform | 2.9488 | 1.649 | 1.1113 | 0.77785 | 0.59616 | 0.52992 | 0.50611 | 0.5039 | 0.5039 | 0.5039
LCC=Cost of Manufacture (COM) + Cost of Externalities

## Slide 35: Sustainability assessments
Chart: Capacities (kt)
| 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100
Total FCI | 10.0397 | 7.0671 | 5.5104 | 4.0591 | 3.3862 | 3.1008 | 2.9967 | 2.9481 | 2.9248 | 2.8681
Fermentation stage | 3.2868 | 2.3329 | 1.8214 | 1.2799 | 0.99721 | 0.94705 | 0.9089 | 0.87882 | 0.87995 | 0.85532
Enzyme & Hydrolysate production | 4.8953 | 3.4041 | 2.7061 | 2.1989 | 1.9422 | 1.7182 | 1.6714 | 1.6552 | 1.6317 | 1.612
Downstream 1,3-dioxolane | 1.8576 | 1.33 | 0.9829 | 0.58036 | 0.44682 | 0.43556 | 0.41635 | 0.41409 | 0.41314 | 0.40077
Chart: Capacities (kt)
| 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100
1,3-Dioxolane | 8.1425 | 5.2172 | 3.8601 | 3.033 | 2.5929 | 2.5389 | 2.5189 | 2.5009 | 2.5009 | 2.5009
Chart: Years
 | -19181159.9244 | -149961795.7729 | -223278212.8395 | -142503737.0548 | -63226078.5029 | 5197085.3762 | 65031497.4712 | 117893375.3021 | 165945713.0589 | 209633215.3985 | 247902909.1736 | 281381738.0083 | 311817036.9489 | 339485490.5313 | 364638630.1516 | 387505120.7156 | 408292839.4101 | 427190765.496 | 444370698.3014 | 459988819.0336 | 474187110.6082 | 487094648.4034 | 498828773.6718 | 509496160.2793 | 519193784.468 | 528009806.4578 | 536024371.903 | 543310340.4896 | 549933948.2955 | 555955409.9373 | 561429465.9753 | 566405880.5553 | 571497685.4038
Chart: Capacity (kt/y)
| 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100
PHB selling price $3.5/kg | -175.57 | -106.03 | -36.49 | 33.05 | 102.59 | 172.13 | 241.67 | 311.21 | 380.75 | 450.29
PHB selling price $3/kg | -196.918 | -138.346 | -79.774 | -21.202 | 37.37 | 95.942 | 154.514 | 213.086 | 271.658 | 330.23

## Slide 36: Social life cycle assessment slca

## Slide 37: Social LCA
Assesses social & socio-economic impacts of products/services
Complements traditional environmental and economic LCA
Focus: human well-being, labour conditions, social responsibility
Collect detailed data on social aspects throughout all life cycle stages
Purpose: Supports informed, socially responsible decisions

## Slide 38: How are social LCAs done?
Data collection:
- Data collection
- Data categorization
- Allocation
2
Social Life Cycle Inventory
1
Goal and Scope
Definition:
- Goal
- Functional Unit
- System boundary(s)
- Data requirements
3
Social Impact assessment
Social impacts:
- Definition Social Impact
category
- Social Impact assessment
- Social Impact classification
- Social Impact
characterization
4
Interpretation
Evaluation:
- Parameter evaluation
- Conclusions
- Completeness, Sensitivity,
Consistency check
- Recommendations for
action
4 Phases of S-LCA according to DIN EN ISO 14075
Impact categories represent important social aspects (= element of an organization’s activities or products that interacts or can interact with human well-being of any interested party which can cause a social impact)
Crucial for the significance

## Slide 39: Goal and Scope
Define purpose & target audience of the study
Select social aspects (e.g. human rights)
Determine system boundaries (cradle-to-gate, cradle-to-grave, etc.)
Data sources: Company reports, supplier audits, NGO databases, surveys, SHDB
Importance: Provides the foundation for impact assessment → identifies hotspots and areas for improvement
Additional note: Data can be quantitative or qualitative, depending on availability
Gate to Gate
Cradle to Gate
Raw material
Processing
Production
Gate to Grave
Use Phase
End-of-life
Cradle to Cradle
Cradle to Grave

## Slide 40: Social Impact assessment: Impact categories
Stakeholder | Impact categories | Subcategories |  | Indicator examples
Local community | Labor rights/Decent work | Forced labor Excessive working time Poverty Freedom of association Wage assessment | Migrant labor Unemployment Child labor Labor laws Discrimination Social benefits | Risk of Child Labour in sector (qualitative) Risk of forced labour by sector Characterization of International Labour Organization’s Forced Labour regional Estimates
Workers, Consumers | Human rights | Indigenous rights Human health issues | Gender equallty High confilicts | Characterization of Indigenous population
Society | Health and safety | Injuries and Fatalities | Toxics and Hazards | Risk of fatal injuries, by sector
Value chain actors | Governance | Legal System | Corruption | Overall Risk of Corruption
- | Community | Hospital beds Drinking water Children out of school | Sanitation Smallholder vs Commercial farms | Risk that there are too few hospital beds to support population
Notes: UNEP/SETAC GUIDELINES FOR SOCIAL LIFE CYCLE ASSESSMENT OF PRODUCTS

## Slide 41: Social Impact Assessment with social hotspot data base
x
Data sources like NGO data
=
Raw values (per 10.000 employers)
Characterisation factors (e.g.
low risk = 0.1
medium risk = 1; very high risk = 10)
Impact assessment results in medium risk hours
Stakeholder groups e.g. worker
Impact categories and sub categories e.g. health and safety
Indicators e.g. fatal accidents at workplace
Paid annual leave:
Low: 4 weeks and more
Medium: between 2 and 4 weeks
High: between 1 and 2 weeks
Very High: None
Notes: https://www.researchgate.net/figure/SOCIAL-DATABASE-AND-MODELLING-FRAMEWORK-27_fig2_364942191

## Slide 42: Interpretation
Characterisation level
Social life cycle inventory of a polymer
Weighing level

## Slide 43: Outlook
Challenges & Opportunities
Managing integration complexity
Driving circular economy and supply chain decisions
Data & Quality
Standardized, high-resolution datasets
Improved reliability and comparability
Policy & Industry Implications
Life cycle thinking embedded in regulations
Proactive sustainability strategies
eLCA
sLCA
LCC
LCSA
Combine LCA, LCC, and sLCA for a holistic sustainability assessment
Notes: Hier auf die Industrie beziehen

## Slide 44: Any Questions?

## Slide 45: References
DIN ISO 14040, Environmental management - Life cycle assessment - Principles and framework (ISO 14040:2021-02)
DIN ISO 18602, Packaging and the environment - Optimization of the packaging system (ISO 18602:2013)
DIN ISO 14075, Environmental management — Principles and framework for social life cycle assessment (ISO 14075:2024)