## Slide 1
Recovery of alcohols in Aqueous Streams from Stabilized Pyrolysis Oil and Stabilized Deoxygenated Pyrolysis Oil Process
Contact: matteo.gilardi@sintef.no, SINTEF Industry
Authors: Matteo Gilardi, Trung Trinh, Bernd Wittgens
fuelup-project.eu
@FuelUp_Project
FUEL-UP Project
Introduction
  Results and discussion
  Process design and optimization
Conclusions
References
The main overall process targets are:
  99.9% recovery of methanol and 99.99 vol% methanol-rich stream purity;
  95% recovery of ethanol, at azeotropic composition (96 wt%).
Column | Specifications
Col1 | - 99.5% recovery of ethanol (and close to 100% of methanol) on the top - 99.5% recovery of H2O in the bottom.
Col2 | - 99.99 vol% methanol purity in distillate - Residual methanol in the bottom 0.04 vol% (lowest methanol loss achievable)
Col3 | - 95 vol% ethanol recovery in distillate. - 99.5 vol% recovery of 1-propanol in the bottom
Col4 | - 30 wt% Acetic Acid purity in the bottom - Reflux ratio=5
Column | Total number of theoretical stages | Optimal feed tray (from the top)
Col1 | 30 | 12 (SDPO), 18 (SPO)
Col2 | 55 | 18
Col3 | 30 | 17
Col4 | 25 | 12
Column 1
Column 2
Column 3
Column 4
Optimized temperature and liquid composition profiles
Column | Reboiler duty [kW] | Condenser duty [kW]
Col1 | 867.8 | 2666.5
Col2 | 648.9 | 648.7
Col3 | 286.3 | 286.2
Col4 | 20 428.5 | 20 429.1
Process flowsheet of the distillation train for methanol, ethanol, and acetic acid recovery from SPO aqueous phase (capacity: 3082 kg/h) and SDPO aqueous phase (capacity: 3082 kg/h)
Ethanol
(azeotropic composition)
Methanol (99.99 wt%)
Acetic Acid
(30 wt%)
Energy requirements of the simulated process
From SPO and SDPO aqueous phase, high recovery rates (99.5% and 95% for methanol and ethanol, respectively) and high purity (99.99 vol% and 96 vol%, respectively) can be achieved adopting a simple process layout made up of three distillation columns.
Recovery of heavier compounds by means of distillation is not economically feasible due to low concentrations and associated high energy costs.
BTG’s process upgrades bio-oil in two steps: selective hydrogenation at mild conditions yields Stabilized Pyrolysis Oil (SPO), which is then deoxygenated at higher temperatures and moderate pressures to produce Stabilized Deoxygenated Pyrolysis Oil (SDPO).
In the FUEL-UP project, a distillation system is studied to recover alcohols from the aqueous phases of both SPO and SDPO-production.
The presented work involves process design, modeling, verification, and optimization to develop an efficient separation train for recovering value-added products from pyrolysis aqueous side streams, while aiming to reduce energy consumption and maximize product recovery.
Methanol and ethanol can be recovered at reasonable costs
36% of the total steam requirements are needed to purify methanol to grade A or grade AA (both require 99.85 wt% of purity) and the recovered ethanol (azeotropic grade)
The recovery of Acetic acid is not economically feasible, since the estimated heat requirement is over 600 MJ/kg of recovered Acetic acid.
48% of the total steam requirement is needed in the first column to remove most of the water content (~85 vol% of the feed).
Design specifications for each distillation column
The optimal number of trays and feed position are chosen to balance investment and operating costs.
NRTL model coefficients have been regressed in Aspen PLUS V14 (licensed by SINTEF) using the Maximum Likelihood algorithm following the same procedure adopted in Gilardi et al. [1] and implemented to COCO-COFE process simulator for this study.
1. M. Gilardi, F. Bisotti, A. Tobiesen, H. K. Knuutila, and D. Bonalumi, ‘An approach for VLE model development, validation, and implementation in Aspen Plus for amine blends in CO2 capture: the HS3 solvent case study’, Int. J. Greenh. Gas Control, vol. 126, p. 103911, Jun. 2023,
The optimal thermodynamic sizing of each column (total number of stages and feed positioning)