## Slide 1
NEWA Model-Chain and Validation Building-Blocks for Wind Conditions
JAVIER SANZ RODRIGO (CENER)
On behlalft of the NEWA consortium
NEWA Final Workshop, Bilbao, 2 April 2019

## Slide 2: Objectives of the NEWA Project
Development of a high-value data base of high-fidelity experiments
Development of methodologies for wind resource assessment and wind turbine site suitability based on a mesoscale to microscale mode-chain
Publication of a European Wind Atlas database accessible through a web interface
Definition of a verification and validation framework for the model-chain based on the experimental campaigns and means to quantify the uncertainties of the wind atlas

## Slide 3: NEWA Mesoscale-to-Microscale Model-Chain
@mesoscale
NEWA database of wind resource characteristics
30-year WRF down to 3 km resolution
+ downscaling to 50 m using WAsP
(generalized wind methodology)
Mesoscale multiphysics ensemble (UQ)
Open source model based on WRF
@microscale
Design tools based on CFD (RANS or LES)
Driven by mesoscale forcing
Include diurnal-cycle thermal stratification
Surface-layer characterization based on
aerial lidar scans of vegetation canopy
Open source model based on OpenFOAM (CFDWind3)

## Slide 4: NEWA Meso-Micro Challenge
Objective: Determine the applicability range of meso-micro methodologies for the NEWA validation domain
Application
Physics/ complexity
Operating conditions
NEWA
https://thewindvaneblog.com/newa-meso-micro-challenge-for-wind-resource-assessment-2a5f41f6df2c

## Slide 5: Verification & Validation (V&V) Process
https://thewindvaneblog.com/science-push-vs-market-pull-in-a-v-v-strategy-for-wind-assessment-b04bc615f16b
IEA-Wind Task 31 Wakebench international V&V framework

## Slide 6: V&V Building-Blocks
ABL climatology & site effects
Large scale topography
Hill-Hill (detached flow)
Mountainous
Complex Terrain
ABL
Homogeneous
Roughness Changes and Canopy
Hilly terrain
(attached flow,
heterogeneous
Inflow)
Isolated Hill (homogenous Inflow)
Coastal-Offshore
Terrain-induced flow separation
Diurnal Cycle
Valley-mountain flows
Roughness & Terrain-induced flow separation
Tendencies
Micro
Meso
Meso-Micro
Attached flow
Surface-layer & stability
Gap flows
Air-Sea interaction
Generalized Wind Climate
Froude
Weather events
Cabauw
GABLS3
MOST
Perdigao
Askervein
Röderser Berg
Østerlid-Blaconies
Hornamossen
Ryningsnäs
Alaiz
Bolund
Fino1
Rune
Ferry Lidars
NEWA Meso-Micro Challenge
Lee
Waves
Blockage
Dynamical-Statistical
Downscaling

## Slide 7: GABLS3 Diurnal Cycle
  Bosveld et al. (2014) The third GABLS Intercomparison case for evaluation studies of Boundary-Layer Models Part A: Case Selection and Set-Up. Boundary –Layer Meteorol 152: 133-156
30 km
Stationary synoptic
Clear skies
No fog
Substantial LLJ
6 years  9 days  night of 1–2 July 2006
+
Cabauw

## Slide 8: GABLS3: Mesoscale Forcings (”Tendencies”)
WRF
ERA Interim
9 > 3 > 1 km
24 hr spin-up
Tendencies from
3 km grid
Lav = 3x3 = 9 km
tav = 60 min
D = 160 m
zhub = 120 m
To microscale

## Slide 9: GABLS3 Benchmark
  Sanz Rodrigo J, Allaerts D, Avila M, Barcons J, Cavar D, Chávez Arroyo R, Churchfield M, Kosović B, Lundquist JK, Meyers J, Muñoz Esparza D, Palma JMLM, Tomaszewski JM, Troldborg N, van der Laan MP, Veiga Rodrigues C (2017) Results of the GABLS3 diurnal cycle benchmark for wind energy applications. J. Phys.: Conf. Ser., 854: 012037

## Slide 10: Open Science Benchmarking
Sanz Rodrigo J, et al. (2017) https://github.com/windbench/gabls3

## Slide 11: Benchmarks on Integrated Quantities (AEP)
https://thewindvaneblog.com/newa-meso-micro-challenge-phase-1-cabauw-and-fino1-2ec51252f946
https://thewindvaneblog.com/newa-meso-micro-challenge-phase-1-cabauw-and-fino1-2ec51252f946
https://thewindvaneblog.com/newa-meso-micro-challenge-phase-2-r%C3%B6deser-berg-5404eafbe7dc

## Slide 12: Conclusions
NEWA open-source model chain based on WRF and OpenFOAM
V&V process conducted under the IEA-Wind “Wakebench” model evaluation framework
“Golden” benchmarks: open-access repositories recognized as reference for validation of wind flow models by the wind energy community
Plenty of validation cases yet to be leveraged from the NEWA experimental database

## Slide 13: Acknowledgements
The NEWA project is supported by a European Commission’s ERA-Net Plus project, number 618122, joining national projects from 9 funding agencies from 8 member states:
Public Service of Wallonia, Department of Energy and Sustainable Building (Belgium)
Department of Economy, Science and Innovation Flemish Government (Belgium)
Danish Energy Authority (Denmark)
Federal Ministry for the Economic Affairs and Energy, on the basis of
the decision by the German Bundestag (Germany)
Latvijas Zinatnu Akademija (Latvia)
Fundação para a Ciência e a Tecnologia (Portugal)
Ministerio de Economía y Competitividad (Spain)
The Swedish Energy Agency (Sweden)
The Scientific and Technological Research
Council of Turkey (Turkey)
www.neweuropeanwindatlas.eu