## Slide 1: 20190406 SPR: USP5 and HDAC6
SA chip used in Biacore T-200
Running Buffer: 20 mM Hepes pH 7.4, 150 mM NaCl, 0.005% (v/v) Tween-20, 0.5% (v/v) DMSO
Biotinylated USP5 Zf-UBD(171-290) at 0.05 mg/mL captured to chip channel 2 (300 s injection) and 3 (150 s injection) and HDAC6 Zf-UBD (1109-1215) at 0.05 mg/mL captured to chip channel 4. Channel 1 was left blank as a reference. The chip was treated with 3x60 s injections with 50 mM NaOH
Samples were diluted 1:4 8-pt concentration series
Data fitted with steady state affinity model
NB: error-degasser failure: vacuum failure-instrument operation not affected but sensograms affected by airspikes

## Slide 2: Z99599878
USP5
USP5
HDAC6
USP5: KD= NB (n=2)
HDAC6: KD= NB (n=1)

## Slide 3: Z327330246
USP5: KD= NB (n=2)
HDAC6: KD= NB (n=1)
USP5
USP5
HDAC6

## Slide 4: MFCD02363436
USP5: KD= 49 ± 1 µM (n=2)
HDAC6: KD= 12 µM (n=1)
USP5
USP5
HDAC6

## Slide 5: STOCK6S-31603
USP5: KD= NB (n=2)
HDAC6: KD= NB (n=1)
USP5
USP5
HDAC6

## Slide 6: F3351-0339
USP5: KD= NB (n=2)
HDAC6: KD= NB (n=1)
USP5
USP5
HDAC6

## Slide 7: F3351-0338
USP5: KD= NB (n=2)
HDAC6: KD= NB (n=1)
USP5
USP5
HDAC6

## Slide 8: MFCD00459040
USP5: KD= 82 ± 1 µM (n=2)
HDAC6: KD= 50 µM (n=1)
USP5
USP5
HDAC6

## Slide 9: BS-11825
USP5: KD= NB (n=2)
HDAC6: KD= NB (n=1)
USP5
USP5
HDAC6

## Slide 10: MFCD00033285
USP5: KD= NB (n=2)
HDAC6: KD= NB (n=1)
USP5
USP5
HDAC6

## Slide 11: D715-279
USP5: KD= NB (n=2)
HDAC6: KD= NB (n=1)
USP5
USP5
HDAC6

## Slide 12: AE-641
USP5: KD= 36 ± 0.7 µM (n=2)
HDAC6: KD= 10 µM (n=1)
USP5
USP5
HDAC6

## Slide 13: UBXML78
USP5: KD= 34 ± 1 µM (n=2)
HDAC6: KD= 1.8 µM (n=1)
USP5
USP5
HDAC6