## Slide 1
Blade pitch optimization
for an offshore vertical axis
wind turbine model
Hubert Branger, Sukanta Roy, Christopher Luneau,
Denis Bourras and Benoit Paillard
branger@irphe.univ-mrs.fr
Support:

## Slide 2
Outline
- Introduction
- IRPHE/Pyhtéas wind-wave facility
Wind turbine physical model
- Tests and Results on pitching optimization
Conclusions - Perspectives
Notes: Outline of the communication, Introduction of the topic

## Slide 3
All the large offshore wind turbines in the world are Horizontal Axis Wind Turbines
There is no Large Offshore Vertical Axis Wind Turbine (VAWT)
No real background on the large ones
Not able to self-start  need a motor to start
- Not able to self-stop  need a brake system to stop
- Vibrations, torque oscillations
- No Financial support
Introduction:
Notes: troposkien

## Slide 4
1) No need to have a Yaw system if the wind direction change
But there might be some good points :
2)  gravity center is lower  floatter 20% smaller Guo et al. (2018), Huijs et al (2018)
3)  the turbine still works even at large inclination good for floating platforms Chowdhury et al (2016)
4)  Wind Farms: more turbines/km2  more Power/km2 Cp is better if turbines work 2x2 or 3x3
Arab et al (2017), Douak etal (2018)

## Slide 5
Three years ago: Eolfi had the SpinFloat project:
 to design 6 MW Vertical Axis Wind Turbine with pitching blades
90 m
 build a small experimental model
 make experiments in IRPHE facility
 find good pitching laws
Irphe had French support
in order to :

## Slide 6
Why pitching the blades ? 1)  For a better driving force
Without Pitch
Apparent wind speed
U
W
F total
FTangential
Fnormal
wind speed
Ftangential is the driving force
Apparent wind speed
U
W
F total
FTangential
Fnormal
With Pitch
wind speed
b
Better torque coefficient
W+
W

## Slide 7
Why pitching the blades ?
2) Good for self starting :
W
Incoming Wind speed
U
No pitch  No movement  equilibrium position
1
2
3

## Slide 8
b3
b2
b1
Why pitching the blades ?
W
Incoming Wind speed
U
Max Drag
Min Drag
Max Lift
1
2
3
2) Good for self starting :
With pitch  rotation starts

## Slide 9
Why pitching the blades ?
3) To slow down or stop:
b3
b2
b1
W
U
Max Drag
Min Drag
Max inverse Lift

## Slide 10
Pitching the blades for Vertical Axis Wind Turbines is not new:
Very Recent papers:
- Douak et al (2018)  pitching efficient for self starting
- Chen et al (2018) :  pitching is efficient with a simple sinus function b = bmax sin( q )
- Zhao et al (2018) :  efficient pitching b(q,TSR) = bmax sin(q) - b2 (TSR) sin2(q)
- Bayati et al 2018, Battisti et al 2018, Li et al 2018  pitching is efficient: 20% on Power Coefficient
- Xu et al 2019:  more complex pitching law:
BUT , they mainly concern:
relatively small turbines,
or blades with large chords,
or turbine with high solidity ratio,
or rod crank or cycloid systems (center of rotation of the blades center rotation of turbine)
Only a few papers are related to large vertical axis wind turbines
There have been many published papers on Vertical wind turbine pitching

## Slide 11
IRPHE/Pythéas Large air sea interaction facility in Marseille
60m
5m
3.0 m
40 m
2.5 m
Wind 15 m/s

## Slide 12
Tri-floater, Horizontal axis
Tri-floater Vertical axis
We previously made research works on floating wind turbines in this faciliy

## Slide 13
To design the wind turbine physical model in relation with the EOLFI requirements for the WINDFLOAT project, we made preliminary studies using open source software XFOIL and QBLADE (Double Multi Stream Tube model + Lift Line Theory + some 3D effects)
Studies on aspect ratio : aR=(blade length/ diameter)
+
Studies on solidity ratio: sR=(number of blades * Chord/ Diameter)
+
Studies on different blade profiles
Finally for the physical model, we end to :
 3 Selig 1046 blades,
 Hight: 90 cm ,
 Chord: 9 cm,
 Radius: 80 cm Solidity Ratio=0.17
Blocage factor=0.18
Cross section of the facility

## Slide 14
Selig 1046 blade
Wind
There is nothing on literature about Selig 1046 blades.
 We measured Lift and Drag Coefficients for all possible incidence angles ( -180° to + 180° )
Dof Sensor
Rotating device
Lift coefficient : comparisons with Naca profiles

## Slide 15
We built almost everything
(connections, bases, caps, electronics, …)

## Slide 16
To pitch the blades, we used 3 servomotors
3 Servo motors
Servo motors very efficient: Able to pitch 60° in 1/10 s

## Slide 17: How it works: Control-command loop for the pitch
We have a pitch command:
U : wind speed
TSR : Tip Speed Ratio= R W /U q : blade azimutal position
Computer with Python program
Teensy card with an ARDUINO Software coding
Wind speed U
Rotational encoder to measure W, TSR and q
Command
Another Teensy Card controls the servomotor mouvements
Control
Pitch
updating

## Slide 18
Results: With a very simple sinus command
Wind turbine rotational velocity increased by a factor 4 !
W : Rotational speed
Azimutal Rotational sensor 360°0°
(equivalent to a mechanical rod-crank or cycloid systems
With pitch
Without pitch

## Slide 19
Results:
Self-starting :
Minimum wind speed to start rotation
U= 4m/s , no pitch: turbine does not start
No pitch
Azimutal initial position of blade 1 before start (°)

## Slide 20
Results:
Self-starting :
U= 4m/s , no pitch: turbine does not start
No pitch
With pitch
U= 1m/s : pitch on turbine starts
Minimum wind speed to start rotation
Azimutal initial position of blade 1 before start (°)

## Slide 21
b to stop = - b to start
If you change b in –b, the turbine slows down and stops.
Results:
Self-stop :

## Slide 22
1) Pitch laws: not only sin (q) but also the harmonics: sin (2 q) , …
3) Pitch laws: not only sin (q) but also the quadrature cos (q)
2) Pitch laws: not only sin (q) but also phase shift sin (q + j) )
4) Pitch laws: coefficients should depend on TSR
How to find better pitch laws ?
q = Blade Azimut
 12 parameters to find

## Slide 23
How to find « optimal » coefficients a1, a2, … a12 ?  Genetic algorithm « Dakota » (Open source Optimization toolbox)
Dakota routines are based on Bayesian statistics, hybrid optimization
Goal: TSR maximum
DAKOTA
Pitch Laws Python
servo moteurs input
Teensy Card / Arduino commands
Dakota sugests a first set for the 12 values (a1, a2, - -, a12)1
TSR
TSR sent to the computer

## Slide 24
How to find « optimal » coefficients a1, a2, … a12 ?  Genetic algorithm « Dakota » (Open source Optimization toolbox)
Dakota routines are based on Bayesian statistics, hybrid optimization
Goal: TSR maximum
DAKOTA
Pitch Laws Python
servo moteurs input
Teensy Card / Arduino commands
TSR
TSR sent to the computer
Dakota sugests a second set for the 12 values (a1, a2, - -, a12)2
Automatic loop

## Slide 25
How to find « optimal » coefficients a1, a2, … a12 ?  Genetic algorithm « Dakota » (Open source Optimization toolbox)
Dakota routines are based on Bayesian statistics, hybrid optimization
Goal: TSR maximum
DAKOTA
Pitch Laws Python
servo moteurs input
Teensy Card / Arduino commands
TSR
TSR sent to the computer
Dakota sugests N sets for the 12 values (a1, a2, - -, a12)N
Automatic loop
The procedure is automatic (no hand control) 1 run = 2 min ; 1 hour  30 runs ; 24 hours  720 runs without interruptions
We made Thousands of non stop runs.
 Dakota find the best parameters (a1, …, a12) to maximize TSR

## Slide 26
Main Result :
Video:
U=4 m/s
Pitch Off
Then
Pitch On

## Slide 27
TSR multiply par 20 with Pitch on !!!!

## Slide 28
We made PIV measurements to measure the flow around the blades
Twin Laser Yag
camera
DANTEC software
Air flow is seeded with a lot of particles
Airbus Helicopter seeding system

## Slide 29
wind
Velocity
Stream Lines
Vorticity
No Pitch
With Pitch

## Slide 30
wind
No pitch
PIV measurements
OPEN FOAM Simulations
With pitch

## Slide 31
Conclusions:
We build models, conducted experiments, found quite optimized pitching laws
Pitch:  allows self-starting at low wind speed
 possibility to slow down and stop the turbine
 increases a lot the rotational velocity (more particularly at low wind speed)
 increase the Power by 20 % with water turbine
80m
Nenuphar Vertiwind
90 m
Eolfi
Spinfloat
Unfortunatly, the two French VAWT projects are canceled 
New experiments are planned with a Water Turbine with blades completely under the water Thank You
Next: