## Slide 1: Development of a second order dynamic stall model Niels Adema
Cork
June 18th 2019
Cssdf

## Slide 2: Introduction
Work done as part of EUREC Master programme
Work started in July 2018
Finished in December 2018
Work supervised by:
  Menno Kloosterman (DNV GL)
  Dr. Gerard Schepers (Hanze/ TNO)

## Slide 3: Background
Design Standards require rotor parked in storm conditions
Yaw system is not operational
Design driving loads
Low damping on blade edgewise modes
Uncertainty in dynamic stall models

## Slide 4: Limitations of current dynamic stall models
Designed for helicopter rotors
Small angles of attack
Uncertain at high angles of attack
No explicit model for self induced vortex shedding
Airfoil in deep dynamic stall. Source: Cardiff University

## Slide 5: Overview of current Dynamic Stall models
Beddoes-Leishman
  Industry workhorse
  Designed in the 80s for helicopters
  1st order equations
ONERA
  Developed for helicopter applications
  1st and 2nd order models
  Requires (lots of) empirical data.
Øye
  Simple model
  Using only time lagged separation position
Chordwise separation position “f“, source: DTU 2004
Steady Kirchoff equation as a function of steady separation position f
Dynamic lift coefficient using time lagged separation position f” as interpolant between fully attached and fully separated flow

## Slide 6: Why a new model?
Need for an engineering model
Suggested model by Herman Snel
Presented EWEC 1997 (Dublin)
Partially based on ONERA model.
Model for vortex shedding
Tuned against Ohio State University measurements
Time series of Cl showing vortex shedding: (OSU measurements)

## Slide 7: Snel Dynamic stall model – 1st order term
The Snel dynamic stall model adds a first and second order term to the steady lift coefficient
The first order term is modelled using a linear 1st order differential equation
The forcing term (ft1) and time constant (cf10) are computed using:

## Slide 8: Snel dynamic stall model – 2nd order term
Working principle
Based on a non-linear mass-spring damper system
Comparable to Van der Pol oscillator
K(x)
C(x)
F(x)
Nonlinear mass/spring/damper system
Chaotic behaviour of van der Pol oscillator. Source: https://en.wikipedia.org/wiki/Van_der_Pol_oscillator

## Slide 9: Snel Dynamic stall model – 2nd order term
The 2nd order model is modelled using a non-linear 2nd-order differential equation
The damping (cf21) is defined as:
The spring term (cf20) is defined as:
Finally the forcing term is defined as:
This equation can be considered as a non-linear mass-spring-damper system

## Slide 10: Snel Model Baseline Results – OSU measurements
Measurements by Ohio State University (OSU)
Dynamic measurements carried out on oscillating airfoils (This study focusses on NACA 4415 and S809)
Reynolds number: 1.25 Million
Chord of 0.457m
Tunnel Speed 37m/s up to 42m/s

## Slide 11: Snel Model Baseline results – NACA4415 low reduced frequency (1/2)
Vortex shedding in measurements
Limited oscillation in model.
Dip in model results (downstroke)

## Slide 12: Snel Model Baseline results – NACA4415 low reduced frequency (2/2)
More unsteadiness in measurements
Model well below measurements
Limited vortex shedding

## Slide 13: Snel Model Baseline results – NACA4415 high reduced frequency
Unsteadiness disappears
1st and 2nd order model produce similar results
2nd order term fades out

## Slide 14: Snel Model Baseline results - Conclusions
Dip in the downstroke prediction
Vortex Shedding is not predicted at right time
The predicted shedding frequency is independent on angle of attack
Noted from model formulation:
  The Snel model uses only (steady) lift data, which tends to zero at high angles of attack
  Two equations are dimensional and should be non dimensional

## Slide 15: Snel Model Improvement(s) – (1/3)
Made model non-dimensional by addition of the time constant
Set forcing term to zero in downstroke &
Reduce amplitude of forcing
Modify damping term in downstroke, shedding still allowed
Make Strouhal number of the spring term dependent on projected chord length

## Slide 16: Snel Model Improvement(s) – (2/3)
All steady/dynamic lift coefficient terms changed to steady/dynamic normal force coefficients
Steady normal and chordwise coefficients follow:
Inverse calculation yields lift and drag
coefficients following:

## Slide 17: Snel Model Improvement(s) – (3/3)
Airfoil Specific Time Constants for Implementation in Bladed
Unconstrained Minimization Algorithm for Lowest Overall Error
Three Analysis
  All OSU Cases
  Low Reduced Frequency
  High Mean Angle of Attack
Three sensitive constants found
  First Order Time Constant
  Second Order Forcing Time Constant
  Strouhal Number

## Slide 18: Snel Model Improved results – NACA4415 low reduced frequency (1/2)
Improved capture of oscillations
Phase of oscillations not always correct
Frequency captured well

## Slide 19: Snel Model Improved results – NACA4415 low reduced frequency (2/2)
Capturing of higher frequency at higher angle of attack
2nd order model bit below measurements.

## Slide 20: Snel Model Improved results – S809 low reduced frequency
Using S809 give good results
Bit below measurements
Trends well captured

## Slide 21: Snel Model Improved results – Frequency Analysis
Power Spectral Density Estimate
Removed Forcing Frequency
NACA 4415 at Low Reduced Frequency
Frequency Prediction Correct
S809 at Higher Reduced Frequency
Frequency Prediction Still Correct

## Slide 22: Snel Model Improved results – Absolute Error Analysis
Absolute Error Following
Error between model and OSU measurements reduced significantly

## Slide 23: Comparison to Beddoes-Leishman model (1/2)
Beddoes-Leishman generally below measurements
Beddoes-Leishman predicts no vortex shedding

## Slide 24: Comparison to Beddoes-Leishman model (2/2)
At high frequency 2nd order term fades
Beddoes-Leishman well below measurements
Improvement with respect to Beddoes-Leishman

## Slide 25: Validation against New MEXICO experiments (1/5)
Model Experiments in Controlled Conditions
Instrumented Rotor with 4.5m Diameter
Large Scale Low Speed Facility of the German Dutch Wind Tunnels
Standstill (both Axial & Yawed) with varying Pitch and Wind Directions
MEXICO model wind turbine, source: ECN
Design Load Cases with Dynamic Stall and Vortex Shedding

## Slide 26: Validation against New MEXICO experiments (2/5)
Axial Flow – Pitch -2.3° - Angle of Attack ± 90°
Standard deviation matches
Bladed Normal Force prediction generally higher
than measurements
Similar offset found in other studies
Frequency much higher than measurements
  Expected outcome with 0.2 Strouhal number
No explanation of the difference is found currently

## Slide 27: Validation against New MEXICO experiments (3/5)
Yawed Flow – Pitch 90° - Wind Direction 30° from N
Blade 1, Angle of Attack ± 25°
Bladed Normal Force Prediction and Standard Deviation matches quite well with New Mexico
Frequency prediction too high but closer

## Slide 28: Validation against New MEXICO experiments (4/5)
Yawed Flow – Pitch 90° - Wind Direction 30° from N
Blade 2, Angle of Attack ± -20°
Unsteadiness in model disappears

## Slide 29: Validation against New MEXICO experiments (5/5)
Interesting Case at Wind Direction -45° from N
Predicted Frequency = Blade Natural Frequency
Not seen in measurements
  Airfoil Specific Time Constants?
  Strouhal Number of different airfoils?
    In Mexico Measurements lower than 0.2
  Flexibility of the blades?
  Wind tunnel effects?
Promising but more research required

## Slide 30: Conclusions and Recommendations for Future Work
Conclusions:
Analysis and improvement to the Snel Second Order Model using OSU experimental data
Snel Model looks promising for predicting unsteady vortex shedding
Improvement with respect to Beddoes-Leishman
Combination with New MECIXO data shows need for further research and validation

## Slide 31: Conclusions and Recommendations for Future Work
Future Work:
Validation of the Snel Model with CFD data
Dedicated Analysis of the Model in combination with negative angles of attack
Combination of Beddoes-Leishman and Snel Second Order term
Test the Model with Full Scale Turbine Data (DAN-AERO project)
Dedicated analysis of Snel model in combination with Bladed

## Slide 32: Thank you for your attention! Questions?
Niels Adema
nielsadema1994@gmail.com
+31 6 11248730

## Slide 33: References
J.G. Leishman, “Challenges in modelling the unsteady aerodynamics of wind turbines”, Wind Energy, Vol. 5, 2002, pp. 85-132. DOI:10.1002/we.62
Choudhry et al., “An insight into the dynamic stall lift characteristics”, Experimental Thermal and Fluid Science, Vol. 58, 2014, pp. 188-208, DOI:10.1016/j.expthermflusci.2014.07.00
W.J. McCroskey, “The Phenomenon of Dynamic Stall”, Technical Report NASA-TM-81264, 1981, Digital Link: https://ntrs.nasa.gov/search.jsp?R=19810011501
S. Schreck, “The NREL Full-Scale Wind Tunnel Experiment”, Wind Energy, Vol. 5, pp. 77-84, DOI: 10.1002/we.72
J.G. Schepers, H. Snel, “Model Experiments in controlled conditions”, Technical Report ECN-E-07-042, 2007, Petten, The Netherlands
V.A. Riziotis et al., “Stability analysis of parked wind turbine blades using a vortex model”, Conference: Science of making torque from the wind, Heraklion, Greece, 2010
H. Snel, “Heuristic modelling of dynamic stall characteristics”, European Wind Energy Conference, Dublin Castle, Ireland, 1997, pp. 429-433
K. Boorsma, J.G. Schepers, “New MEXICO experiment Preliminairy overview with initial validation”, Report ECN-E--14-048, 2014, Petten, The Netherlands
J.G. Schepers, K. Boorsma et al., “Final report of IEA Task 29, Mexnext (Phase 1), Report ECN-E--12-004, 2012.
M.A. Khan. “Dynamic Stall Modeling for Wind Turbines”. MSc Thesis, TU Delft, 2018. To be found digitally on: uuid:f1ee9368-ca44-47ca-abe2-b816f64a564f