## Slide 1: unroutable LHCONE traffic
Bruno Hoeft / KIT
Michael O‘Connor / ESnet
Richard Cziva / Esnet
Samuel Ambroj Perez / KIT
Magnus Bergroth / NORDUnet

## Slide 2: LHC  VPNs
LHCOpticalPrivatNetwork  a CERN centric star VirtualPrivatNetwork
  VPN with 15 participants only, mutual agreements between connected partner, no formal rules

## Slide 3: LHCOpenNetworkEnvironment – MAP
Australia
ASIA
AMERICA
EUROPE
LHCONE  a still growing international distributed VPN
  VPN with 104 endsites connected through 26 VirtualRouting andForwarding implenentations at the connecting Network Service Providers (NSPs)

## Slide 4: NSP Packet Filtering Requirements
All LHCONE Traffic is subject to the following conditions:
Traffic injected into the LHCONE must only be originated from addresses within an LHCONE routable prefix
Only address ranges present in the LHCONE routing table should be transported on the network
Objective: In order to maintain route symmetry and access control, each NSP will implement policy and packet filters to manage their connected customer address prefix ranges.
Ensures that a return route exists in the LHCONE network
Blocks spoofed packets (Similar to BCP 38)
https://twiki.cern.ch/twiki/pub/LHCONE/LhcOneVRF/LHCONEconnectionguide-1.2.pdf

## Slide 5
Prefix Lists will be negotiated between connecting institutions and their NSP within the constraints imposed by the LHCONE Acceptable Use Policy (AUP).
LHCONE NSPs have agreed to to configure:
BGP import filters
Source address packet filters
End sites are encouraged to implement source address filters at their edge in order to eleminate their own unroutable LHCONE packets. NSPs will generally discard none compliant packets without informing the site.
Connecting institutions/sites will not add prefixes to the LHCONE routing table without direct cooperation with their NSP.
AUP: https://twiki.cern.ch/twiki/bin/view/LHCONE/LhcOneAup
NSP Border Gateway Protocol (BGP) Import Policy

## Slide 6
ESnet counted:
All LHCONE ingress packets
Unroutable source packets
Packets with non-lhcone/missing origin ASN
* corrected for netflow sampling rate (1000)
aarnet
aglt2
anl
ansp
asgc
bnl
caltech
canet
cern
cernlight
duke
flr
fnal
geant
ind-gpop
internet2
JGN
kiae
kreonet
cern
ornl
mit
net2
nordunet
ou
pnnl
rnp
sinet
slac
tacc
transpac
uchicago
ucsb
ucsd
uiuc
unl
uta
uwmadison
vanderbilt
ESnet
Three months of ESnet netflow IPv4 & IPv6 sampling from Feb. 2019 - April 2019 for the following connected sites and peers
The Investigation

## Slide 7
Very good results!!!
58 Unroutable source addresses from networks in Thailand arrive via JGN LHCONE transit services
4 Unroutable source addresses from networks in Canada arrive via I2 LHCONE transit services
ESnet monitoring Unroutable Source Addresses by percentage

## Slide 8
A small number of U Toronto hosts are transmitting large amounts of data on LHCONE. ESnet had routes for U Toronto in the past.
This may be a reachability problem for U Toronto. ESnet no longer has any routes to their ASN 239
ESnet monitoring

## Slide 9
unsampled Ingress Packet Filters based on LHCONE routing table
Total LHCONE traffic  0,2% / none ICMP  approx. 57%
DE-KIT : unroutable IPv4/6 LHCONE packet statistics
priv
AARNIEC-RoEduNet
AIT-TH
ASGC-NET
Associação Rede Nacional (BR)
CANARIE
Bcnet Vancouver
CAS-PRG-6TCZ
CAS-TCZ
CERNET
CHINANET-FJ
CIECCHQ-CN
CIEMAT
CZ-RELCOM-19930901
DFN WIN-IPV6
ERNET-IN
ES-REDIRIS-20010521
Fundação Carlos Chagas Filho (BR)
FR-RENATER
Color legend : IPv6 and IPv4 / IPV4 / IPv6
FR-IN2P3-LAL-ORSAY
FR-IN2P3-LLR-PALAISEAU
FR-CEA-SACLAY-GRILLES
FR-IN2P3-LPNHE-PARIS
FR-IN2P3-LPC-CLERMONT-AUBIERE
FR-IN2P3-LAPP-ANNECY
FR-IN2P3-CPPM-MARSEILLE
GEANT
GARR-P-P
GARRB-NET
GARRX-NET
GR-GRNET-19991208
GZIN
IANA – reserved
IHEP-IPv6
Imperial College London
Indiana University
INFNNET-LNF
Inst. Nat. de Physique Nucleaire
IT-GARR-20011004
JINR-NET
Kasetsart University, Thailand
KREONet-KR
NL-GEANT-20020131
PNPI
REDIRIS
RoEduNet-IPv6-NET-1
RRC-KIAE-Moscow
RU-ROSNIIROS-20180806
RWTH Aachen
SAVECOM SAVECOM-NET
SINET-JPNIC
SUT-TH
T-NCU.EDU.TW-NET
T-NSYSU.EDU.TW-NET
T-NTHU.EDU.TW-NET
TANET
TANET-B T-HCRC.EDU.TW-NET
TANET-BNETA
TANET-BNETS Taiwan
TANET-NET
TANET-NET Taiwan
TANET Taiwan
TEIN2-CERNET
THAINET-TH
TFN-NET TAI-SHIN-NET
TRIUMF
UAM
UK-GEANT-20020131
UNI Michigan
UNIVERSIDADE DE SAO PAULO
UNI of Nebraska-Lincoln
University of Toronto
IJS-IPv6-NET - Ljubljana
VANDERBILT
WIN-IP
 | IPv4 | IPv6
Total packets (during 4 weeks) | 1.044.471 | 1.376.338
Packet/day | 37.302 | 35.290
Privat IP destination | 10.0.0.0/16, 172.16.0.0/12, 192.168.0.0/16 | fe00::/16
Number of sources | 44 + private | 33 + private
Ingress Packet Filters

## Slide 10
- Reduced to 30 different sites only by
- Combining private address areas
- Removed sites with less than 1000 packets (per month)
- Pull different subnets of one source/site together
unroutable IPv4 packets
total : 1.010.889 + 33582 = 1.044.471
packts per day: 19.707
ICMP approx. 43% = 459.508
none ICMP = 584.963

## Slide 11
unroutable IPv4 packets
632 different sources
min: 3 average: 53 max: 2910
33582
16 different sources
min: 12 average: 6.834 max: 41.790
109340
67 different sources
min: 2 average: 1.195 max: 31.734
80093
2 different sources
min: 26.229 average: 26.275 max: 26.321
52650
33 different sources
min: 2 average: 12.907 max: 418.228
425931
18 different sources
min: 5 average: 3.559 max: 22.647
61566
Reduced by Geant and FR-Renater and GARR (ICMP only)
18 diffrent sources
min: 5 average: 3.559 max: 22.647
61366

## Slide 12
1 source
min:
66.005
66005
1 source
min:
208.693
208693
11 different sources
min: average: max:
4 5.050 23.712
55554
6 different sources
min: average: max:
10 152.437 749.085
914626
1 source
min:
52.512
52512
IPv6 Filter : unroutable LHCONE packet
filter Privat address space (link local)
IT-GARR  ICMP packet of network devices and the main injector (2 Perfsonar Server) are became part of LHCONE
FR-Renater  ICMP packts of network devices

## Slide 13
              automate unroutable packet information gathering
  → store into a organized and structured database (kibana)
  visualise the data (packet beat / elastic search / Kibana / grafana) with different levels
    abstract overview
    and zoomable into detailed view (up to source/dest. of a single packet) this data shall be available for the LHCONE connected sites (but not for the world), one idea:
    community securing the data
    restrict access --> personal authentication enabled (via eduGAIN)
project just started,
working on first results by the end of this year (2019)
Project @ DE-KIT : unroutable packet -- web portal

## Slide 14
Worldmap of misrouted packets captured during last 30 days

## Slide 15
Routing-tables of
collected and analysed NSPs
LHCONE regional diffrent routing tables

## Slide 16
Internet2 IPv4 (Oct. 2018)

## Slide 17
Internet2 IPv4 (2019)

## Slide 18
Number of unroutable LHCONE packets reduced from 2.4million to 1million found 1.4 million packtes marked as „false positive“ or could be sorted out
LHCONE ingress filtering/control has improved dramatically since measurement began in Q1 2018!
  But still Detection will be beneficial:
      Regularly scheduled monitoring?
      Periodic NSP self run audits?
Growth in Asia has likely contributed to a small number of exceptions.
  Work towards Prevention
      NSPs initiative at Edge Site filter configuration
        RPF → too strict? → Rather opt for ACLs
        Templated policy & filter configuration
Routing table inconsistency may also be a source of false positives.
Conclusion / actions
Site 2
Site 3
NREN 1
Site 1
ACL
NSP
ACL
ACL
ACL
ACL
ACL
RPF
RPF
RPF

## Slide 19
Questions
Suggestions
Discussion

## Slide 20
Backup Slids

## Slide 21: Recent presentations
unroutable LHCONE packets:
  LHCOPN/ONE Meeting March 06, 2018 https://indico.cern.ch/event/681168/contributions/2848474/attachments/1611723/2559528/LHCONE-Filter-Policy-Practice.pdf
  LHCOPN/ONE Meeting Oct. 30, 2018 https://indico.cern.ch/event/725706/contributions/3120030/attachments/1743507/2821722/LHCONE-MTU-recommendation.pdf
  LHCOPN/ONE Meeting June 04, 2019 https://indico.cern.ch/event/772031/contributions/3360612/attachments/1855532/3047503/LHCONE_Edge_Filtering_Policy_and_Practice_Umea_1.pdf
regional LHCONE routing table diffrences:
  LHCOPN/ONE Meeting Oct. 30, 2018 https://indico.cern.ch/event/725706/contributions/3149436/attachments/1744301/2823417/LHCone_routing_digging.pdf
  LHCOPN/ONE Meeting June 04, 2019 https://indico.cern.ch/event/772031/contributions/3428968/attachments/1855890/3048260/LHCone_routing_digging_2019.pdf

## Slide 22
LHCONE NSP
ASN 99
L3 Exchange Fabric
ASN 100
Compute Center
ASN 101
Compute Center
ASN 102
Compute Center
ASN 103
BGP
BGP
BGP
BGP
An exchange is like an NSP:
BGP import filtering
Packet filtering
Community based BGP filtering
An exchange is like a site:
Require the full LHCONE table via a transit NSP
Packet filters are configured and require maintenance
Will L3 Exchange Fabrics implement and maintain LHCONE specific services?
Should there be an LHCONE defined role for these network organizations?
Are they permitted to attach new sites?
Is an L3 Exchange an edge site or an NSP?
What process defines how they add new sites?
Indiana GigaPOP is a current ESnet example.
SOX is planned to be the second and will connect UFL, FSU and others.
Edge Filtering Special Case
L3 Network Exchange Fabrics

## Slide 23
private
grouping different CIDR of one organization
removing sites with less than 1000 unroutable packets over four weeks
All counted packets (44 Sites)

## Slide 24: Routing tabel diffrenz e.g: Géant (IPv6)
Missing :
AARNET
  Via Internet2 ESnet
AMPRO
  via ESnet
No change between Oct. 2018 and June 2019