## Slide 1: Mimicking EMG features of amputated limbs by restricting unaffected limbs
Morten Bak Kristoffersen, Andreas Franzke, Alessio Murgia, Raoul Bongers, Corry van der Sluis | TIPS, March 20 2019
Notes: RB:

## Slide 2: Introduction
Research on upper limb prosthetics often uses able-bodied participants
This is, unfortunately, not going to change
Validity
  Direct Control vs. Machine learning control
EMG of able-bodied vs those with an acquired limb deficiency
  Effect of movements of the wrist joint and fingers
Can EMG of able-bodied be made more alike the EMG of those with an acquired limb deficiency?

## Slide 3: Methods

## Slide 4: Methods
Measure EMG from both limbs while performing bilateral movements
3 postures
  Down, Front, Reaching
Able hand restriction
  Yes/No

## Slide 5: Methods
Sampling rate: 1000 Hz
8 Otto Bock 13E200=50AC Electrodes
7 movements
  3 contrations of 3 seconds
  3 seconds of rest between contractions
Movements | 
Hand open | Wrist extension
Key grip | Pronation
Fine pinch | Supination
Wrist flexion | 

## Slide 6: Methods
Acquired unilateral limb-loss at the transradial level.
18+ years old.
The stump needs to be properly healed.
2 cm broad region on the forearm with no scaring.
14 participants joined
Inclusion criteria

## Slide 7: Demographics
Par No. | Sex | Age | Loss of dominant hand? | Time since loss (years) | Prosthesis Type | How often use prosthesis ? | How many hours prosthesis user per day
1 | F | 43 | No | 2.5 | Cosmetic | Daily | 5 -- 12
2 | M | 74 | Yes | 53 | Myo | Daily | 12++
3 | F | 50 | No | 21 | Myo | Daily | 12++
4 | M | 26 | Yes | 0.5 | - | - | -
5 | M | 59 | Yes | 25 | Myo | Daily | 12++
6 | M | 47 | No | 3 | Myo | Daily | 5--12
7 | M | 30 | No | 7 | Myo | Daily | 12++
8 | M | 45 | Yes | 11 | Myo | Daily | 5--12
9 | M | 80 | Yes | 29 | Myo | Daily | 2--5
10 | M | 67 | Yes | 47 | - | - | -
11 | M | 54 | No | 26 | Myo | Daily | 12++
12 | M | 52 | No | 32 | - | - | -
13 | M | 59 | Yes | 49 | Myo | Daily | 5--12
14 | M | 62 | No | 47 | Myo | Daily | 12++
Summary | 86% M | 53 (15) | 50% Yes | 25 (18) | 71% Myo | 78% Daily | 42% 12++

## Slide 8: Methods

## Slide 9: Outcome measures
Common EMG features used in machine learning
  Mean absolute value
  Slope sign changes
  Zero crossings
  Wavelength
Similarity of EMG / Shared control signals
Non-negative Matrix Factorisation (NNMF)
  Cosine of Principle Angle [Cheung et al 2005]
  Normalised Dot Product [Cheung et al 2005]
EMG pattern distinctiveness
  Next talk (Andreas Franzke)

## Slide 10
  Cheung et al 2005, INT J NEUROSCI

## Slide 11: Results
Mean Absolute Value
* p=.003

## Slide 12: Similarity of EMG
Participant | Unrestricted |  | Restricted | 
 | Unaffected | Affected | Unaffected | Affected
1 | 6 (90%) | 6 (91%) | 6 (91%) | 6 (90%)
2 | 7 (95%) | 5 (90%) | 7 (94%) | 6 (90%)
3 | 7 (94%) | 6 (94%) | 6 (92%) | 7 (95%)
4 | 7 (95%) | 8 (100%) | 7 (94%) | 8 (100%)
5 | 6 (93%) | 7 (94%) | 6 (91%) | 7 (94%)
6 | 7 (93%) | 7 (94%) | 6 (94%) | 6 (94%)
7 | 7 (94%) | 7 (94%) | 7 (93%) | 7 (95%)
8 | 7 (95%) | 7 (93%) | 6 (91%) | 7 (93%)
9 | 7 (94%) | 7 (92%) | 7 (92%) | 7 (91%)
10 | 7 (95%) | 7 (95%) | 6 (90%) | 7 (94%)
11 | 6 (94%) | 6 (95%) | 6 (92%) | 5 (90%)
12 | 6 (90%) | 7 (97%) | 6 (90%) | 7 (95%)
13 | 7 (92%) | 6 (91%) | 7 (94%) | 7 (94%)
14 | 7 (93%) | 6 (93%) | 7 (98%) | 6 (90%)
Explained variance

## Slide 21: Discussion
Mean absolute value had an significant effect of restriction
Other features showed no clear trend
Only 1 shared control signal
  Structure of EMG from affected limb differs from unaffected
  Many control signals required to explain the variance
      More channels
      Targeted electrode placement

## Slide 22: Conclusion
Mean absolute value is the most important feature
Hand should be restricted
Please share your ideas!

## Slide 24: Formulas
CPA = Cos(signal1,signal2)
NDP = dot(signal1, signal2)/(norm(signal1) * norm(signal2))