## Slide 1: Quantum Tunneling Cantilever Deflection Metrology
A Novel Metrology for Scanning Probe Microscopy
and Other Cantilever Based Devices
 | Dr Marek T. Michalewicz Quantum Precision Instruments Asia Private Limited, Singapore

## Slide 2
Atomic Force Microscopy & cantilever based devices:
first built ~ 20 years ago at IBM
total number of units ~ 25,000 (2008)
total market ~ US$ 780 M (2008)
total cantilever market ~ US$ 93 M (2008)
What is AFM and who needs one?
Click the image

## Slide 3
Optical Metrology

## Slide 4
Remove Optical Metrology
Notes: SOLUTION:
Replace EXTERNAL Optical Metrology with
Quantum Tunneling Metrology INCORPORATED into cantilever structure

## Slide 5
Pain points: | Quantum-Pi solution:
size (limited by light spot size) | no spot, no size limitation
Problem
Solution
Notes: the field is dominated by optical metrology with following limitations:
Problems people would pay to solve:
Optics:
• Size limitations of cantilevers: You can’t make the cantilevers smaller due to:
• Size of reflective spot must be big enough to reflect laser beam
• Optical diffraction (same as above?)
• Limited use in challenging environments such as liquids, vacuum, turbid solutions / smoky atmospheres and low temperatures:
• Hard to fit optical metrology assembly into a vacuum chamber that has limited volume
• Hard to calibrate in liquids due to different refractive indexes
• Light scattering in turbid solutions and smoky environments (example: biological applications)
• Requires precise control of environmental factors such as temperature and humidity
• For measurements at temperatures below 1 K, the cantilever is heated by light absorption
• Limited sensitivity of cantilevers. For nanotribology it would be desirable to have low spring constants and thin membranes as this will ensure that the cantilevers are not too stiff.
• Precision optical metrology requires thick substrates and stiff multilayer mirror stacks to maximize reflection.
• Torsion measurement requires elaborate optics like quadrant detectors. Torsion is useful for detecting friction when moving the cantilever sideways while being in contact with the surface to be measured.
• Unable to meet certain requirements for frequency:
• Cantilevers with frequency response in 0-1kHz range and deflection 1pm/(Hz) are not available and are acutely needed (why and why?)
• Not well suited for monolithic integration. (Why is it desirable?)
• ((Bio-)Chemical sensors and millipede systems) Not well suited for parallel and multiplexed detection:
• Difficulties in laser alignment and power management
Piezoresistive:
• ((Bio-)Chemical sensors) As piezoresistors cover a large length of the cantilever and high doping levels are required, stress measurement not localized. This leads too:
• Thermal and electric noise as well as conductance fluctuation noise
• Nonlinearity in piezo-response
• Cycle fatigue
• Low sensitivity: Cantilever bending of more than 50 nm is required to detect measurable and reproducible piezoresistance
Capacitance:
• ((Bio-)Chemical sensors) Interference with the variations in the dielectric constant of fluidic media

## Slide 6
Pain points: | Quantum-Pi solution:
size of optics (in UHV chambers) | metrology integrated within cantilever
Problem
Solution
Notes: the field is dominated by optical metrology with following limitations:
Problems people would pay to solve:
Optics:
• Size limitations of cantilevers: You can’t make the cantilevers smaller due to:
• Size of reflective spot must be big enough to reflect laser beam
• Optical diffraction (same as above?)
• Limited use in challenging environments such as liquids, vacuum, turbid solutions / smoky atmospheres and low temperatures:
• Hard to fit optical metrology assembly into a vacuum chamber that has limited volume
• Hard to calibrate in liquids due to different refractive indexes
• Light scattering in turbid solutions and smoky environments (example: biological applications)
• Requires precise control of environmental factors such as temperature and humidity
• For measurements at temperatures below 1 K, the cantilever is heated by light absorption
• Limited sensitivity of cantilevers. For nanotribology it would be desirable to have low spring constants and thin membranes as this will ensure that the cantilevers are not too stiff.
• Precision optical metrology requires thick substrates and stiff multilayer mirror stacks to maximize reflection.
• Torsion measurement requires elaborate optics like quadrant detectors. Torsion is useful for detecting friction when moving the cantilever sideways while being in contact with the surface to be measured.
• Unable to meet certain requirements for frequency:
• Cantilevers with frequency response in 0-1kHz range and deflection 1pm/(Hz) are not available and are acutely needed (why and why?)
• Not well suited for monolithic integration. (Why is it desirable?)
• ((Bio-)Chemical sensors and millipede systems) Not well suited for parallel and multiplexed detection:
• Difficulties in laser alignment and power management
Piezoresistive:
• ((Bio-)Chemical sensors) As piezoresistors cover a large length of the cantilever and high doping levels are required, stress measurement not localized. This leads too:
• Thermal and electric noise as well as conductance fluctuation noise
• Nonlinearity in piezo-response
• Cycle fatigue
• Low sensitivity: Cantilever bending of more than 50 nm is required to detect measurable and reproducible piezoresistance
Capacitance:
• ((Bio-)Chemical sensors) Interference with the variations in the dielectric constant of fluidic media

## Slide 7
Pain points: | Quantum-Pi solution:
difficult calibration | easy calibration (software)
Problem
Solution
Notes: the field is dominated by optical metrology with following limitations:
Problems people would pay to solve:
Optics:
• Size limitations of cantilevers: You can’t make the cantilevers smaller due to:
• Size of reflective spot must be big enough to reflect laser beam
• Optical diffraction (same as above?)
• Limited use in challenging environments such as liquids, vacuum, turbid solutions / smoky atmospheres and low temperatures:
• Hard to fit optical metrology assembly into a vacuum chamber that has limited volume
• Hard to calibrate in liquids due to different refractive indexes
• Light scattering in turbid solutions and smoky environments (example: biological applications)
• Requires precise control of environmental factors such as temperature and humidity
• For measurements at temperatures below 1 K, the cantilever is heated by light absorption
• Limited sensitivity of cantilevers. For nanotribology it would be desirable to have low spring constants and thin membranes as this will ensure that the cantilevers are not too stiff.
• Precision optical metrology requires thick substrates and stiff multilayer mirror stacks to maximize reflection.
• Torsion measurement requires elaborate optics like quadrant detectors. Torsion is useful for detecting friction when moving the cantilever sideways while being in contact with the surface to be measured.
• Unable to meet certain requirements for frequency:
• Cantilevers with frequency response in 0-1kHz range and deflection 1pm/(Hz) are not available and are acutely needed (why and why?)
• Not well suited for monolithic integration. (Why is it desirable?)
• ((Bio-)Chemical sensors and millipede systems) Not well suited for parallel and multiplexed detection:
• Difficulties in laser alignment and power management
Piezoresistive:
• ((Bio-)Chemical sensors) As piezoresistors cover a large length of the cantilever and high doping levels are required, stress measurement not localized. This leads too:
• Thermal and electric noise as well as conductance fluctuation noise
• Nonlinearity in piezo-response
• Cycle fatigue
• Low sensitivity: Cantilever bending of more than 50 nm is required to detect measurable and reproducible piezoresistance
Capacitance:
• ((Bio-)Chemical sensors) Interference with the variations in the dielectric constant of fluidic media

## Slide 8
Pain points: | Quantum-Pi solution:
difficulty with liquid media (unknown refractive index) | no optics, no relevance of refractive index
Problem
Solution
Notes: the field is dominated by optical metrology with following limitations:
Problems people would pay to solve:
Optics:
• Size limitations of cantilevers: You can’t make the cantilevers smaller due to:
• Size of reflective spot must be big enough to reflect laser beam
• Optical diffraction (same as above?)
• Limited use in challenging environments such as liquids, vacuum, turbid solutions / smoky atmospheres and low temperatures:
• Hard to fit optical metrology assembly into a vacuum chamber that has limited volume
• Hard to calibrate in liquids due to different refractive indexes
• Light scattering in turbid solutions and smoky environments (example: biological applications)
• Requires precise control of environmental factors such as temperature and humidity
• For measurements at temperatures below 1 K, the cantilever is heated by light absorption
• Limited sensitivity of cantilevers. For nanotribology it would be desirable to have low spring constants and thin membranes as this will ensure that the cantilevers are not too stiff.
• Precision optical metrology requires thick substrates and stiff multilayer mirror stacks to maximize reflection.
• Torsion measurement requires elaborate optics like quadrant detectors. Torsion is useful for detecting friction when moving the cantilever sideways while being in contact with the surface to be measured.
• Unable to meet certain requirements for frequency:
• Cantilevers with frequency response in 0-1kHz range and deflection 1pm/(Hz) are not available and are acutely needed (why and why?)
• Not well suited for monolithic integration. (Why is it desirable?)
• ((Bio-)Chemical sensors and millipede systems) Not well suited for parallel and multiplexed detection:
• Difficulties in laser alignment and power management
Piezoresistive:
• ((Bio-)Chemical sensors) As piezoresistors cover a large length of the cantilever and high doping levels are required, stress measurement not localized. This leads too:
• Thermal and electric noise as well as conductance fluctuation noise
• Nonlinearity in piezo-response
• Cycle fatigue
• Low sensitivity: Cantilever bending of more than 50 nm is required to detect measurable and reproducible piezoresistance
Capacitance:
• ((Bio-)Chemical sensors) Interference with the variations in the dielectric constant of fluidic media

## Slide 9
Pain points: | Quantum-Pi solution:
light scattering in turbid media (life science applications) | no optics, problem solved
Problem
Solution
Notes: the field is dominated by optical metrology with following limitations:
Problems people would pay to solve:
Optics:
• Size limitations of cantilevers: You can’t make the cantilevers smaller due to:
• Size of reflective spot must be big enough to reflect laser beam
• Optical diffraction (same as above?)
• Limited use in challenging environments such as liquids, vacuum, turbid solutions / smoky atmospheres and low temperatures:
• Hard to fit optical metrology assembly into a vacuum chamber that has limited volume
• Hard to calibrate in liquids due to different refractive indexes
• Light scattering in turbid solutions and smoky environments (example: biological applications)
• Requires precise control of environmental factors such as temperature and humidity
• For measurements at temperatures below 1 K, the cantilever is heated by light absorption
• Limited sensitivity of cantilevers. For nanotribology it would be desirable to have low spring constants and thin membranes as this will ensure that the cantilevers are not too stiff.
• Precision optical metrology requires thick substrates and stiff multilayer mirror stacks to maximize reflection.
• Torsion measurement requires elaborate optics like quadrant detectors. Torsion is useful for detecting friction when moving the cantilever sideways while being in contact with the surface to be measured.
• Unable to meet certain requirements for frequency:
• Cantilevers with frequency response in 0-1kHz range and deflection 1pm/(Hz) are not available and are acutely needed (why and why?)
• Not well suited for monolithic integration. (Why is it desirable?)
• ((Bio-)Chemical sensors and millipede systems) Not well suited for parallel and multiplexed detection:
• Difficulties in laser alignment and power management
Piezoresistive:
• ((Bio-)Chemical sensors) As piezoresistors cover a large length of the cantilever and high doping levels are required, stress measurement not localized. This leads too:
• Thermal and electric noise as well as conductance fluctuation noise
• Nonlinearity in piezo-response
• Cycle fatigue
• Low sensitivity: Cantilever bending of more than 50 nm is required to detect measurable and reproducible piezoresistance
Capacitance:
• ((Bio-)Chemical sensors) Interference with the variations in the dielectric constant of fluidic media

## Slide 10
Pain points: | Quantum-Pi solution:
heating of cantilever at very low temperatures | no light beam to heat cantilever
Problem
Solution
Notes: the field is dominated by optical metrology with following limitations:
Problems people would pay to solve:
Optics:
• Size limitations of cantilevers: You can’t make the cantilevers smaller due to:
• Size of reflective spot must be big enough to reflect laser beam
• Optical diffraction (same as above?)
• Limited use in challenging environments such as liquids, vacuum, turbid solutions / smoky atmospheres and low temperatures:
• Hard to fit optical metrology assembly into a vacuum chamber that has limited volume
• Hard to calibrate in liquids due to different refractive indexes
• Light scattering in turbid solutions and smoky environments (example: biological applications)
• Requires precise control of environmental factors such as temperature and humidity
• For measurements at temperatures below 1 K, the cantilever is heated by light absorption
• Limited sensitivity of cantilevers. For nanotribology it would be desirable to have low spring constants and thin membranes as this will ensure that the cantilevers are not too stiff.
• Precision optical metrology requires thick substrates and stiff multilayer mirror stacks to maximize reflection.
• Torsion measurement requires elaborate optics like quadrant detectors. Torsion is useful for detecting friction when moving the cantilever sideways while being in contact with the surface to be measured.
• Unable to meet certain requirements for frequency:
• Cantilevers with frequency response in 0-1kHz range and deflection 1pm/(Hz) are not available and are acutely needed (why and why?)
• Not well suited for monolithic integration. (Why is it desirable?)
• ((Bio-)Chemical sensors and millipede systems) Not well suited for parallel and multiplexed detection:
• Difficulties in laser alignment and power management
Piezoresistive:
• ((Bio-)Chemical sensors) As piezoresistors cover a large length of the cantilever and high doping levels are required, stress measurement not localized. This leads too:
• Thermal and electric noise as well as conductance fluctuation noise
• Nonlinearity in piezo-response
• Cycle fatigue
• Low sensitivity: Cantilever bending of more than 50 nm is required to detect measurable and reproducible piezoresistance
Capacitance:
• ((Bio-)Chemical sensors) Interference with the variations in the dielectric constant of fluidic media

## Slide 11
Pain points: | Quantum-Pi solution:
unable to meet deflection/frequency requirements | very fast signal, solutions possible
Problem
Solution
Notes: the field is dominated by optical metrology with following limitations:
Problems people would pay to solve:
Optics:
• Size limitations of cantilevers: You can’t make the cantilevers smaller due to:
• Size of reflective spot must be big enough to reflect laser beam
• Optical diffraction (same as above?)
• Limited use in challenging environments such as liquids, vacuum, turbid solutions / smoky atmospheres and low temperatures:
• Hard to fit optical metrology assembly into a vacuum chamber that has limited volume
• Hard to calibrate in liquids due to different refractive indexes
• Light scattering in turbid solutions and smoky environments (example: biological applications)
• Requires precise control of environmental factors such as temperature and humidity
• For measurements at temperatures below 1 K, the cantilever is heated by light absorption
• Limited sensitivity of cantilevers. For nanotribology it would be desirable to have low spring constants and thin membranes as this will ensure that the cantilevers are not too stiff.
• Precision optical metrology requires thick substrates and stiff multilayer mirror stacks to maximize reflection.
• Torsion measurement requires elaborate optics like quadrant detectors. Torsion is useful for detecting friction when moving the cantilever sideways while being in contact with the surface to be measured.
• Unable to meet certain requirements for frequency:
• Cantilevers with frequency response in 0-1kHz range and deflection 1pm/(Hz) are not available and are acutely needed (why and why?)
• Not well suited for monolithic integration. (Why is it desirable?)
• ((Bio-)Chemical sensors and millipede systems) Not well suited for parallel and multiplexed detection:
• Difficulties in laser alignment and power management
Piezoresistive:
• ((Bio-)Chemical sensors) As piezoresistors cover a large length of the cantilever and high doping levels are required, stress measurement not localized. This leads too:
• Thermal and electric noise as well as conductance fluctuation noise
• Nonlinearity in piezo-response
• Cycle fatigue
• Low sensitivity: Cantilever bending of more than 50 nm is required to detect measurable and reproducible piezoresistance
Capacitance:
• ((Bio-)Chemical sensors) Interference with the variations in the dielectric constant of fluidic media

## Slide 12
Pain points: | Quantum-Pi solution:
difficult to measure cantilever torsion | torsion will be measured
Problem
Solution
Notes: the field is dominated by optical metrology with following limitations:
Problems people would pay to solve:
Optics:
• Size limitations of cantilevers: You can’t make the cantilevers smaller due to:
• Size of reflective spot must be big enough to reflect laser beam
• Optical diffraction (same as above?)
• Limited use in challenging environments such as liquids, vacuum, turbid solutions / smoky atmospheres and low temperatures:
• Hard to fit optical metrology assembly into a vacuum chamber that has limited volume
• Hard to calibrate in liquids due to different refractive indexes
• Light scattering in turbid solutions and smoky environments (example: biological applications)
• Requires precise control of environmental factors such as temperature and humidity
• For measurements at temperatures below 1 K, the cantilever is heated by light absorption
• Limited sensitivity of cantilevers. For nanotribology it would be desirable to have low spring constants and thin membranes as this will ensure that the cantilevers are not too stiff.
• Precision optical metrology requires thick substrates and stiff multilayer mirror stacks to maximize reflection.
• Torsion measurement requires elaborate optics like quadrant detectors. Torsion is useful for detecting friction when moving the cantilever sideways while being in contact with the surface to be measured.
• Unable to meet certain requirements for frequency:
• Cantilevers with frequency response in 0-1kHz range and deflection 1pm/(Hz) are not available and are acutely needed (why and why?)
• Not well suited for monolithic integration. (Why is it desirable?)
• ((Bio-)Chemical sensors and millipede systems) Not well suited for parallel and multiplexed detection:
• Difficulties in laser alignment and power management
Piezoresistive:
• ((Bio-)Chemical sensors) As piezoresistors cover a large length of the cantilever and high doping levels are required, stress measurement not localized. This leads too:
• Thermal and electric noise as well as conductance fluctuation noise
• Nonlinearity in piezo-response
• Cycle fatigue
• Low sensitivity: Cantilever bending of more than 50 nm is required to detect measurable and reproducible piezoresistance
Capacitance:
• ((Bio-)Chemical sensors) Interference with the variations in the dielectric constant of fluidic media

## Slide 13
Pain points: | Quantum-Pi solution:
size (limited by light spot size) | no size limitation
size of optics (in UHV chambers) | metrology integrated within cantilever
difficult calibration | easy calibration (software)
difficulty with liquid media (unknown refractive index) | no optics, no relevance of refractive index
light scattering in turbid media (life science applications) | no optics, problem solved
heating of cantilever at very low temperatures | no light beam to heat cantilever
unable to meet deflection/frequency requirements | very fast signal, solutions possible
difficult to measure cantilever torsion | torsion will be measured
Problem
Solution
Notes: the field is dominated by optical metrology with following limitations:
Problems people would pay to solve:
Optics:
• Size limitations of cantilevers: You can’t make the cantilevers smaller due to:
• Size of reflective spot must be big enough to reflect laser beam
• Optical diffraction (same as above?)
• Limited use in challenging environments such as liquids, vacuum, turbid solutions / smoky atmospheres and low temperatures:
• Hard to fit optical metrology assembly into a vacuum chamber that has limited volume
• Hard to calibrate in liquids due to different refractive indexes
• Light scattering in turbid solutions and smoky environments (example: biological applications)
• Requires precise control of environmental factors such as temperature and humidity
• For measurements at temperatures below 1 K, the cantilever is heated by light absorption
• Limited sensitivity of cantilevers. For nanotribology it would be desirable to have low spring constants and thin membranes as this will ensure that the cantilevers are not too stiff.
• Precision optical metrology requires thick substrates and stiff multilayer mirror stacks to maximize reflection.
• Torsion measurement requires elaborate optics like quadrant detectors. Torsion is useful for detecting friction when moving the cantilever sideways while being in contact with the surface to be measured.
• Unable to meet certain requirements for frequency:
• Cantilevers with frequency response in 0-1kHz range and deflection 1pm/(Hz) are not available and are acutely needed (why and why?)
• Not well suited for monolithic integration. (Why is it desirable?)
• ((Bio-)Chemical sensors and millipede systems) Not well suited for parallel and multiplexed detection:
• Difficulties in laser alignment and power management
Piezoresistive:
• ((Bio-)Chemical sensors) As piezoresistors cover a large length of the cantilever and high doping levels are required, stress measurement not localized. This leads too:
• Thermal and electric noise as well as conductance fluctuation noise
• Nonlinearity in piezo-response
• Cycle fatigue
• Low sensitivity: Cantilever bending of more than 50 nm is required to detect measurable and reproducible piezoresistance
Capacitance:
• ((Bio-)Chemical sensors) Interference with the variations in the dielectric constant of fluidic media

## Slide 14
Quantum-Pi cantilever: how it works
Notes: The cantilever is made up of alternating conducting and isolating nano-layers. A quantum tunnelling current flows from the end of the cantilever across a narrow gap (a few tens of nanometers) to corresponding layers that are part of the substrate structure. If the cantilever bends ever so slightly, this will change the alignment of the layers which again changes the quantum tunnelling current. This way one can measure the deflection of the cantilever by measuring the change in the quantum tunnelling current.

## Slide 15
Proven Fabrication Processes
Institute of Microelectronics have confirmed all process steps.
The detailed process has been documented in IME-Quantum-Pi project plan.
Quantum-Pi POC is to build functional devices using these established processes.
Greatest challenges:
Cutting the quantum tunneling gap. But it’s been done!
Transfer of knowledge to Singapore from Cornell U. USA, Prof. H. Craighead
H. Craighead et. al. Cornell University
Focussed Ion Beam milling:
example from University of Wales
Notes: NanoNow, Issue 1,

## Slide 16
Cleland & Roukes, UCSB & CalTech
Proven Fabrication Processes

## Slide 17
Two patents:
"Measuring Using Tunneling Current Between Elongate Conductors" (PCT/AU99/00733; US 09/786,641) has been granted in the USA, Russia, China, Israel, Singapore, Australia, Canada and South Africa. It is pending in 22 other countries: Europe (20 countries), Japan and Brazil.
“Sensor Device and Method”, PCT/SG2007/000278 for AFM cantilever metrology.
Quantum-Pi plans to:
file additional divisional patent applications,
file new patents,
file fencing patents.
Patent Protection: Defensibility

## Slide 18
Business Model
38 AFM and 25 AFM cantilever manufacturers
customers NOT competitors

## Slide 19
Summary
Problem |  |  |  |  | 
AFM users will pay for cantilevers that provide easier calibration, smaller size, better dynamic range without complex optics. Our customers will be AFM and AFM cantilever manufacturers, who will sell onwards to AFM users. |  |  |  |  | 
Proposed Solution |  |  |  |  | 
The Quantum-Pi solution is a quantum tunneling based metrology integrated into a cantilever. All fabrication steps are standard CMOS fab processes, and only one key challenge exists in forming a very narrow tunneling gap. |  |  |  | IP Situation - Strategy Two patents. One granted, one PCT filed. Immediate follow-on with divisional and fencing patents. | 
Business Model |  |  |  |  | 
Market size over US$ 200 M. We will sell our disruptive technology solution through existing 38 AFM and 25 AFM cantilever manufacturers. |  |  |  |  | Quantum-Pi’s technology disruption is the world’s first feasible replacement to cantilever optics metrology. Revenue will be from licensing and device sales.
Notes: NEXT Step: pilot production through A*STAR IME R&D Foundry !!!!!!!!!!!!