## Slide 1: OnSSET teaching material
Babak Khavari, Andreas Sahlberg, Alexandros Korkovelos, Dimitris Mentis, Nandi Moksnes

## Slide 2
Basic GIS concepts
Ellipsoid, Datum & Geographic Coordinate System
Projection is the systematic transformation of the latitude and longitude of a location into a pair of two dimensional coordinates or else the position of this location on a plane (flat) surface
Coordinate Reference System (CRS) defines how the map is related to real world places
Notes: The earth is in the form of a sphere and what a map projection does is that it tries to vizualise this spherical area onto a flat surface. In other words it is used to turn 3 dimensional objects into 2 dimensional representations. A coordinate system then defines how your 2D representaion is related to real places on earth-
CRS (SRS) defines how well the 2D map is related to the 3D world

## Slide 3
Basic GIS concepts
Ellipsoid, Datum & Geographic Coordinate System
There is always distortion
  Area
  Scale
  Direction
  Shape
Map projections
  Cylindrical projections
  Conical projections
  Planar projections
WGS84
World Mercator

## Slide 4
Basic GIS concepts
Projected Coordinate System & Spatial Reference
WGS 1984 World Mercator
World Equidistant Cylindrical (Sphere)
Asia North Lambert Conformal Conic

## Slide 5: Points
Single vertex
Described by coordinates and attributes
What is considered a point is subjective
Applies to features:
    Without area
    Too small to be displayed at current scale

## Slide 6: Lines
Vertices are connected
Includes describing attributes

## Slide 7: Polygon
Enclosed areas
First and last vertex has the same coordinates
Includes describing attributes

## Slide 8: Raster data
Matrix of cells
Represents data over large areas
Thematic, Continuous and Imagery
Wide range of use (base maps, surface maps, thematic maps etc.)
Matrix
Cell

## Slide 9: Cell size – Spatial resolution
Small cell size Large cell size
Higher spatial resolution
Higher detail and accuracy
Faster processing
Faster display
Smaller file size
Slower processing
Slower display
Larger file size
Might miss details
Lower accuracy
Lower spatial resoulation

## Slide 10: Continuous vs Thematic
7 | 7 | 14 | 14 | 5 | 5
1 | 3 | 13 | 13 | 1 | 3
4 | 3 | 13 | 13 | 13 | 2
3 | 3 | 3 | 13 | 13 | 3
1 | 1 | 3 | 13 | 14 | 14
1 | 1 | 2 | 4 | 14 | 14
4.5 | 13.5 | 3.5
3.3 | 10.5 | 7.8
1 | 5.5 | 14
Average

## Slide 11: Continuous vs Thematic
7 | 13 | 5
3 | 13 | 13
1 | 13 | 0
Mode
7 | 7 | 0 | 0 | 5 | 5
1 | 3 | 13 | 13 | 1 | 3
4 | 3 | 13 | 13 | 13 | 2
3 | 3 | 3 | 13 | 13 | 3
1 | 0 | 3 | 13 | 0 | 0
1 | 1 | 2 | 4 | 0 | 0
e.g.
0 = water
1 = forest
2 = grass
3 = urban areas

## Slide 12
# | Dataset | Type
1 | Population density & distribution | Raster
2 | Administrative boundaries | Raster
3 | Existing grid network | Line shapefile
4 | Substations | Point shapefile
5 | Power plants | Point shapefile
6 | Mines & Queries | Point shapefile
7 | Roads | Line shapefile
8 | Planned grid network | Line shapefile
Step 1. Acquire the necessary GIS data for the area of interest
9 | Nighttime lights | Raster
10 | GHI | Raster
11 | Wind speed | Raster
12 | Hydro power potential | Point shapefile
13 | Travel time | Raster
14 | Elevation Map | Raster
15 | Slope | Raster
16 | Land Cover | Raster
# | Dataset | Type
GIS data requirements may vary depending on the objective of the electrification study

## Slide 13
Step 2. Use GIS techniques to extract useful information for the analysis
(the data are transferred to excel/csv)
Population (2010) | Country
0 | Kenya
388 | Kenya
2,136 | Kenya
2,139 | Kenya
280,088 | Kenya
543,581 | Kenya
X | Y
2370166 | 228283
1907255 | -441856
2953836 | -904402
3155102 | -451877
2692191 | -833762
1655673 | -582265
Grid cell Coordinates
Distance existing (km) | Distance planned (km)
243 | 228
44 | 44
141 | 112
73 | 73
133 | 133
1 | 403
Distance from Existing & Planned Transmission Network
Distance from Roads (km)
11
9
4
20
5
451
GHI (kWh/m2/year)
1822
1827
2006
1814
1912
1750
Travel hours (h)
1
3
4
15
2
0
Grid cell distance from the nearest town
Wind resource availability
Wind velocity (m/s)
4.3
3.9
7.1
4.2
6.5
7.8

## Slide 14
Friday, May 10, 2019
Access Level | Tier 1 | Tier 2 | Tier 3 | Tier 4 | Tier 5
Indicative appliances powered | Task lighting + phone charging or radio | General lighting + fan + television | Tier 2 + medium power appliances (i.e. general food processing, refrigeration) | Tier 3 + Medium or continuous appliances (i.e. water heating, ironing, water pumping, rice cooking, micro wave) | Tier 4 + High power and continuous appliances (i.e. air conditioning)
Consumption per capita & year (kWh) | 8 | 44 | 160 | 423 | 598
Consumption per urban household/year (based on average household size: 5) | 40 | 220 | 800 | 2,115 | 2,990
Adapted from Global Tracking Framework, 2015
What should be the electricity consumption level per household?
Step 3b. Enter country-specific data (Energy Access Target)

## Slide 15: The seven step methodology
Parameter | Metric | Base Year Value | Value 2030
Population, total | Million Persons | 42.5 | 65.4
Urban population | Percent of total population | 25 % | 32%
Rural population | Percent of total population | 75% | 68%
Electricity access, Total | Percent of total population | 31% | 100%
Electricity access, Urban | Percent of urban population | 80% | 100%
Electricity access, Rural | Percent of rural population | 15% | 100%
Household size, Urban | People per household | 5 | 4
Household size, Rural | People per household | 7 | 6
Step 3a. Collect country-specific data (Social)
Source: Sahlberg et al. 2021
Notes: Next, we also need a number of non geospatial data. First of all, we need to collect demographic parameters for the country or the region that we are studying.
1. We need to know what the total population is, according to the latest population estimate or the latest population census. We collect that information for the start year of our analysis, which can be e.g. 2020.
The population data also needs to projected on how it will grow until the end of our analysis, in this case, it could be 2030.
2. Apart from the population we need also need to know how many percent of the population lives in urban locations in the start year as well as in the end year. This will give us both the urban and rural share.
3. We also need to know what is the average household size in urban areas and in rural areas on average. This dataset is used to calculate the approximate number of buildings in the village.
Finally a key data set is, how many people have access to electricity today? In this example here, we have 31 percent, meaning 69 percent don't have access to electricity today In addition we break it down further to how much of the rural and urban population has access to electricity.
The OnSSET tool main objective is to electrify un-electrified population and in the example here, we aim for universal access to electricity by 2030 by setting all of the electricity access rates targets at 100 percent.

## Slide 16
Parameter | Capital cost $/km
HV lines (>69 kV) | 53,9006
MV lines (>33 kV) | 9,000 3
LV lines (220 V) | 5,000 3
HV/LV transformer | 5 000 $ per unit 3
Transmission loses | 18%
Connection cost per HH | $125
Cost of producing electricity | 0.05
Values adopted by:
IRENA, 2012
ESMAP - World Bank, 2015
Ministry of Energy Kenya, 2015
International Energy Agency, 2017
Latest updated in September 2017
Step 3c. Enter country-specific data (Technology specifications & Costs)
Plant type | Typical Plant capacity (kW) | Investment cost ($/kW) | O&M costs (% of investment cost/year) | Fuel cost $/liter (future) | Efficiency | Capacity factor | Life (years)
Diesel Genset Mini Grid | 100 | 721 | 10% | 0.50 (0.70) | 33% | 0.7 | 15
Small Hydro Mini Grid | 1000 | 5,000 | 2% | - | - | 0.7 | 30
Solar PV Mini Grid | 100 | 3,200 | 1.5% | - | - | Obtained for each grid point depending on solar availability | 20
Wind Turbines Mini Grid | 100 | 3,000 | 2% | - | - | Obtained for each grid point depending on wind availability | 20
Diesel Genset Stand Alone | 1 | 938 | 10% | 0.50 (0.70) | 28% | 0.7 | 10
Solar PV Stand Alone | 0.4 | 5,500 | 1.2% | - | - | Obtained for each grid point depending on solar availability | 15

## Slide 17
Step 4. Data Processing, Projection and Calibration
Friday, May 10, 2019
Identify current Electrification status:
Night Lights index: >0.05
Population: >50 people
Distance from grid: <5 km

## Slide 18: Example of stand-alone PV cost
The cost per Solar Home System (SHS) multiplied by the number of households
Example: If 1 SHS costs 200 USD, the total investment cost will be: 6 x 20 = 1200 USD
The cost per SHS depends on the size of the system
Prepare the required data, processing and calibration
Source: Sahlberg et al. 2021
Notes: Here we have an example looking at stand alone systems. That means that every customer will use their own system. If we have a small village where we are looking at the cost of supplying electricity by solar home systems we need to find out which type of solar system is needed to meet the demand in the household and how many households are in the village. The cost of the system will simply be the solar home systems for each of the household. Of course, if we have a high demand, we need a large solar home system for each household, if we have a lower demand, we can use a smaller solar system.

## Slide 19: Example of mini-grid costs
Cost of generation system
  PV panels
  Batteries
  Balance of System
  …
The cost of the distribution system
  Low-Voltage (LV) lines
  Medium-Voltage (MV) lines
  Cost per connection per household…
Example: If the distribution grid requires 2 km of LV lines and the cost per LV lines is 5000 USD/km, the total cost for LV lines in the settlement is 10,000 USD
Prepare the required data, processing and calibration
Source: Sahlberg et al. 2021
Notes: If you look at a mini grid, we have a slightly different design. Instead of providing solar panels for every single household we install one larger generation site. The mini-grid could be powered by diesel, hydro wind or a combination of these three sources. Depending on the size of the village, economy of scale can justify the larger investment. If we install renewable resources, they are usually intermittent which then needs to be supported by batteries. But what sets the mini-grids apart from the standalone costs are that we also need to build a distribution network. We need to get the electricity from where it is generated to each household. In the standalone example, every household had their own generation, so there was no need for a distribution network. But here, the generation source is not directly at the customer, so we need a network to distribute electricity to the households. The area of the settlement affects the demand for distribution network. The model estimates how much lower voltage lines are needed to connect all of the customers and if a medium voltage line is required. In addition there is a connection cost per household. None of there additional infrastructure costs are part of the standalone costs.

## Slide 20
Step 5. Calculate technology costs for every settlement in the country
Settlements people) | MG Hydro | MG PV | SA PV | MG Diesel | SA Diesel | MG Wind
11000 | 99.00 | 0.16 | 0.33 | 27.49 | 0.40 | 99.00
500 | 99.00 | 99.00 | 0.34 | 33.87 | 0.39 | 99.00
1300 | 99.00 | 99.00 | 0.33 | 12.12 | 0.31 | 99.00
23000 | 99.00 | 0.22 | 0.35 | 22.25 | 0.42 | 99.00
25000 | 0.16 | 21.53 | 0.34 | 22.94 | 0.46 | 99.00
680 | 99.00 | 99.00 | 0.35 | 27.23 | 0.47 | 99.00
15000 | 99.00 | 46.68 | 0.34 | 50.02 | 0.67 | 0.13
LCoEs achieved per technology per settlement
99 → Not available

## Slide 21
The cost of grid-connection depends on:
  The distribution network
  The new MV line required to connect the settlement
  The cost of electricity generated (or imported) for the grid
Example: If the new MV line is 3 km and the cost of MV lines is 9000 USD/km, the total cost of the new line is 27,000 USD
Existing/planned HV line
New MV line
Example of grid connection cost
OnSSET calculations and summaries
Source: Sahlberg et al. 2021
Notes: This is called the electrification algorithm which compares grid extension to the least cost of grid technology. When we look at the cost of connection to the centralized grid we follow a similar approach as the previous technologies to calculate the LCOE. However, there are some additions. We need to know where the existing infrastructure is to calculate what the cost of connecting a new settlement to it.
When we extend a medium voltage line from the existing grid infrastructure, we need to define how long it has to be. Depending on how far away the settlement is from the existing infrastructure we can calculate the cost per km of this medium voltage lines. Similar to the mini-grid network, we need to have a distribution network in the settlement using low voltage lines and potentially medium voltage line within a settlement, depending on its size and demand levels.
Finally, we also need to include the cost of the electricity that is produced by the national power plants. In summary, we have the extension of the grid to connect the settlement, the cost of building the distribution network and the cost of buying electricity from the central grid. All of these costs combined are the cost for grid to a settlement. Again, we follow a similar approach where we calculate investment costs for extension and distribution network where we have the operation and maintenance costs of all of these technologies. One important aspect here is that we use the cost of generated electricity as a fuel cost as we need to buy that from the grid connected power plants.

## Slide 22
Location A Off-grid = 0.30 USD/kWh
Location B Off-grid = 0.25 USD/kWh
Location C Off-grid = 0.30 USD/kWh
Grid-extension = 0.40 USD/kWh Too expensive
Max MV line distance: 50 km
Grid-extension with MV lines
Grid-extension = 0.25 USD/kWh
Grid-extension = 0.20 USD/kWh
Grid-extension = 0.20 USD/kWh

## Slide 23
Based on the optimal split identify per technology:
New connections by 2030
Additional capacity needed
Investments requirements
Step 7. Results, Summaries an Visualization

## Slide 24
The processes for a GEP Scenario Generator analysis using OnSSET
Collect GIS datasets
Process datasets using QGIS if needed
(QGIS)
Run the plugin to creata a CSV-file with all GIS data
(QGIS)
Import the CSV-file and update variables in the code
(Jupyter Notebook)
Run the code
(Jupyter Notebook)
Use the Results file to create maps in QGIS
Use the summary file to create charts and tables in Excel

## Slide 25
Wednesday, May 22, 2019
Running the model – Scenario Development
Population growth
Grid price
Grid price
Low
Low
Low
High
High
High
Low/Low Scenario
Low/High Scenario
High/Low Scenario
High/High Scenario

## Slide 26
# | Dataset | Type
1 | Population density & distribution | Raster
2 | Administrative boundaries | Raster
3 | Existing grid network | Line shapefile
4 | Substations | Point shapefile
5 | Power plants | Point shapefile
6 | Mines & Queries | Point shapefile
7 | Roads | Line shapefile
8 | Planned grid network | Line shapefile
9 | Nighttime lights | Raster
10 | GHI | Raster
11 | Wind speed | Raster
12 | Hydro power potential | Point shapefile
13 | Travel time | Raster
14 | Elevation Map | Raster
15 | Slope | Raster
16 | Land Cover | Raster
# | Dataset | Type
GIS data requirements may vary depending on the objective of the electrification study
I. GIS based energy-related data

## Slide 27: Calibrating and projecting the population
GIS data is used to find the spatial distribution of population
The population is calibrated to match official statistics in the base year
Further, the population is divided between urban and rural settlements based on population density to match official statistics
Finally the population is projected until the final year of the analysis based on projected urban and rural growth rates
Social inputs | Example: Madagascar
Population in start year (e.g. 2015) | 24.2 million
Population in end year (e.g. 2030) | 36.0 million
Urban share in start year (e.g. 2015) | 35.1 %
Urban share in end year (e.g. 2030) | 44.3 %
Urban household size (people/household) | 3.7
Rural household size (people/household) | 4.4
Electricity access in start year (e.g. 2015) | 15 %

## Slide 28: LCOE example
Consider a small PV system designed to deliver enough electricity to power a few light-bulbs during-night time
System size: 17 W
Investment cost for 17 W system: 130 USD
Annual energy generation: 35 kWh
Operation & Maintenance cost: 2 USD/year
Fuel cost: 0
Discount rate: 10 %
System life: 20 years

## Slide 29: LCOE example – Year 0

## Slide 30: LCOE example – Year 1

## Slide 31: LCOE example – Year 2

## Slide 32: LCOE - Salvage

## Slide 33: LCOE example – Year 15

## Slide 34: LCOE example – Final cost

## Slide 35: LCOE example – Final cost
What happens if we consider another discount rate?
Example 5%:
0.385 USD/kWh

## Slide 36: Load curves
Example load curves adopted from the “Progress Toward Sustainable Energy 2015” report by the World Bank and International Energy Agency
Peak load

## Slide 37: Electricity load assessment

## Slide 38: Power generation system sizing and operating costs

## Slide 39: Calculating LCOE for stand-alone solar PV technologies
Total investment cost is given by multiplying the capacity with the investment cost (USD/kW)
Annual operation and maintenance is given as a percentage of the total investment cost
No fuel cost
Parameter | Unit
Investment cost | 5500 USD/kW
O&M cost | 1.5 % of investment cost/year
Expected technology lifetime | 20 Years

## Slide 40: Calculating LCOE for mini-grid solar PV
Parameter | Unit
Grid cell area | Km2
Households (from population and household size) | -
MV line cost | USD/km
LV line cost | USD/km
O&M of transmission and distribution network | Percent of investment cost/year
Connection cost per household | USD/household
MV line capacity | kV
LV line capacity | kV
LV line max length | Km
Service transformer cost | USD/unit (50 kVA)

## Slide 41: Calculating LCOE for stand-alone diesel – diesel price
Parameter | Example
Generator efficiency | 28 %
Capacity factor | 0.7
Diesel pump price | 1.00 USD/l
Diesel truck volume | 300 Litre
Diesel truck consumption | 14 Litre/km
LHV diesel | 9.94 kWh/l

## Slide 42: Calculating LCOE for mini-grid diesel
Similar to stand-alone diesel, with additional cost for distribution network
Adjusted input parameters to account for economies of scale for larger systems
Parameter | Example
Generator efficiency | 33 %
Capacity factor | 0.7
Diesel pump price | 1.00 USD/l
Diesel truck volume | 15 000 Litre
Diesel truck consumption | 33.7 Litre/km
LHV diesel | 9.94 kWh/l

## Slide 43: Example 1.
Chart: Population per technology
| Grid | Stand-alone PV
2030 | 15622339.2917 | 10404276.7083
Chart: population per technology
| Grid 93% | Stand-alone PV 5% | Mini-grid PV 1% | Mini-grid hydro 1%
2030 | 24169638.2096 | 1695768.279 | 156332.047 | 4877.4644

## Slide 44: Example 2.
Chart: Population per technology
| Grid | Stand-alone PV
2030 | 15622339.2917 | 10404276.7083
Chart: population per technology
| Grid 93% | Stand-alone PV 5% | Mini-grid PV 1% | Mini-grid hydro 1%
2030 | 24169638.2096 | 1695768.279 | 156332.047 | 4877.4644

## Slide 45: Example 1.
Chart: Investment cost per technology
| Grid | Stand-alone PV | Mini-grid PV
 | 1616340635.7355 | 410343290.2375 | 40876051.4237
Total investment cost: 2067559977 USD

## Slide 46: Example 2.
Chart: Investment cost per technology
| Grid | Stand-alone PV | Mini-grid PV
 | 1616.3406 | 410.3433 | 40.8761
Total investment cost: 2.1 billion USD

## Slide 47
The role of GIS modelling
The role of GIS modelling
Notes: On the picture here, you can see different settlements spread out on the map. Those are the light yellow areas. We see some larger areas, which might be a small town or a village. But we also see these more dispersed, smaller settlements, which might be just a couple of households. If we look at a settlement, there are a number of different things that we need to know. First of all, we need to know how many people lived there or how many households or buildings are in this location. And what is the electricity demand in this location? This will affect e.g. the need for a distribution network.
We also want to know about the energy resources that are available. How much is the solar resource in this location during a year? What is the wind resource during the year? And if possible, is there any hydro resource nearby which we could build a hydro mini-grid to produce electricity? In that case, we need to know, first of all, how much hydropower can be generated at this location, but also how far away is this location? Because if we are installing hydro turbine that's not directly at the settlement, we will need a distribution line to connect from the hydro generator to the customers. The longer it is, the more costly. We also want to know information about existing infrastructure. One key information that we need to know is how far away is the existing transmission network?

## Slide 48
Scenario and sensitivity analysis in energy systems modelling
Forecasting, scenarios and backcasting
Source: Adapted from Sahlberg et al. 2018
FUTURE
FUTURE
FUTURE
Forecasting
Scenarios: exploratory and normative
Backcasting
Present
Present
Present
Picture source: Adapted from van Bers et al. 2016, I
Notes: In this mini-lecture we will talk about how we use scenario and sensitivity analysis. In general, we could say that there are three types of scenario types that we can develop where a scenario is a possible future development.
The first set of scenarios we can call forecasting scenarios. Forecasting scenarios try to predict the most likely future developments. These scenarios try and predict different developments of demand, technology costs, fuel prices based on e.g. historical trends and scientific reports.
The second set of scenarios is exploratory or normative scenarios, which means that we try to explore a lot of different alternative futures instead of finding what we think is the most likely development of different variables. As an example, instead of estimating what we think that the oil price will be in the next year we look at a wide range of different developments. Aspects such as: What if the oil price decreases? What if it stays the same? What if it increases with different rates? And how does this affect the results? Instead of trying to find the most likely development we want to explore different developments to find a robust solution that will work well under different developments of these scenarios.
Both of these scenario methods look at different variables and what their results will be in the future.

## Slide 49
Identify geospatial energy related data
Key datasets used in OnSSET
Administrative boundaries
Road network
Nighttime light
Power plants
Mines
Existing Grid Network
Current population
Projected population and Grid Network
Wind power capacity factor
Global Horizontal Irradiance
Mini and small hydropower potential
Spatial cost of Diesel gensets
Source: Mentis et al. 2021
Korkovelos et al., 2019, Mentis et al. 2017
Existing Grid Network
Notes: In this mini-lecture we will look at an example of an electrification analysis, using the OnSSET tool, for all of sub-Saharan Africa. To start with we need to collect all geospatial data sets. First of all, we need to look at the administrative boundaries which delineate the area or the country that we are studying. In this case, we're studying all countries in sub-Saharan Africa. Another important data set is the road network, which indicates how well connected each settlement is. Nighttime lights show the light that's detectable by a satellite that passes over the globe during night time. What does the satellite detect? That there are lights during night time. We can through that assume that there's probably some access to electricity or something that emits this light. We can also look at power plants and mines, the former is the producer of electricity, the second one is a consumer of electricity. On key data set is information about where the existing grid network is, which affects the cost of extending to new settlements (as seen in the picture). This data set is also used to identify which are the currently electrified settlements. Of course, we also need to take into account how the population is distributed, we can see that we have some areas in darker shade here where a lot of people live and we also have brighter areas with much lower population density, which will also affect the choice of technology to provide electricity. And then we also look at the projections of these. How do we expect population to grow in different areas and are there already committed grid network extensions that we should include in our analysis?