## Slide 1: Learning to Diagnose Leading Edge Erosion Degradation on an Airfoil via Aerodynamic Pressure Coefficients
25th May, 2021
WESC2021 "Structural Health Monitoring: Applications and Potential in Wind Energy (I)"
Gregory Duthé1, Imad Abdallah1, Yuriy Marykovskiy1,2, Sarah Barber2, Eleni Chatzi1
1ETH Zürich
2Eastern Switzerland University of Applied Sciences

## Slide 2: Contents
Introduction and Method Overview
Data Pipeline
Model Architecture
Results
Conclusion

## Slide 3: The Aerosense project
Project goal: develop a first ever MEMS-based surface pressure and acoustic smart measurement system that is thin, non-intrusive, robust, modular, low power and self-sustaining, wirelessly transmitting, easy to install and cost-effective for wind turbines.
Use cases:
  Operators: blade surface (and structural?) damage detection, performance optimisation, amplitude modulation detection (increase operating time).
  OEMs: optimisation of aeroacoustic design tools and wind turbine designs, understanding 3D field aerodynamics.
Scope:
  3 years May 2020 – April 2023
  Funding from SNF/Innouisse BRIDGE programme: CHF 2.3 m
Partners:
  Eastern Switzerland University of Applied Sciences (OST)
  ETH Zurich Chair of Structural Mechanics and Monitoring
  ETH Zurich Center for Project-Based Learning
  Octue (UK)
Advisory Board:
  RES, EKZ Renewables, Enercon, GE (LM), Brüel&Kjaer
  Fraunhofer IWES, ECN, DTU, TU Delft, NREL.

## Slide 4: Introduction
Leading edge erosion (LEE):
  Reduces power production
  Increases noise
  Can affect blade structural integrity
Current LEE condition monitoring methods:
  Manual or drone-based inspection
  Vibration based
  SCADA analysis
  → Limited for continuous monitoring, no methods based on aerodynamics
AeroSense project:
  System composed of MEMS-based pressure sensors placed around blade ‘slice’
  Continuous measurement of blade aerodynamics
  → How can we use this to diagnose the extent of leading edge erosion?
Source: Eisenberg, Drew, Steffen Laustsen, and Jason Stege. "Wind turbine blade coating leading edge rain erosion model: Development and validation." Wind Energy 21.10 (2018): 942-951.

## Slide 5: Method overview

## Slide 6: Data pipeline (1/6): Airfoil Geometries
Robust model development:
  Needs to be able to generalize to any wind turbine
  Needs to account for warping during operation
  → Diverse range of airfoil geometries need to be simulated
Simulate many airfoils, but how to choose which ones?
  Avoid biasing the output dataset by manual selection
  Need realistic airfoils, not random shapes
  → Airfoil Shape Variational AutoEncoder

## Slide 7: Data pipeline (2/6): Airfoil Shape VAE
Idea:
  Train generative model on dataset of airfoils
  Sample from latent space to create new airfoils
Variational AutoEncoder (VAE)
  VAEs condition the latent space well for sampling
  Simple MLP probabilistic encoder
  Decoder based on PARSEC parametrization1
H.Sobieczky, Parametric airfoils and wings, in: K. Fujii, G.S. Dulikravich (Eds.), Notes on Numerical Fluid Mechanics, vol. 68, Vieweg Verlag, 1998, pp. 71–88.

## Slide 8: Data pipeline (3/6): Airfoil Shape VAE
Resulting latent space
  Latent space visualisation using TSNE
Generation procedure

## Slide 9: Data pipeline (4/6): Probabilistic CFD Inputs
Robust model development: need to generalize to a wide variety of inflow conditions
CFD boundary conditions generated via probabilistic sampling
  Distributions of input variables mimic plausible wind turbine conditions
Roughness (prediction goal):
  4 patches with increased roughness at the leading edge
  Each patch has roughness height sampled from a truncated half-normal distribution

## Slide 10: Data pipeline (5/6): CFD Simulation and Validation
CFD model:
  OpenFOAM 2D k-omega SST LM
  Changes in surface sand-grain roughness at 4 patches replicate LEE
Validation of CFD model
  Trends in pressure distributions match previous experimental work by Maniaci et al.1
Maniaci, D.C., White, E.B., Wilcox, B., Langel, C.M., van Dam, C.P., Paquette, J.A., 2016. Experimental Measurement and CFD Model Development of Thick Wind Turbine Airfoils with Leading Edge Erosion. J. Phys. Conf. Ser. 753, 022013.

## Slide 11: Data pipeline (6/6): Summary

## Slide 12: ML Architecture (1/3): Data Representation
Multiple options for data ‘substrate’
  Arrays (values at fixed points in space, i.e., image representation)
  Point clouds (values at any point in space)
  Graphs (set of vertices and edges)
Data representation has big impact on ML architecture and performance
We choose to use the point cloud representation
  Simple yet efficient
  Many possible point cloud ML architectures possible

## Slide 13: ML Architecture (2/3): PointNet
ML architecture based on PointNet1
Qi, Charles Ruizhongtai, et al. "Point-Net: Deep Learning on Point Sets for 3D Classification and Segmentation. CoRR abs/1612.00593 (2016)." arXiv preprint arXiv:1612.00593 (2016).

## Slide 14: ML Architecture (3/3): Two stage model
Two parts:
  Flow parameter estimation (AoA, Uin, Turb), either ML based or analytical methods*
  Roughness predictor
* See WESC presentation given by Julien Deparday: Development of a method for obtaining local inflow angle from pressure gradient at leading edge on operating wind turbine blades

## Slide 15: Results (1/2)
First prototype dataset of 300 CFD simulations:
  Same value of roughness used in all patches
  240 used for training, 60 for validation
Initial results:
  15 roughness predictions for validation shown
  Overall promising results, but:
    Often overpredicts roughness
    Predictions are worse for smaller roughness values

## Slide 16: Results (2/2)
Possible causes of roughness overprediction:
  Could be due to the small size of the dataset
  Small increases in roughness have a minor impact on the pressure field
  Effects of roughness on boundary layer transition not yet accounted for in our CFD model
Solutions:
  Larger dataset required
  Adjust distribution of roughness
  More accurate CFD model required (modified k-omega SST LM)

## Slide 17: Conclusion
We developed a pipeline to create a robust dataset which:
  Replicates a wide range of operational conditions
  Uses CFD on diverse airfoil geometries obtained via generative ML
  Aims to introduce as little exclusion bias as possible
We used a split machine learning approach which, given a pressure field around an airfoil:
  Aims to predict the roughness at the leading edge of an airfoil
  Aims to predict the flow conditions
Future work:
  Generate full dataset (5k samples)
  Increase accuracy of CFD model
  Test and compare multiple ML architectures and analytical flow estimators

## Slide 18
Thank you for your attention!
dutheg@ethz.ch
Find out more here:
https://www.iet.hsr.ch/index.php?id=19191&L=4
Other AeroSense presentations:
Development of a method for obtaining local inflow angle from pressure gradient at leading edge on operating wind turbine blades – Julien Deparday in Smart Blades Technologies, 14:05 on Tuesday
Digital Twin Workflow Development Framework in the Context of Fluid Structure Interaction - Yuriy Marykovskiy in Digital Twin Technology, 14:25 on Tuesday
Towards A Self-sustaining Wireless Smart Sensor Node for Continuous Monitoring of Wind Turbines - Tommaso Polonelli in Novel Sensing and New Measurement Concepts for Wind Turbines, 14:15 on Friday