## Slide 1
Pedro Santos, Julia Gottschall (Fraunhofer IWES)
Johannes Becker, Linda Schempf, Ute Knörr (GEO-NET Umweltconsulting GmbH)
A business case for wind resource assessment using scanning wind lidars
23 November 2021 WindEurope 2021 – Resource Assessment Quickfires
doi.org/10.5281/zenodo.5722362

## Slide 2
Resource assessment at the Austrian Alps… what would you do?
2 met masts?
3 met masts?
© Fraunhofer IWES
© Fraunhofer IWES
1 or 2 met masts and a profiling lidar?
OR… another solution?

## Slide 3
What we’ve done
Methodology to reduce numerical modeling uncertainty in resource assessment using one scanning lidar [1]
[1] J. Gottschall et al.: Advancing wind resource assessment in complex terrain with scanning lidar measurements (2021). In Energies. DOI: 10.3390/en14113280
© Fraunhofer IWES
© Fraunhofer IWES

## Slide 4
The methodology and example case study
Process 1-min PPI scans to 30-min ensemble means and cluster the data in a capture matrix.
Project numerical model output (3D wind field) onto single scanning lidar beams
Normalize observed and simulated radial wind speed fields
Map of differences between observations and simulations as basis for numerical model calibration
[1] J. Gottschall et al.: Advancing wind resource assessment in complex terrain with scanning lidar measurements (2021). In Energies
Demonstration campaign published in [1]
First commercial campaign in 2021 (Windsfeld project)
Milestones

## Slide 5
Takeaways
Dr. Julia Gottschall – julia.gottschall@iwes.fruanhofer.de
Dr. Pedro Santos – pedro.santos@iwes.fraunhofer.de
Questions? More details?
Fraunhofer IWES/GEO-NET proposed a methodology for assessing numerical modeling biases using scanning lidars
First commercial scanning lidar campaign for resource assessment in complex terrain carried out in 2021
Results can reduce AEP uncertainty via numerical model calibration and optimization of wind farm layout
© Fraunhofer IWES

## Slide 6
Federal Republic of Germany
Federal Ministry for Economic Affairs and Energy
Federal Ministry of Education and Research
European Regional Development Fund (ERDF):
Federal State of Bremen
Senator of Civil Engineering, Environment and Transportation
Senator of Economy, Labor and Ports
Senator of Science, Health and Consumer Protection
Bremerhavener Gesellschaft für Investitionsförderung und Stadtentwicklung mbH
Federal State of Lower Saxony
Free and Hanseatic City of Hamburg
Acknowledgements
Fraunhofer IWES is funded by: