## Slide 1: Estimated cost of Great Britain’s linepack flexibility per kWh of natural gas Dr Grant Wilson: i.a.g.wilson@bham.ac.uk

## Slide 2: Gas system flexibility
Flexibility provided by the gas system requires better visibility and discussion around its value. This should happen throughout the RIIO-2 time period
Currently, there is considerable focus on the electrical system and its ability to provide flexibility over different timeframes
This presentation will provide values on the historical scale of linepack (only one element of gas system flexibility), and an estimate of the cost to the system, and thus the cost of linepack flexibility per kWh of ‘overnight’ energy storage

## Slide 3: Measured data – from National Grid and GDNs

## Slide 4: Measured data – from National Grid and GDNs

## Slide 5: Gas system flexibility
Adding all of the daily changes in linepack (linepack flexibility) over a year provides a cumulative sum value for the years 2014 to 2020 inclusive
These cumulative values are displayed on the next slide, with NTS being the National Transmission System values and GDN being the Gas Distribution Network values

## Slide 6: Linepack flexibility annual totals (cumulative sum of daily flex)

## Slide 7: Cumulative daily linepack flexibility from measured data
Each year the NTS and GDNs higher pressure tiers typically provide around 100 TWh of cumulative daily linepack flexibility
In comparison pumped storage ranged between 4 TWh in 2009 and under 2 TWh per year in 2020
Challenging to disaggregate the costs of linepack and the costs of transporting gas around the NTS system

## Slide 8: Estimated costs of linepack provision
Capex cost estimate is the replacement cost of compressors on the NTS system, say £30-£40 million with a lifetime of 25 years
With 23 compressor stations and 3 compressors per compressor station – say there are 3 replacements each year ~= £120 million per year
Opex costs of compressors estimate using all the gas badged as ‘shrinkage’ at the NTS, say £60 million in 2020 (more in 2021)

## Slide 9: Estimated costs of linepack storage
Total is £120 million + £60 million per year for compressor capex and opex, and rounding up to £200 million
Regardless of the levels of linepack flexibility (much lower in summer than in the winter), the gas pressures in the NTS are still required to transport gas itself rather than provide flexibility
In 2020, the NTS transported approximately 900 TWh of natural gas (including exports)

## Slide 10: Estimated costs of linepack storage
Therefore, a simple cost estimate for linepack flexibility is to use the ratio of 100 TWh of cumulative daily linepack flexibility to the 900 TWh of 2020’s total gas transported
Doing so gives a cost of linepack of:
£200 million x 100 / 900 == £23 million (rounded up)

## Slide 11: Estimated costs of linepack storage
Using this method of linepack flexibility cost estimation
100 TWh at a cost of £23 million equates to 0.023 pence to store a kWh of natural gas as overnight linepack flexibility
Even if all of the £200 million was allocated to linepack flexibility this would equate to 0.2 pence per kWh

## Slide 12: What does ‘overnight’ storage at 0.023 pence per kWh mean?
The costs are uncertain from the perspective of the allocation of costs – but it is clear that linepack provides a very low cost method of storing energy overnight
Throughout the RIIO-2 timeframe, this requires greater focus to understand the costs of storage and make them more visible
Importantly, can the cost of overnight linepack storage somehow be passed through on a more cost reflective basis?

## Slide 13: What does ‘overnight’ storage at 0.023 pence per kWh mean?
Shifting demand from the natural gas system to the electrical system can also shift part of the need for overnight flexibility
There are a number of options for the provision of overnight flexibility to the electrical system including, demand side response, e.g., through time of use tariffs, batteries, pumped storage, and many more types of storage
However, these forms of overnight storage are likely to cost more than the cost of linepack flexibility, and therefore, this is an area that OfGEM needs to consider with the help of sector stakeholders during the RIIO-2 timeframe

## Slide 14: RIIO-2 discussions
On a whole system basis, if the gas system can continue to provide very low cost overnight (and seasonal) storage but in future in a low-carbon manner, do regulatory incentives need to change to make this happen?
Deeper stakeholder discussions should therefore take place through this regulatory timeframe to reduce the risk of appeals to the CMA

## Slide 15: Gas system flexibility
This presentation does not consider seasonal flexibility, or the ability of interconnectors, cavern storage and LNG to explicitly ramp up and down their output to the NTS system
Balancing energy systems across seasonal and multi-year timeframes seems to continue to require balancing that is orders of magnitude greater than daily storage1
Understanding future costs of flexibility is an area that needs further detail for different approaches across the whole system. A better understanding of the levels and costs of existing gas system flexibility can help
1 NET ZERO - KEEPING THE ENERGY SYSTEM BALANCED
MacLean, Wilson and Godfrey (2021)
https://doi.org/10.5281/zenodo.5116342

## Slide 16
i.a.g.wilson@bham.ac.uk
Lecturer, Energy Informatics Group
Fellow of the Alan Turing Institute
School of Chemical Engineering
University of Birmingham
0121 414 5383
https://www.linkedin.com/in/iagwilson/
Leads the Energy Informatics Group: activities include analysis on energy system flexibility, using multi‐vector, multi‐scale data analytics
Contact details