## Slide 1: Knowledge Graph Primer
Providing answers for users’ information questions – even the ones you had not thought of.
Dr. Peter J Lawrence
Peter.Lawrence@inova8.com

## Slide 2: Creating a realistic plant model: a digital-twin
What are the issues to be solved applying knowledge graphs to an industrial application
Limitations of 1D modeling (simple subject-property-object)
Useful concepts from Basic Formal Ontology
Extension to 2D modeling (reified statements so we can have other data such as UnitsOfMeasure, accuracy, version and so on)
Extension to 3D modeling (so we can capture the fact that knowledge is always changing over time)
Avoiding complex taxonomies with shapes

## Slide 3: 1-D Modeling
1-D using simple statements to create the schema and model
1-D Schema consists of
  A taxonomy of classes aka Types of thing
  Attributes/dataProperties of these types of things
  Relations/objectProperties linking types of things
In other words, simple RDF/RDFS/OWL/RDFS+ types of model

## Slide 4: Limitations of 1-D Models
A relationship alone does not have enough information
:Peter
:Beth
:marriedTo
  :Peter :marriedTo :Beth
    When, where, by whom, how, why, …?
:Pump101
42^^xsd:float
:dischargePressure
  :Pump101 :dischargePressure 45
    When, what units, what accuracy, …
:Tank101
:Unit10
:partOf
  :Tank101 :partOf :Unit10
    Geographically part of, organizationally part of, in the same maintenance hierarchy, …?
:Blend45
:SRN
:consistsOf
  :Blend45 :consistsOf : StraightRunNaptha
    What percentage of SRN in this blend, how was SRN added, why added, …
:FT107
:FC107
:connectedTo
  :FT107 :connectedTo :FC107
    How connected, why connected, has it always been connected this way, …

## Slide 5: 2-D Modeling
Reification of attributes and relations
    Definition: the act of changing something abstract (= existing as a thought or idea) into something real:
Example
    1-D Model: :Peter :marriedTo :Beth
    :marriedTo occurred in an instance of a marriage ceremony, lets create this thing
    2-D Model: :PeterBethMarriage a :Marriage ;
        :Peter :partner :PeterBethMarriage ;
        :Beth :partner :PeterBethMarriage ;
        :PeterBethMarriage :tookPlace ‘1991’;
        :PeterBethMarriage :at :Kelby ;
      … and so on

## Slide 6: 1-D to 2-D model transformation
:Peter
:Beth
:marriedTo
Much more powerful organization of knowledge
More verbose
  But storage is cheap!
Obsoletes the need for custom ‘PropertyGraph’ technology
:Peter
:Beth
:PeterBethMarriage
:partner
:partner
:Kelby
:at
1-D to 2-D model transformation
:Marriage
a
”1991”xsd:date
:tookPlace

## Slide 7: 1-D to 2-D Plant Model Transformation
:Reboiler-001
:Pipe-003
:connectedTo
:Reboiler-001
:Pipe-003
:Reboiler-001-Pipe-003
:connectorFrom
:connectorTo
:ProcessConnector
1-D to 2-D model transformation
:Connector
a
:connectorType
:Connector-Reboiler-001-process-Pipe-005
:connectorFrom :Reboiler-001 ;
:connectorTo :Pipe-005 ;
:connectorType :ProcessConnector ;
.

## Slide 8: Blank Nodes Or Not
It is possible to avoid the creation of a unique IRL for these relationships.
For example
      [ ] a :Marriage ;
        :isPartnerIn :Peter ;
        :isPartnerIn :Beth ;
        :tookPlace ‘1991’;
        :at :Kelby ;
        …
  Where [ ] is a blank node
  Blank nodes are assigned an arbitrary ID within the triple store
  When serialized out they are often assigned a unique, but not repeatable, urn
  However, these cause problems:
    When debugging models
    Transferring a graph from one triplestore to another

## Slide 9: Use (or misuse!) of Blank nodes
:Connector-Reboiler-001-process-Pipe-005
:connectorFrom :Reboiler-001 ;
:connectorTo :Pipe-005 ;
:connectorType :ProcessConnector ;
.
[]
:connectorFrom :Reboiler-001 ;
:connectorTo :Pipe-005 ;
:connectorType :ProcessConnector ;
.
Constructed name (easier to debug)
Blank Node (not recommended!)
:QVYkYmFzaWNfc3RyaW5nX1dVJGNoYXJfdHJhaXRzX1dzdGRWJGFsb :connectorFrom :Reboiler-001 ;
:connectorTo :Pipe-005 ;
:connectorType :ProcessConnector ;
.
Generated UUID (recommended for production)

## Slide 10: 1-D to 2-D Verb to Noun Mappings
1-D (verb) | 2-D (noun)
:marriedTo | :Marriage
:connectedTo | :Connection
:connectedFrom | :Connection
:partOf | :Assembly :PartWhole
:comprises | :Composition
:constitutes | :Constituent
:isAttrubute | :Attribute
… | …
These are encountered in plant modeling
Probably all that is required to build a ‘digital twin’
1-D models use ‘verbs’ to link subjects to objects
2-D models use ‘noun phrases’ to which other objectProperties and dataProperties are associated

## Slide 11: 1-D to 2-D Examples
1-D Relation | 2-D Relationship
:Pump101 :dischargePressure 45; | :Pump101-DischargePressure a :Attribute; :of :Pump101; :property :DischargePressure; :value 45; :accuracy .05; …
:Tank101 :partOf :Unit10 | :Unit10-part-Tank101 a :PartWhole ; :whole :Unit10 ; :property :OperationalPart ; :part :Tank101 ; …
:Blend45 :consistsOf :StraightRunNaptha | :Blend45-component-SRN a :Constituent ; :blend :Blend45 ; :property :BulkConstituent ; :component :SRN ; :percentage ’85’ ; …
:FT107 :connectedTo :FC107 | :FT107-mv-FC107 a :Connection ; :from :FT107 ; :connectionType :MeasuredVariable ; :to FC107 ; :medium “4-20”; …

## Slide 12: 1-D to 2-D Examples
1
-
D Relation
2
-
D Relationship
:Pump101 :
dischargePressure
45;
:Pump101
-
DischargePressure
a :Attribute;
:of :
Pump101;
:property :
DischargePressure
;
:value
45;
:accuracy .05;
…
:Blend45 :
consistsOf
:
StraightRunNaptha
:Blend45
-
component
-
SRN a :Constituent ;
:blend
:Blend45 ;
:property :
BulkConstituent
;
:component
:SRN ;
:percentage ’85’ ;
…
:FT107 :
connectedTo
:FC107
:FT107
-
mv
-
FC107 a :Connection ;
:from :FT107 ;
:
connectionType
:
MeasuredVariable
;
:to FC107 ;
:medium
“4
-
20”;
…
:Tank101 :
partOf
:Unit10
:Unit10
-
part
-
Tank101
a :
PartWhole
;
:whole
:
Unit10 ;
:property :
OperationalPart
;
:part :Tank101 ;
…

## Slide 13: 2-D Models Elsewhere
‘Reification’ appears in many ‘standard’ models:
  SKOS a simple model of a taxonomy of concepts
    SKOS was extended to SKOS-XL, incorporating the 2-D styles
  PROV models the provenance of documents/media/ etc
    Built upon the same reification-of-predicates principles

## Slide 14: PROV
PROV models provenance:
    How some document was written
    :Who, why, when it was changed and so on
Person
ContentItem
Person
Activity
ContentItem
1-D RDF
2-D PROV
wasGeneratedBy
:wasAssociatedWith
:wasGeneratedBy
:wasAttributedTo
:involvedIn
:CharlesDickens :wrote :TaleOfTwoCities
:TaleOfTwoCitiesAuthorship a :Activity ;
:wasAssociatedWith :CharlesDickens ;
:activity :Authorship
:of :TaleOfTwoCities ;
…
:HenrykSienkiewicz
:wrote
:QuoVadis

## Slide 15: Purchase Order
A classic RDBMS 101 model
:PO#3
:ProductA
:PO#3
:PO#3-LineItem2
:ProductA
1-D RDF
2-D
wasGeneratedBy
:within
:of
:orderLineItem
:PO#3-LineItem2 a :LineItem ;
:within :PO#3;
:status :backOrdered
:of :ProductA ;
…
:backOrdered
:status

## Slide 16: Continuants and Occurrents
Entities/ThingsThings
Continuant/Endurants
Occurrent/Perduants
2-D Models add to the types of ‘things’ in our model
These can be in two groups
  Continuants/Endurants: Type of things that have a permanent existence
  Occurrents/Perduants: Types of things that express a process or activity that often links things together
:Tank
:Unit
:FlowMeter
:Material
:…
:Attribute
:Person
:Marriage
:Connection
:PartWhole
:Constituent
:…
:Instrument

## Slide 17: Initial Type structure (aka taxonomy) for 2-D Models
:Tank
:Unit
:FlowMeter
:Material
:…
:Attribute
:Person
:Marriage
:Connection
:PartWhole
:Constituent
:…
:Instrument
:Continuant
:Occurrent
:Entity
Only 4 types of occurrents are required for plant modeling/
digital-twin
(I believe!)
1000’s of types of continuants maybe required for plant modeling (eq ISO 15926).
Let’s explore this further!

## Slide 18: 3-D Models: Temporal Changes
A model captures the state of entities, but not only at a point in time, but also as that model changes over time.
Changes occur for many reasons, but they can be loosely categorized as:
  Corrections when the state was recorded incorrectly so now the model has to change to reflect the correct state.
    These changes need not be part of the ‘current’ model, so a change-logging approach is best suited to this case
  Evolutions when the state is evolving over time.
    There are two approaches
      3-D modeling
      4-D modeling

## Slide 19: 3-D How?
:Reboiler-001
:Pipe-003
:Reboiler-001-Pipe-003
:connectorFrom
:connectorTo
:ProcessConnector
:Connector
a
:connectorType
:Connector-Reboiler-001-process-Pipe-005
:connectorFrom :Reboiler-001 ;
:connectorTo :Pipe-005 ;
:connectorType :ProcessConnector ;
.
:Period1
:connectorPeriod
09-03-2002^xsd:dateTime
04-01-2021^xsd:dateTime
:starting
:until
:connectorPeriod [ :starting 09-03-2002^xsd:dateTime ;
:until 04-01-2021^xsd:dateTime ]

## Slide 20: 3-D Advantages
The advantage of this 2-D/3-D model is that
  Any 2-D model can be extended to 3-D
  :starting and/or :ending are not essential/optional
This allows any model to evolve over time in a very consistent way.

## Slide 21: 4-D Modeling (alternative to 3-D)
3-D is not the only approach to time-varying plant models.
4D models regard everything as perpetual ‘things’ that are brought together for a period.
  Thus, an attribute persists for ever, but it is brought together with its target for a certain period.
  Similarly, an asset is perpetual, but is brought together with its plant tag for the period during which it performs the function of that tag.
Used in ISO 15926

## Slide 22: 3-D Alternatives
Personally, I find 4-D models less intuitive and more complex than 3-D models
However, this demonstrates the flexibility of graph-models:
  how the facts are captured is very flexible,

## Slide 23: Change logging
Logging added and deleted triples in such a way that
  The time of the change is recorded
  By whom the change was executed
  The set of triples that were changed
  The ability to rollback a change
In RDBMS, O-O, NoSQL worlds, change logging can be complex because of all the different structures that are being managed.
In the RDF Graph world, there is only one data building block:
  the subject-property-object triples
Therefore, change logging requires recording the triple before and after change, together with the time and other meta data about the change.
Not only is this conceptually very simple, it is also very easy to rollback changes

## Slide 24: Change Logging in the Graph World
Suppose a pump’s maximum discharge pressure was incorrectly recorded
:Pump101
42^^xsd:float
:maximumDischargePressure
:Pump101
43^^xsd:float
:maximumDischargePressure
Change
Current Graph
:aChange
:Change
a
Log
Change Logging Graph
:Pump101
42^^xsd:float
:maximumDischargePressure
:subject
:property
:object
:PJL
:by
03/05/2020
:at
:Update
:reason

## Slide 25: 3-D Models are not Taxonomies
3-D models capture the processes by which equipment is assembled, and deployed, attributes are assigned, and their values changed.
3-D imply nothing about ‘taxonomies’

## Slide 26: Why do we like taxonomies?
A taxonomy can be a short-hand for grouping behaviours:
  Every subtype of Instrument can be expected to have a signal connection
    They will, though, have other characteristics such as status signal, local indication, and so on.
  Every subtype of :Pump can be expected to have an inlet and outlet flow (hopefully with a pressure increase)
    They will, though, have other characteristics such as drive type, accuracy, and so on.

## Slide 27: Gorilla-Gorilla-Gorilla!
Forcing one into a strict taxonomy, can create anomalies, such as the reclassification of gorillas:
Gorilla-Gorilla Gorilla
Originally unaware there were different types of Gorilla, but then sub-categories emerged. That meant the originally identified instances had to be recategorized as Gorilla-Gorilla-Gorilla!

## Slide 28: Avoiding Taxonomies
Taxonomies are used as a shorthand for describing behaviours.
  A technique reinforced by the object-orientated paradigm
Alternatively separate grouping-model from behaviour-model
  Behaviour-model
    We can use graph shape-description languages to capture the rules of any thing that we want to model
    OWL, SHACL, SHEX, …
  Grouping-model
    We can use loose taxonomies such as SKOS to capture groupings of things that enhance our search capabilities without imposing unnecessary meaning on the subclasses (known as broader/narrower in SKOS)

## Slide 29: Behaviour Model: Shaping Things with SHACL
SHACL allows many different things to be described by the ‘shape’ of its nodes and edges.
  The advantage of using SHACL (or alternatively SHEX) is that many different yet similar ‘things’ can be declared without the need to have a complex taxonomy of classes, complex RDFS, or OWL.
For example
  an :ElectricallyDriven-Rotary-Metering-Pump
    a petrol-station fuel pump meter
  is similar to a :PressureDifferentialDriven-PositiveDisplacement-Metering-Pump
    a residential gas meter,
  but it would be difficult to describe in RDFS.
  I am sure OWL devotees would want to prove this to be incorrect!

## Slide 30: Pump-Motor :G102A Description
For something to be classified as, say, a :Pump-Motor set it requires the following assembly:
  :G102A is a functional ‘tag’ on a P&ID/PFD
  In reality, it requires a pump, currently :A6789
  And a driver, currently :M235
  It also needs to be plumbed into its service, inputting :SRN-Feed and exhausting :SRN-Exhaust
In the context of this assembly of parts, we can immediately infer what a component ‘is’ by seeing the role that it performs in this assembly:
  :G102A is a functional item within the context of a P&ID or PFD
  :A6789 functions as a pump part of that assembly because it takes a feed and produces an exhaust
  :M235 functions as driver of that assembly.
:G102A
:A6789
:M235
:SRN-Feed
:SRN-Exhaust

## Slide 31: Pump-Motor :G102A Graph
:G102A
:as
:as
:of
:AssemblyPart1
:AssemblyPart2
:hasPart
:hasPart
:Deployed
:A6789
:M235
:of
:Transfer1
:from
:to
:DrivePower
:of
:Process
:SRN-Feed
:SRN-Exhaust
:Connector1
:Connector2
:from
:to
:to
:from
:of
:of
Note, not showing the 3-D temporal nodes but could be added
Continuant
Occurrent
OccurrentType
:G102A
:A6789
:M235
:SRN-Feed
:SRN-Exhaust

## Slide 32: Pump-Motor Graph Shape
<anyTag>
<anyPump>
<anyDriver>
:<any>
:<any>
:<any>
<anyFeed>
<anyExhaust>
:<any>
:<any>
:hasPart
:hasPart
:of
:of
:from
:to
:from
:to
:to
:from
:Deployed
:as
:as
:DrivePower
:of
:Process
:of
:of
This graph fragment represents the ‘shape’ we want our Pump-Motor installation data to take for it to be classified as valid installation.
SHACL is one graph specification we can use to describe this pattern
These patterns would be called Reference Data Library in ISO-15926 terminology
<anyTag>
<anyPump>
<anyDriver>
<anyFeed>
:<anyExhaust>

## Slide 33: Pump-Motor SHACL
The following illustrates how a shape can be specified:
:pumpMotorShape
a :NodeShape ;
:property [
:description “Installation must have one motor deployed” ;
:path :hasPart ;
:maxcount 1 ;
:node [
a :NodeShape ;
:description “need an occurrence of an assembly” ;
:property [
:description “must be a :Deployed occurrent” ;
:path :as ;
:hasValue :Deployed ]
:property [
:description “must be a motor thing”
:path :of ;
:node [ … description of a valid motor…]
]
]
:property [
:description “Installation must have one pump deployed” ;
… and so on
]

## Slide 34: Shape Advantages
If it quacks and has feathers it is a duck!
Jeśli kwaka i ma pióra, to jest kaczka!
O-O:
  Declares something as being of type Pump-Motor
  Leads to a complex hierarchy/taxonomy of types
  Rigid structure that inhibits evolution
Graph Shape:
  Deduces something is a Pump-Motor from the role (aka data) in the graph
  No need for hierarchy of types
  Shapes can evolve,
    which might show some things lose their validity
  Same ‘thing’ can satisfy more than one shape
    Motor, Maintenance-Item, Electrical equipment and so on
  Can be used to define a user-interface

## Slide 35: Grouping Model: SKOS ontology
We should avoid taxonomies as a way of defining the behavior of individuals
  Graphs and shapes of graphs provide a much better way.
However, we like to see ‘trees’ of things:
  A visually easy way to find things
  Allows categorization into different groups/collections
To solve this dichotomy, we can use SKOS
  Simple Knowledge Organization System
  Simply has :Concepts linked together with :broader/:narrower
  (ok a bit more than that but not much)

## Slide 36: SKOS Example
ElectricallyDriven-Rotary-Metering-Pump
:ElectricallyDriven-Rotary-Metering-Pump
a skos:Concept
skos:broader :ElectricalEquipment ;
      :RotaryEquipment ;
      :Instrumentation ;
      :Pump ;
PressureDifferentialDriven-PositiveDisplacement-Metering-Pump
:PressureDifferentialDriven-PositiveDisplacement-Metering-Pump
a skos:Concept ;
skos:broader :PositiveDisplacmentEquipment ;
      :Instrumentation ;
      :Pump ;

## Slide 37: SKOS Example
SKOS is very flexible.
It can be used to construct a taxonomy of plant equipment
However, it is not intended to convey the behavior of the equipment
  That is achieved using rules such as SHACL
:PlantItem
Top concept
:ElectricalEquipment
:RotaryEquipment
:Instrumentation
:Pump
:PositiveDisplacementEquipment
Collection Concepts
skos:broader
skos:broader
skos:broader
skos:broader
skos:broader
:M1234
:PD743
Instance Concepts
skos:broader
skos:broader
Sub-Collection Concepts
:ElectricallyDriven-Rotary-Metering-Pump
:PressureDifferentialPositiveDisplacement-Metering-Pump
skos:broader
skos:broader
skos:broader
skos:broader
skos:broader
skos:broader

## Slide 38: Putting it all together: Digital Twin Modeling

## Slide 39: Modelling Concept Building Blocks
Attributes
Constituents
Transfers
Parthoods
Continuants
Transfers
Parthoods
Attributes
Constituents
Occurrents
Relationship properties:
Edge kind
Effective period
…any user-defined
3D

## Slide 40: Modelling Concept Building Blocks
:Reactor
:CWR
:Feed
:V101
:Reactant
$this.getSignal("<SEEQ://host.docker.internal:34216/api/signals/6608A381-5AC4-4D2A-94A4-39A55A226815
42
:Stripper.Overhead
:Temperature
:Unit-Unit
:Stored
:ContainedWithin
:FeedTo
:ReturnFrom
:Movement
Continuants
Transfers
Parthoods
Attributes
Constituents
Occurrents
Relationship properties:
Edge kind
Effective period
…any user-defined
3D

## Slide 41: Production Modeling Vocabulary
UnitA
UnitB
MaterialA
Tank1
LineupX
MaterialA
MaterialB
Plant
TransferY
ContentsZ
ContentsW
at
what
where
where
what
from
to
to
from
produced
feed
what
where
Continuants
Transfers
Parthoods
Attributes
Constituents
Occurrents
part of
part of
part of
part of
ContentsW
of
Edges
where == location
of == continuant performing role
what == what is being acted upon
from == source
to == destination
part of/produced/to/feed/from
== part-whole

## Slide 42: Putting it all together: Tennessee-Eastman Plant Digital Twin
Reactant
G
Sep.Liq
TestPlant
Condensate
Condensate
CondensateFeed
Overhead
Feed
Product
Vapour
Feed
Product
Bottoms
Feed
Condensate
Overhead
PI
Y16
V101
V102
V103
V104
S101
G101
G104
G103
B103
H101
H102
Feed + Condensate - Bottoms
CondensateFeed-Condensate
Feed
G
TestOffsite
A
D
E
A+C
G
F
2F
H
TestOnsite
TestSite
5
Y20
Y12
L1
XA
XC
XD
XE
XF
XG
XH
XB
Y30
Y31
Y32
Y33
Y34
Y35
Y36
Product
Purge
9
XD
XE
XF
XG
XH
U8
1
2
U3
FL
FL
FL
FL
ANALYSER
XA
XC
XD
XE
XF
XB
FL
Y10
FL
Y5
U5
TI
JI
PI
U6
FL
TI
Y18
A
D
E
C
CWS
CWR
CWR
CWS
TI
TI
PI
SC
LI
U1
Y1
Y2
Y3
3
FL
TI
U2
U12
Y8
Y6
Y9
Y21
Y7
Y22
Stm
Cond
Y11
Y14
Y19
FL
FL
Y17
LI
Y15
U10
U11
Y4
U4
Y23
Y24
Y25
Y26
Y27
Y28
Y29
U9
U7
Y37
Y38
Y39
Y40
Y41
Y13
input A
input D
input E
input C
Reactor
Condenser
Vapour
Separator
Stripper
Purge
Output
Product
Output
Compressor
ANALYSER
ANALYSER

## Slide 43: Example Refinery: Digital-Twin Model
LowEnergy
HighYield
1FI001.MV
3FI001.MV
3FI002.MV
3FI003.MV
3FI004.MV
2LI001.MV
2LI002.MV
5LI001.MV
5LI002.MV
5LI003.MV
1FI002.MV
1FI003.MV
4FI001.MV
4FI002.MV
4FI003.MV
4FI004.MV
1FI004.MV
Plant:1
Unit:3
Unit:4
Feed:1
Prod:1
Prod:2
Feed:3.1
Prod:3.1
Prod:3.2
Feed:4.1
Prod:4.1
Prod:4.2
Flare:3.1
Flare:1
Flare:4.1
TankFarm:5
TankFarm:2
Tank:2.1
Tank:2.2
Tank:5.1
Tank:5.3
Tank:5.2
IntermediateE
IntermediateD
IntermediateC
IntermediateB
FeedA
FeedB
FeedC
ProdA
ProdB
ProdC
ProdD
Fuel
IntermediateA

## Slide 44: Thank You!

## Slide 45: Plant Digital-Twin Model
42
27
24
15
Unit
1
Unit
1
Unit
3
Unit
4
TK1
TK2
TK3
TK4
Capture the ‘physical’ plant
Identify measurements and calcs in relation to plant
Capture planned material flows
Capture actual material flows
SRN
HGO
ANS
RES
LNAP
Materiel
Dimension
(What-Material)
Spatial Dimension
(Where-Topology)
Temporal Dimension
(When-Measurement)
Notes: A physical data model differs from a process data model.
We start with the plant, and then identify the key elements of the plant: the units and tanks.
Then we place the streams (battery limits) that convey material to and from units.
Next we identify the measurements associated with the tanks and battery limits. These provide the criteria associated with the resources.
Finally the scheduling system provides the material movements that are scheduled to move from one location to another. Operations then confirm that these movements took place.
From this information we can support all of the business processes that manage a plant.

## Slide 46: Adding Unstructured to Structured: From strings, through things, to facts
Documents
Text Index
Aka Key words
String Search
Text Indexing
Query:
Poland+France+Diaspora
Knowledge Index
Aka semantic model
Knowledge Model
Aka Ontology
Fact Search
Knowledge Extraction
Query:
?doc where contains facts
?doc :relatedTo ?migration .
?migration :from :Poland ; :to :France
Vocabulary
Aka taxonomy
Entity Index
Aka Entity Catalog
Thing Search
Entity Extraction
Query:
Poland|Polish
+France|French
+Diaspora|Migration