## Slide 1: Knowledge graphs in construction
Seppo Törmä
VisuaLynk & Metropolia

## Slide 2: Varieties of building data

## Slide 3: Interrelated but disconnected subdomains
Building
design (BIM)
Agents
People
Energy
efficiency
Materials
Processes,
activities,
plans
Sensor data
Classifi-
cation systems
Ownership, tenancy
Occupancy, preferences,
acoustics, Indoor air
Past energy profile
Energy simulations
Energy systems
Energy-related renovation measures
User
requirements
Workspaces
Required activities
Activity precedence
Lifecycle impacts
Safety and recycling. demolition
Occupancy
profiles
Building performance
Construction
conditions
Positioning
Types of processes and methods
Types of elements,
spaces,
products
Notifications
Feedback
Products
Product requirements, product selections
Information
entities
Container
of models
Statistics
Container of plans
Built
assets
Apartments,
owners
Renovation
scenarios
Renovated
entities
Required
processes
How to connect multiple conceptual domains? How to connect the data in those domains?

## Slide 4
Construction
project
Telecom
networks
Knowledge graph
Linked Data
(RDF, URI)
Ontologies
(OWL)
Rules
(SWRL, SHACL, ...)
Database for
network-structured
data
Real-world
networks
Networks of
heterogeneous relations between entities
applicable to
Transportation
networks
Social
networks
examples
Labeled
property
graph
Semantic knowledge graph
solution
solution
standards
RDF-Star
Asset
management
Enterprise management
examples
convergence
Queries
(SPARQL
Programming support
Fast graph
algorithms
advantage
Rich models
Flexibility
Reasoning
advantage
Query
(GraphQL)
Decentralization, federation
Standards-based tools
standards

## Slide 5: Semantic knowledge graph – a small example

## Slide 6
Knowledge graph
Service
knowledge graph
Enterprise
knowledge graph
Applications of knowledge graphs
Knowledge graph in construction
Asset knowledge graph
Project knowledge graph
Google
knowledge graph
Amazon
product graph
Uber
knowledge graph
Apple’s
Siri
LinkedIn
BBC
Elsevier
Roche
Bechtel
Bosch
...
Enterprise
ontology
examples
examples
involves
300-500 concepts
scope
subtypes
subtypes

## Slide 7
Knowledge graph in construction
Asset knowledge graph
Project knowledge graph
subtypes
Digital logbook
Digital twin of a building
BIM data
BAS data
IoT data
Agents
Legal aspects
FM data
data combined from
applications areas
Facility
management
Product data
Financial data
Situation
picture
Digital twin of the process
Lean
construction
Entity-activity flows
Preconditions
BIM data
Quantity surveys
Project plans
data combined from
Supply chains
Monitoring data
applications areas
Climate impacts
Positioning
Imaging
Status event
ISO19650
Asset information model
ISO19650
Project information model

## Slide 8: Challenge of ontologies
For service knowledge graphs, the underlying ontologies have been carefully defined
For enterprise knowledge graph, it is a common practice to develop a company-specific enterprise ontology
  Specific industry sector, company culture, practices, information systems
  Ontology development can usually be done in a half a year
In asset management area, available data and systems are more regular
  Good ontologies exist, and it makes less sense to develop own ontologies
In project management, there is no realistic possibilities to develop new ontologies in the time frame of a construction project
  There is a consortium of companies with different background that come together for the duration of a project
  If information management is based on knowledge graphs, they must rely on standard ontologies
Where do the ontologies come from?
Are there existing ontologies that can be used?

## Slide 9: Ontologies relevant in the construction domain
ifcOWL – BIM models (building objects, their relations and properties)
ICDD – Containers for the exchange of multiple interlinked datasets
DCAT2 – Data catalogs
BOT – Building topology (space and their relations, elements and interfaces)
OWL-Time – Temporal concepts (time intervals, instants, temporal relations)
PROV-O – Provenance metadata
QUDT – Units of measure and quantity kinds
OPM – Property objectification
BFO – Fundamental categories, top-level concepts
FOAF, Org – Agents and organizations
FIBO – Legal roles of agents, to define assets and ownership
SSN/SOSA – Sensor data and sensor networks
Bricks – Building automation systems data
Saref, Saref4Bldg – Devices, sensors, and sensor data
How to manage the multiplicity of ontologies?
How to combine information across ontologies?

## Slide 10: Digital Construction Ontologies (DiCon) – a unified view
https://w3id.org/digitalconstruction/0.5

## Slide 11: BIM4EEB Renovation toolkit
BIMMS (BIM Management System) – SPARQL/REST
(synchronized)
BIMEaser
BIMPlanner
BIM4Occupants
Fast mapping
Receive/create BIM
From BIM tool or
From fast mapping
BIM
BIM
Scenarios
OPRs
BIM
Measures
OPRs
RDF
RDB
LBS
Master plan
Week plan
Occupants
Apartments
Activities
Notification
feedback
(BIM)
BIM4Occupants
AUTERAS/BIMcpd
BIM
Detailed
measures
Identify occupancy profiles
Condition/consumption sensors
Preferences
Explore renovation scenarios
Renovation measures
OPR (owner’s project requirements)
Detail renovation measures
Room automation
Constraint checking, performance analysis
Specify the location breakdown structure
BIM spaces, external areas, workspaces
Make a master plan
Baseline of activities
Multiple versions
Schedule week plans
Tasks scheduled to a specific week
Monitor execution
Actual times and resources
Coordinate with occupants
Alert, notify
Visits, safety, noise, outages
BIM
Occupants
Apartments
Occupancy
profiles
Tools interact through shared data
External data

## Slide 12: Summary and conclusions
Knowledge graphs are a practical and available information management technology with standards for
  data representation (RDF)
  data serialization (Turtle)
  ontology definition (OWL)
  query languages (SPARQL)
  rules and constraints (SHACL)
  object identification (URI)
  decentralized access (Linked Data principles)
In construction domain there are many established ontologies available
  SSN/SOSA, QUDT, OWL-Time, PROV-O, FOAF, FIBO, Bricks, ifcOWL, ...
Due to the nature of asset and project management, it is advisable to use established ontologies
Digital Construction Ontologies is a comprehensive and unified ontology suite aligned with relevant existing ontologies