## Slide 1
Nature-based Solutions for hydro-meteorological hazards
Training 4: Assessing Risks in Socio-Ecological Systems
EU funded project GA no. 776848
Notes: Disclaimers:
- The information, photos, figures and data used are created in the OPERANDUM project, unless another source is mentioned.
- Editable versions of all training units are available upon request. Please contact OPERANDUM by filling out the contact form on the website: https://www.operandum-project.eu/contact/

## Slide 2
EU funded project GA no. 776848
About OPERANDUM
4-year, European project, with 26 international partners
Sustainable solutions based on nature - Nature-based Solutions - to adapt to extreme weather events
Demonstrate the tools and methods for the validation of these solutions in 10 Open Air Laboratories (OALs)
2
Open Air Labs Austria, Finland, Germany, Greece, Ireland, Italy, Scotland (UK), Australia, China, Hong Kong (China)
Notes: OPERANDUM is a European project that researches sustainable solutions based on nature to adapt to extreme weather events. We call these type of solutions 'nature-based solutions’.
In the project, solutions are demonstrated for different types of hydro-meteorological hazards in 10 open air laboratories.
The project is a collaboration between 26 partners in 14 countries – covering universities, NGOs, and SMEs – over 4 years.

## Slide 3
Training Unit 4 at a glance
EU funded project GA no. 776848
3
Part I: Natural Hazards, Risks & NbS in Social-Ecological Systems
Social-Ecological Systems
Risks & Vulnerability in Social-Ecological Systems
Examples of NbS to reduce risks​
Part II: Approaches for Vulnerability & Risk Assessment
OPERANDUM‘s approach to Risk & Vulnerability Assessment
  Impact chains
  Indicators
    Calculation process for vulnerability and risk assessment (Optional)
Challenges
Notes: Part I: Natural Hazards, Risks & NbS in Social-Ecological Systems
Social-Ecological Systems
Risks & Vulnerability in Social-Ecological Systems
Examples of NbS to reduce risks​
Part II: Approaches for Vulnerability & Risk Assessment
OPERANDUM‘s approach to Risk & Vulnerability Assessment
  Impact chains
  Indicators
    Calculation process for vulnerability and risk assessment (Optional)
Challenges
The presentation material has been created by UNESCO together with the University of Glasgow, the University of Surrey, and ITC.

## Slide 4
Learning objectives
EU funded project GA no. 776848
4
After completing this training unit, you should be able to understand:
What Social-Ecological Systems are
How risks can be assessed in such systems
Why it is important in the context of Nature-based Solutions
OPERANDUM’s approach to Risk & Vulnerability Assessment:
  Impact chains
  Indicators
Notes: After completing this training unit, you should be able to understand:
What Social-Ecological Systems are
How risks can be assessed in such systems
Why it is important in the context of Nature-based Solutions
OPERANDUM’s approach to Risk & Vulnerability Assessment:
  Impact chains
  Indicators

## Slide 5
EU funded project GA no. 776848
Social-Ecological Systems and NbS
5
Social-ecological Systems (SES) are complex systems of people and nature, emphasizing that humans must be seen as a part of, not apart from, nature
SES consist of subsystems that interact to produce outcomes, which in turn feedback to the subsystems and SES
Understanding these systems, and their vulnerability and risks, are crucial for planning and implementation of nature-based solutions (NbS) for hydro-meteorological hazards
Sources: adapted from Berkes and Folke (1998); Minh Tu Nguyen et al. 2019
Notes: Social-ecological Systems (SES) are complex systems of people and nature, emphasizing that humans must be seen as a part of, not apart from, nature
SES consist of subsystems that interact to produce outcomes, which in turn feedback to the subsystems and SESs
Understanding these systems, and their vulnerability and risks, are crucial for planning and implementation of nature-based solutions (NbS) for hydro-meteorological hazards
The figure on the right shows the following:
General context: adaptation of agricultural systems to salinity intrusion in the Mekong Delta of Vietnam
The figure shows the interlinkage between the social sub-system and the ecological sub-system of a social-ecological system.
These systems are influenced by internal and external drivers of change. The former are linked to the locality; the latter to processes at the national or international levels
To provide solutions (in this case adaptation to salinity intrusion) one needs to understand all the components and their interactions.

## Slide 6
EU funded project GA no. 776848
Risk and Vulnerability
Risk
Exposure
Vulnerability)
,
,
= f
(Hazard
Characteristics of:
Natural hazards (for example: drought, flood, storm surge, landslide).​
and / or Technological hazards
People, ecosystems, infrastructure
6
Susceptibility, coping capacity, adaptive capacity, ecosystem robustness
Social, Economic,
Environmental, Institutional
Sources: Hagenlocher et al. (2018); IPCC (2022)
Notes: Risk is defined as the potential for adverse consequences resulting from the interaction of one or multiple (socio-) natural hazards with vulnerable elements of the SES exposed to these hazards
Risks are determined by the hazard, exposure and vulnerability
  See slide

## Slide 7
EU funded project GA no. 776848
What are natural hazards?
7
“The potential occurrence of a natural or human-induced physical event or trend that may cause loss of life, injury or other health impacts, as well as damage and loss to property, infrastructure, livelihoods, service provision, ecosystems and environmental resources.”
Source: NOAA GOES-16 satellite
Harvey 2017-08-25 2231Z.png
Public Domain
Source: Image by Jerry Coli from Pixabay
Free for commercial use
Source: Commander Mark Moran et al.
Katrina-new-orleans-flooding3-2005.jpg
Public Domain
Source: Sloan/USDA
Dust Bowl - Dallas, South Dakota 1936.jpg
Public Domain
Flooded city
Storm surge breaching coastal defences
Dust bowl (drought)
Hurricane
Source: IPCC (2022)
Notes: “The potential occurrence of a natural or human-induced physical event or trend that may cause loss of life, injury or other health impacts, as well as damage and loss to property, infrastructure, livelihoods, service provision, ecosystems and environmental resources.” (IPCC, 2022)

## Slide 8
EU funded project GA no. 776848
What is vulnerability?
8
Vulnerability is the propensity or predisposition to be adversely affected.
It encompasses a variety of concepts and elements, including sensitivity or susceptibility to harm and lack of capacity to cope and adapt.
Social
Social groups
Social networks
Mobility
Economic
Economic sectors
Critical infrastructure
Environmental
Ecosystem services
Biodiversity
Institutional
Land use planning
Effectiveness
Failure
Source: IPCC (2022)
Notes: Vulnerability is the propensity or predisposition to be adversely affected.
It encompasses a variety of concepts and elements, including sensitivity or susceptibility to harm and lack of capacity to cope and adapt, considering social, environmental, economic and institutional systems.

## Slide 9
EU funded project GA no. 776848
What is exposure, risk & impact?
9
Exposure: ‘’The presence of people; livelihoods; species or ecosystems; environmental functions, services, and resources; infrastructure; or economic, social, or cultural assets in places and settings that could be adversely affected”
Risk: "The potential for adverse consequences for human or ecological systems, recognising the diversity of values and objectives associated with such systems"
Impacts: "The consequences of realised risks on natural and human systems”
Houses exposed on the coastline
Photo: Fabrice Renaud
Source: IPCC (2022)
Notes: Exposure: ‘’The presence of people; livelihoods; species or ecosystems; environmental functions, services, and resources; infrastructure; or economic, social, or cultural assets in places and settings that could be adversely affected”
Risk: "The potential for adverse consequences for human or ecological systems, recognising the diversity of values and objectives associated with such systems"
Impacts: "The consequences of realised risks on natural and human systems”

## Slide 10
EU funded project GA no. 776848
Linking the concepts
10
Photo taken from USGS website
Source: IPCC (2014)
Notes: This figure is from the IPCC and it show how risk is composed, the link to socio-economic processes and to the climate and how all this is interlinked.
Note that this is climate change focused, but many hazards have no connection to climate change (earthquakes, volcanic eruptions, tsunamis, for example) and this needs to be noted.

## Slide 11
EU funded project GA no. 776848
NbS and Risks in Social-Ecological Systems
11
Nature-based Solutions could:
Reduce the magnitude and extent of hazards (e.g., floodplain restoration)
Reduce the exposure of SESs (e.g., buffer zone with marshes)
Reduce vulnerability of SESs (e.g., protected area, afforestation, adaptation policies)
Notes: Nature-based Solutions could:
Reduce the magnitude and extent of hazards (e.g., floodplain restoration)
Reduce the exposure of SESs (e.g., buffer zone with marshes)
Reduce vulnerability of SESs (e.g., protected area, afforestation, adaptation policies)

## Slide 12
EU funded project GA no. 776848
NbS approaches & benefits
Interventions for natural hazards
Hybrid Approach
12
Grey Approach
Natural Approach (Green/Blue)
Environmentally friendly, systemic and resource-efficient interventions which help build resilience and sustainability
Flexible and resilient with on-going urbanization and climate change
Multifunctional – they deliver manifold of services and benefits in the long term
Context-specific (which makes it difficult to design and evaluate) and maintenance can be costly
Single-objective oriented designs with limited co-benefits
Often expensive to build
Lack sustainability in a longer time frame, could influence the ecosystem
Their failure can have catastrophic impact, and provide a false sense of security
Nature-based Solutions (NbS)
Notes: There are different types of approaches that can be taken in terms of interventions for natural hazards: grey, natural (green/blue), and hybrid
This slide summarises some of the advantages why green/blue and hybrid solutions may have over gray approaches.
  See slide
Of course, decisions on DRR solutions need to be done individually to each case.

## Slide 13
EU funded project GA no. 776848
Protecting ourselves from natural hazards
13
Green approach
Mangrove, Mekong Delta,
Vietnam
Photos: Fabrice Renaud (2020)
Grey approach
Sea-dyke, Mekong Delta,
Vietnam
Hybrid approach
Mangrove and sea-dyke, Mekong Delta, Vietnam
Notes: When the aim is to protect from natural hazards, these 3 approaches could look like this (see slide)

## Slide 14
EU funded project GA no. 776848
Conserving or Restoring natural features
14
Artificial sand dune, Bellochio Beach, Italy
Photo: Fabrice Renaud/University of Glasgow (2022)
Guincho-Cresmina Dune System, Portugal
Photo: Fabrice Renaud (2016)
Notes: When conserving or restoring natural features, a natural approach is often used (green/blue) approach
For example:
  Artificial sand dune, Bellochio Beach, Italy
  Guincho-Cresmina Dune System, Portugal

## Slide 15
EU funded project GA no. 776848
Creating natural features in urban environments
15
Photo by Nazarizal Mohammad on Unsplash
Urban vegetation
Transformation of urban parks
Bishan-Ang Mo Kio Park
2008
2011
Photos by Pagodashophouse
Notes: When creating natural features in urban environments, a natural approach (green/blue) is often used in combination with grey elements – these are hybrid approaches
For example:
  Urban vegetation
  Transformation of urban parks
    The river is given more space to meander
    Flooding can now take place in the park and minimizes impact on inhabited areas

## Slide 16
EU funded project GA no. 776848
Effectiveness of NbS for V&R reduction
16
Risk levels for different NbS implementation phases rely on organic elements
Risk reduction can fluctuate seasonally
Source: Shah et al. (2020)
Notes: This figure shows risk levels on the y axis and time on the x axis. The aim of an NbS is to reduce risk to a given level (horizontal dashed line called "Max DRR capacity of NbS").
During the planning phase, there will obviously be no risk reduction. Once the NbS is implemented and depending on the nature of the NBS, risk will start reducing, first slowly, then more rapidly until it reaches full maturity and max DRR capacity. This is one of the factors that has to be considered when developing NbS, i.e. the time lag that might be much reduced with e.g. engineered structures.
The oscillations can be due to shorter term variability in the capacity of the NbS to reduce risks. For example, in temperate climate, vegetation cover may be less in winter and trees might also lose their leaves.
The two tail-ends of the graph show that with sustained monitoring and maintenance of the NbS with can keep the Max DRR function but without it, the NbS performance might degrade and cause problems in terms of DRR function.

## Slide 17
Takeaways: Natural Hazards, Risks & NbS in Social-Ecological Systems
EU funded project GA no. 776848
Social-ecological Systems (SES) are complex systems of people and nature, emphasizing that humans must be seen as a part of, not apart from, nature.
Risks are the potential for adverse consequences resulting from the interaction of one or multiple (socio-) natural hazards with vulnerable elements of the SES (Social, Environmental, Economic, Institutional) exposed to these hazards. Impacts are the consequences of realized risks on natural and human systems.
Nature-based Solutions for hydro-meteorological hazards can decrease intensity and frequency of hazards, thus, lowering probability of realisation of risks, by:
  Protection from natural hazards
  Conserving or restoring natural features
  Creating natural features
17
Next up: Approach for Vulnerability & Risk assessment
Notes: Social-ecological Systems (SES) are complex systems of people and nature, emphasizing that humans must be seen as a part of, not apart from, nature.
Risks are the potential for adverse consequences resulting from the interaction of one or multiple (socio-) natural hazards with vulnerable elements of the SES (Social, Environmental, Economic, Institutional) exposed to these hazards. Impacts are the consequences of realized risks on natural and human systems.
Nature-based Solutions for hydro-meteorological hazards can decrease intensity and frequency of hazards, thus, lowering probability of realisation of risks, by:
  Protection from natural hazards
  Conserving or restoring natural features
  Creating natural features

## Slide 18
Literature review
Identifying stakeholder priorities and needs
Conceptual framework for vulnerability and risk assessment of SES
Indicators for vulnerability and risk assessment
Determining impact chains
Past studies
Present requirements
Proposed V & R approach
FGD, Surveys
EU funded project GA no. 776848
OPERANDUM approach
18
A conceptual framework for vulnerability and risk (V&R) assessment of SES in the context of NbS was developed, by:
Notes: A conceptual framework for vulnerability and risk (V&R) assessment of SES in the context of NbS was developed, by:
  Considering past studies, through a literature review
  Considering present requirements, including
    Identifying stakeholder priorities and needs
    Determining impact chains
    This was done using focus group discussions and surveys.
The proposed vulnerability and risk (V&R) approach consists of a conceptual framework and indicators

## Slide 19
EU funded project GA no. 776848
Underrepresentation of Ecosystems in V&R Assessment
19
Most vulnerability and risk assessment frameworks that have used indicator-based approaches rely predominantly on social indicators - the role of ecosystems is under-represented:
  Of the 62 dimensions considered for drought vulnerability and risk assessments only 9 were related to the environment*
  39% of reviewed indicators for NbS focus on ecological sub-systems**
There is no frameworks specifically developed in the context of NbS to reduce hydro-meteorological risks
Sources: *Hagenlocher et al. (2019), **Shah et al. (2020), ***Sebesvari et al. (2016)
Comparison of the share of indicators dealing with the 4
vulnerability domains in SES-type papers vs. all reviewed papers***
Notes: Most vulnerability and risk assessment frameworks that have used indicator-based approaches rely predominantly on social indicators
This is logical in many ways, but as we know that we are dealing with social-ecological systems, a better representation of the latter is required.
The role of ecosystems is thus underrepresented:
  Of the 62 dimensions considered for drought vulnerability and risk assessments only 9 were related to the environment*
  39% of reviewed indicators for NbS focus on ecological sub-systems **
There is no frameworks specifically developed in the context of NBS to reduce hydro-meteorological risks

## Slide 20
Catchment
National
Sub-catchment
Provinces/ Municipalities
Ecological system
Social system
Interaction with regional and global scales
Influence of global climate change on hazards, exposure and vulnerability
change scenarios on SES
Influence of socioeconomic
SES attributes at various scales
Multiple hydro-meteorological hazards
(factors: magnitude, duration, extent, probability of occurrence)
Exposure of SES
Ecosystem exposure
Social system exposure
Vulnerability of SES
Ecosystem susceptibility
Ecosystem
robustness
Social susceptibility
Coping and adaptive capacity
Risk within NBS project site
Nature-Based Solutions
IUCN’s NBS principles
Nature conservation
Synergy with all solutions
Site-specific contexts
Transparency & participation
Diversity and evolve over time
Landscape scale
Trade-offs within SES
Policy integration
OPERANDUM framework for V&R assessment
EU funded project GA no. 776848
20
Reduce magnitude and extent of hazards (e.g., floodplain restoration)
Reduce vulnerability of SES (e.g., protected area, adaptation policies)
Reduce exposure of SES (e.g., buffer zone with marshes)
Source: Adapted from
Shah et al. (2020)
Notes: This slide shows the new framework developed within OPERANDUM and that aims to better capture the contribution of NbS to reduce risks. NbS can play that role by reducing hazard characteristics, exposure and the multiple dimensions of vulnerability, and on different scales. The framework is informed by the IUCN NbS principles.
We already looked at the definitions of hazards, exposure and vulnerability.
Important to note is that exposure considers both ecosystems and social systems.
Vulnerability of a SES includes the following:
  Susceptibility of ecosystems and social systems refers to the internal predisposition to suffer a certain degree of harm when exposed to a hazard (Sebesvari et al. 2016).
  Coping capacity is the ability of people, organizations, and systems, using available skills, resources, and opportunities, to address, manage, and overcome adverse conditions with the aim of achieving basic functioning in the short to medium term (Sebesvari et al. 2016).
  Adaptive capacity is the strengths, attributes, structures, resources available to an individual, community, society, or organization that can be used to prepare for and undertake actions to strategically reduce exposure, susceptibility and adverse impacts as well as enhance capacities in the long run (Sebesvari et al. 2016).
  Ecosystem robustness: The existence of a set of “strategic options" open to the ecosystem and the capability of the ecosystem to switch among multiple functionalities (Sebesvari et al. 2016).

## Slide 21
EU funded project GA no. 776848
V&R assessment method: Impact chains
21
Source: Hagenlocher et al. (2018); USGS
Notes: Impact chains show how a risk assessment can be carried out and how all the dimensions (exposure, hazards, vulnerability, impact) are interrelated

## Slide 22
EU funded project GA no. 776848
Example: Impact chain for OAL Greece
22
Notes: This example of OAL Greece is using the impact chain method in a simplified way
OALs are the selected hazard prone areas where NbS are implemented
Important to note is to always start with the risk: what risk are we trying to reduce and how is this risk generated?
Then the hazard and then the other components.
See slide for examples
This method thus shows the relationship between hazard, exposure, vulnerability and risks

## Slide 23
EU funded project GA no. 776848
V&R assessment method: NbS Indicators
23
Source: Shah et al. (2020)
Multiple hydro-meteorological hazards
(Factors: magnitude, duration, extent, probability of occurrence)
Exposure of SES
Vulnerability of SES
Social system exposure
Population exposed to floods (%)
Population exposed to drought (%)
Businesses exposed to hazards (%)
Ecosystem exposure:
Ecosystems exposed to floods (%)
Ecosystems exposed to drought (%)
Ecosystems exposed to landslide (%)
Ecosystem susceptibility:
Normalized Difference Vegetation Index (NDVI)
Biodiversity (Scoring or Index)
Ecosystem robustness:
Ecosystem Functionality Index (EFI scores)
Policies supporting biodiversity conservation
Government expenditure on environmental protection (%)
Proportion of drought tolerant crops (%)
Social susceptibility:
Number of income-generating activities per household;
Insurance coverage (% of population);
Dependency on road communication;
Agricultural crop production (tonnes/year);
Coping and adaptive capacity:
Government assistance (% of population covered);
Existence of hazard/vulnerability/risk maps (yes/no);
Irrigation technology and pumps (N/S);
Existence of adaptation policies/strategies (yes/no);
135 indicators in total, classified by risk components that should be selected according to SES context of OAL:
Notes: However, in order to get more insight into the real vulnerability risks, we need to use indicators
In OPERANDUM, 135 indicators in total were identified
These indicators are classified by risk components that should be selected according to SES context of OAL:
  Hazards
  Exposure
  Vulnerability
See slide for examples

## Slide 24
EU funded project GA no. 776848
Data collection for different indicators
24
Primary data
Collected by the researcher through surveys, interviews, etc. Examples:
Number of income-generating activities per household​
  Insurance coverage​
  Dependency on road communication​
  Participation in decision making ​
  Knowledge on climate / risks
Secondary data Existing information in databases, publications, books, government websites, etc. Examples:
Land use
Land exposed to hazards (e.g., flooding, landslide)
Buildings
Agricultural crop production
Road and rail network
NDVI (Normalized Difference Vegetation Index)
Policies related to conservation, adaptations, etc.
Notes: Data collection for different indicators
  Primary data is collected by the researcher through surveys, interviews, etc.
  For example:
    Number of income-generating activities per household​
      Insurance coverage​
      Dependency on road communication​
      Participation in decision making ​
      Knowledge on climate / risks
  Secondary data is existing information in databases, publications, books, government websites, etc.
  For example:
    Land use
    Land exposed to hazards (e.g., flooding, landslide)
    Buildings
    Agricultural crop production
    Road and rail network
    NDVI (Normalized Difference Vegetation Index)
    Policies related to conservation, adaptations, etc

## Slide 25
EU funded project GA no. 776848
Optional: Calculation process for V&R assessment (1/2)
25
Data collection for V&R indicators
Secondary sources
Normalization of indicator values (xi’)
Combine normalized indicators for each vulnerability domain (VD)
Ecosystem susceptibility
Primary surveys
Social susceptibility
Lack of ecosystem robustness
Lack of coping/adaptive capacities
Min-max linear normalization
Notes: Optional slide

## Slide 26
EU funded project GA no. 776848
Optional: Calculation process for V&R assessment (2/2)
26
Calculate susceptibility metric (VDSUS)
Calculate lack of capacities and robustness metric (VDCAR)
Calculate Hazards (H) and Exposure (ESES)) of SES
Calculate Risk of SES
Combined index score representing vulnerability of the SES (VUSES)
Risk = H * ESES * VUSES
Notes: Optional slide

## Slide 27
EU funded project GA no. 776848
Example: Indicator-based approach (OAL Italy)
27
Photo taken from USGS website
SES hazard, exposure, and risk scores for a 200-year flood event in OAL Italy for without and with NbS scenarios
Without NbS
With NbS
Notes: This is the preliminary risk assessment that was done for the Panaro river – OAL Italy – and how the hazard affects various municipalities in the region.
The row on the top are risk simulations without NbS and the bottom row is with NbS.
If you look column by column, you see that the hazard characteristics (flood depth and duration) are reduced with NbS in all municipalities, the exposure is reduced in most cases and the final risk is reduced everywhere with NbS in place.

## Slide 28
EU funded project GA no. 776848
Spatial aspects of V&R assessment
28
Area of interest for V&R assessment: Flood prone area
Sub-catchment scale
Provincial scale
Catchment scale
V&R assessment might need to consider different spatial scales
Social and ecological indicators can be related to different spatial scales
OAL Greece
Ecosystem: Catchment of Spercheios river Social system: Several municipalities across the OAL
Notes: However, V&R assessment might need to consider different spatial scales for indicators
For example, in OAL Greece, social and ecological indicators are related to different spatial scales
  Ecosystem is the whole catchment area of the river
  Social system are several municipalities across the OAL
  While the area of interest for the V&R assessment is only the flood prone area (indicated in red)

## Slide 29
EU funded project GA no. 776848
Spatial aspects of V&R assessment
29
V&R assessment might need to consider different spatial scales
Social and ecological indicators can be related to different spatial scales
OAL Austria
Very small area, local scale
Only few social and ecological indicators are related to local scales
Area of interest for V&R assessment: Landslide
Notes: In OAL Austria, the area relevant for V& R assessment is even smaller
The hazard – landslide – is in a very small area / local scale
While only a few social and ecological indicators are related to local scales

## Slide 30
EU funded project GA no. 776848
Temporal aspects of V&R assessment
30
V&R assessment needs to consider different temporal aspects (i.e., change over the years) related to:
  Hazard characteristics (e.g., rainfall, flood flow, water level, ground water level, etc.)
  Exposure of SES (e.g., population, exposed land)
  Vulnerability of SES (e.g., agricultural crop production, ground water level, dependent population)
Source: Shah et al. (2020)
Notes: V&R assessment needs to consider different temporal aspects (i.e., change over the years) related to:
  Hazard characteristics (e.g., rainfall, flood flow, water level, ground water level, etc.)
  Exposure of SES (e.g., population, exposed land)
  Vulnerability of SES (e.g., agricultural crop production, ground water level, dependent population)
In the figure, the fluctuation of risk and max DRR capacity of the NbS to reduce this risk, could change over time.

## Slide 31
EU funded project GA no. 776848
Temporal aspects of V&R assessment
31
Example: OAL UK
Temporal variability of protection effects provided by vegetation in case of NBS for reducing landslide.
Growth of vegetation over time will reduce risk in this area.
Effectiveness of protection vegetation (or change of risk) could be assessed by monitoring indicators.
Hazard (e.g., landslide caused by heavy rainfall) Indicator: magnitude of landslide
Exposure of SES
(e.g., land exposed to landslide)
Indicator: proportion of land exposed to landslide (%)
Vulnerability of SES
Indicators for ecosystem susceptibility: NDVI,
Soil erosion rate
Risk
Notes: Example: OAL UK
  Temporal variability of protection effects provided by vegetation in case of NBS for reducing landslide.
  Growth of vegetation over time will reduce risk in this area.
  Effectiveness of protection vegetation (or change of risk) could be assessed by monitoring indicators.

## Slide 32
EU funded project GA no. 776848
Challenges for Vulnerability & Risk assessment
Finding suitable indicators for V&R assessment in the contexts of NbS
Data availability for indicators (in various spatial and temporal scales)
Primary data collection for indicators could be challenging, but is vital, especially with implementation in small areas
Implementation and functioning of NbS may take a long time, and monitoring of V&R indicators is required to determine risk reduction
32
Notes: Finding suitable indicators for V&R assessment in the contexts of NBS
Data availability for indicators (in various spatial and temporal scales)
Primary data collection for some indicators could be challenging, for example in a pandemic situation, but it is vital in case of risk assessment in very small area. Online/ remote surveys via email, phone or post could be applied.
Since implementation and functioning of NbS may take long time, long-term monitoring of V&R indicators would be required to compare the impact of NbS on risk reduction. Proving cost and logistics could be challenging.

## Slide 33
Takeaways: Approach for Vulnerability & Risk assessment
EU funded project GA no. 776848
Most vulnerability and risk assessment frameworks that have used indicator-based approaches rely predominantly on social indicators - the role of ecosystems is under-represented.
OPERANDUM developed a framework for V&R assessment for Nature-based Solutions in Social-Ecological Systems, based on the 8 IUCN principles for NbS. Methods include impact chains, and indicator-based assessment.
Spatial and temporal aspects need to be taken into account in V & R assessment. Challenges to this type of assessment include data availability and resources to monitor NbS long-term.
33
Notes: Most vulnerability and risk assessment frameworks that have used indicator-based approaches rely predominantly on social indicators - the role of ecosystems is under-represented.
OPERANDUM developed a framework for V&R assessment for Nature-based Solutions in Social-Ecological Systems, based on the 8 IUCN principles for NbS. Methods include impact chains, and indicator-based assessment.
Spatial and temporal aspects need to be taken into account in V & R assessment. Challenges to this type of assessment include data availability and resources to monitor NbS long-term.

## Slide 34
Take home messages
EU funded project GA no. 776848
34
Social-ecological Systems (SES) are complex systems of people and nature, emphasizing that humans must be seen as a part of, not apart from, nature.
OPERANDUM developed a framework for V&R assessment for Nature-based Solutions in Social-Ecological Systems. Methods include impact chains, and indicator-based assessment.
Spatial and temporal aspects need to be taken into account in V & R assessment. Challenges to this type of assessment include data availability and resources to monitor NbS long-term.
Notes: Social-ecological Systems (SES) are complex systems of people and nature, emphasizing that humans must be seen as a part of, not apart from, nature.
OPERANDUM developed a framework for V&R assessment for Nature-based Solutions in Social-Ecological Systems. Methods include impact chains, and indicator-based assessment.
Spatial and temporal aspects need to be taken into account in V & R assessment. Challenges to this type of assessment include data availability and resources to monitor NbS long-term.

## Slide 35
EU funded project GA no. 776848
Further reading
35
OPERANDUM
Renaud et al. (2019) Deliverable 6.1: Review on vulnerability and risk assessment specific to Nature Based Solutions. H2020 OPERANDUM project. Link.
Shah et al. (2019) Deliverable 6.2: Vulnerability and risk assessments of socio-ecological systems (SES): conceptual framework, impact chains and indicators. H2020 OPERANDUM project. Link.
Vulnerability & Risk Assessment
Hagenlocher et al. (2018). Vulnerability and risk of deltaic social-ecological systems exposed to multiple hazards. Science of the total environment, 631, 71-80. Link.
IPCC (2022). Annex II: Glossary [Möller, V., et al. (eds.)]. In: Climate Change 2022: Impacts, Adaptation and Vulnerability. Contribution of Working Group II to the Sixth Assessment Report of the Intergovernmental Panel on Climate Change [Pörtner H.-O., et al. (eds.)]. Cambridge University Press, Cambridge, UK and New York, NY, USA, pp. 2897–2930. Link.
Shah et al. (2020). A review of hydro-meteorological hazard, vulnerability, and risk assessment frameworks and indicators in the context of nature-based solutions. International journal of disaster risk reduction, 50, 101728. Link.
Nature-based Solutions
IUCN (2016). Nature-based solutions. Link
Notes: Disclaimers:
- The information, photos, figures and data used are created in the OPERANDUM project, unless another source is mentioned.
- Editable versions of all training units are available upon request. Please contact OPERANDUM by filling out the contact form on the website: https://www.operandum-project.eu/contact/

## Slide 36
Next steps
EU funded project GA no. 776848
36
Unit 1: NbS Concepts and Approaches
Unit 2: Good Practices from Open Air Laboratories
Unit 3: Stakeholder Engagement and Co-Creation
Unit 4: Assessing Risks in Socio-Ecological Systems
Unit 5: NbS Selection and Engineering
Unit 6: NbS Modelling and Monitoring
Unit 7: NbS Policy Context and Permitting Paths
Unit 8: Promoting NbS Uptake and Public Acceptance
Unit 9: Replication and Business Uptake
Unit 10: GeoIKP – NbS Platform

## Slide 37
EU funded project GA no. 776848
Training 4: Assessing Risks in Socio-Ecological Systems
Thank you!
Find us on: