## Slide 1
Nature-based Solutions for hydro-meteorological hazards
Training 5: NbS Selection and Engineering
EU funded project GA no. 776848
Notes: Disclaimers:
- The information, photos, figures and data used are created in the OPERANDUM project, unless another source is mentioned.
- Editable versions of all training units are available upon request. Please contact OPERANDUM by filling out the contact form on the website: https://www.operandum-project.eu/contact/

## Slide 2
EU funded project GA no. 776848
About OPERANDUM
4-year, European project, with 26 international partners
Sustainable solutions based on nature - Nature-based Solutions - to adapt to extreme weather events
Demonstrate the tools and methods for the validation of these solutions in 10 Open Air Laboratories (OALs)
2
Open Air Labs Austria, Finland, Germany, Greece, Ireland, Italy, Scotland (UK), Australia, China, Hong Kong (China)
Notes: OPERANDUM is a European project that researches sustainable solutions based on nature to adapt to extreme weather events. We call these type of solutions 'nature-based solutions’.
In the project, solutions are demonstrated for different types of hydro-meteorological hazards in 10 open air laboratories.
The project is a collaboration between 26 partners in 14 countries – covering universities, NGOs, and SMEs – over 4 years.

## Slide 3
Training Unit 5 at a glance
EU funded project GA no. 776848
3
Part I: Engineering approach to design NbS
Problem definition
Identification of the input parameters
Solution behaviour modelling
Calculations and checks
Analysis and assessment of calculation results
Part II: NbS design process & implementation
Examples from OPERANDUM
Notes: Part I: Engineering approach to design NbS
Problem definition
Identification of the input parameters
Solution behaviour modelling
Calculations and checks
Analysis and assessment of calculation results
Part II: NbS design process & implementation
Examples from OPERANDUM
These training materials are developed by UNESCO in collaboration with Rina-C and the University of Bologna

## Slide 4
Learning objectives
EU funded project GA no. 776848
4
After completing this training unit, you should be able to understand:
How an engineering process is managed
How the engineering method can be applied to NbS
The application of quantitative approach vs the qualitative approach in the definition of NbS
How the evaluate the reliability of a NbS
Starting with the actual implementation: the OPERANDUM approach of engineering of a new NbS
Notes: After completing this training unit, you should be able to understand:
How an engineering process is managed
How the engineering method can be applied to NbS
The application of quantitative approach vs the qualitative approach in the definition of NbS
How the evaluate the reliability of a NbS
Starting with the actual implementation: the OPERANDUM approach of engineering of a new NbS

## Slide 5
EU funded project GA no. 776848
Nature-based Solutions in OPERANDUM
5
Deep rooting plants, bioswales, bioretention, green rooftops, grazing of the foreland
Natural water retention measures and water storage management
Sealing streams and channels, optimized forest management, snow accumulation control, drainage trenches, live fascines and brush layers, live pole draining, live crib walls and slope grids.
Constructed wetlands, overland flow area, sedimentation ponds and pits, peak flow control structures, submerged dams, riparian buffer zones, continuous cover forestry and a decision support protocol.
Artificial dune, marine sea grasses
Flooding
Coastal Erosion
Nutrient and sediment loading
Drought
Landslide
Notes: Nature-based Solutions to hydro-meteorological hazards that have been implemented in OPERANDUM Open Air Laboratories
  See slide for overview

## Slide 6
EU funded project GA no. 776848
Approach for engineering NbS in OPERANDUM
6
Traditional engineering approaches are intended as processes based on data and calculations rather than on empirical/expert judgement approaches.
To make the 25 solutions developed within OPERANDUM easily applicable and compliant with traditional engineering approaches, an engineering approach to design NbS was developed.
Engineering approach to design NbS
Notes: How are these solutions implemented?
Traditional engineering approaches are intended as processes based on data and calculations rather than on empirical/expert judgement approaches.
To make the 25 solutions developed within OPERANDUM easily applicable and compliant with traditional engineering approaches, an engineering approach to design NbS was developed.
  This approach consists of 5 steps:
    Problem definition
    Identification of the input parameters
    Solution behaviour modelling
    Calculations and checks
    Analysis and assessment of calculation results

## Slide 7
EU funded project GA no. 776848
1. Problem definition
7
What is the problem to be solved?
How can the problem be solved?
Which is the best location to deploy the solution in order to better tackle the problem?
When is the best time for the deployment of the solution?
Notes: This refers to the general understanding of a specific event or process which generates negative impacts on a given area. The target is the definition of the problem to be solved or, in a wider sense, the aspects to be improved, and the comprehension of the main causes involved in the event in order to define the possible solutions able to mitigate their negative effects.
Once the general context of the problem is defined, a solution strategy can be defined, evaluating the potential best ways to mitigate the negative effects related to such problem. Of course, a problem may have many different solutions and to select the most appropriate one, the boundary conditions (external factors such as economic resources availability, timing of the solution deployment, environmental impacts, regulatory framework and logistics) are important. These boundary conditions influence indirectly the effectiveness of the solution: for instance, an ideal optimal solution could be too expensive or have a huge impact on the local context; for this reason an apparently less efficient solution could be preferred, considering a complex balances between pros and cons.
According to different boundary conditions, the scale, size and location of the solution may change significantly. In addition, two different approaches affecting the selection of the best location can be followed:
    an active system solution targeting the actions generating the negative impact
    a passive system solution targeting the negative effects only (e.g. local protection or reinforcement).
  In this first step the rough layout for the solution deployment can be defined, while the final and detailed configuration can be determined only downstream of the detailed analysis and calculations
A correct schedule is a very relevant aspect because of natural and/or anthropic actions changing during the year (e.g. seasonal variations of natural events or different anthropic presence) that may influence the feasibility or the effectiveness of the proposed solution.

## Slide 8
EU funded project GA no. 776848
2. Identification of input parameters
8
Possible input parameters for defining the configuration of the solution (non-exhaustive and context-specific).
Example of parameters to consider for a coastal solution:
  Topographical conditions (or bathymetric conditions when required);
  Hydraulic conditions (e.g., river flow, meteocean conditions, water levels, permeability etc.);
  Geotechnical parameters (e.g., stratigraphy and geotechnical parameters of the in situ soils);
  Natural conditions (e.g., presence and characteristics of vegetation and fauna);
  Anthropic variables (e.g., presence of interfering structures, underground services, anthropic activities that may be relevant for the design).
Engineering approach to design NbS
Notes: See slide.
Bathymetric conditions refer to the submerged topography and physiographic features of ocean and sea bottoms
Metocean refers to the of meteorology and (physical) oceanography

## Slide 9
EU funded project GA no. 776848
3. Solution behaviour modelling
9
The overall site conditions and the solutions selected in the previous steps have now to be linked by:
  One or more models representing the global behavior of the solution in the actual environment.
The way the actual parameters are translated in a model - in terms of action and capacity of the system - is the main critical aspect of this step.
Types of models and their application used in OPERANDUM
10
8
6
4
2
Notes: This step is the conceptual core of the approach.
The overall site conditions and the solutions selected in the previous steps have now to be linked by:
  One or more models representing the global behavior of the solution in the actual environment (a model is an analytical representation of the reality.)
  These could be climate models, hydraulic models, etc. (see slide)
The way the actual parameters are translated in a model in terms of action and capacity of the system is the main critical aspect of this step.
In some cases, the model has been already defined in literature and is standardized by regulations, literature studies and guidelines. In other cases, modelling through specialistic software may allow to simulate the interaction between natural actions and the system.

## Slide 10
EU funded project GA no. 776848
4. Calculations and checks
10
An appropriate model of the system is be developed, correctly representing the structure or system, the materials used, and the acting forces.
The model could be a simplified model, defined by formulas implemented for instance through an excel sheet, or a more complex model, built using specialistic software.
  In the preliminary phase, simplified formulas or simplified models may be used to define the general geometry.
  In the next stages the level of detail should increase, reaching also very high level of detail and accuracy, in case of critical aspects to be studied.
Engineering approach to design NbS
Notes: An appropriate model of the system is be developed, correctly representing the structure or system, the materials used, and the acting forces.
The model could be a simplified model, defined by formulas implemented for instance through an excel sheet, or a more complex model, built using specialistic software.
  In the preliminary phase, simplified formulas or simplified models may be used to define the general geometry.
  In the next stages the level of detail should increase, reaching also very high level of detail and accuracy, in case of critical aspects to be studied.

## Slide 11
EU funded project GA no. 776848
5. Analysis and assessment of calculation results
11
The results of the calculation and checks phase have to be analysed in detail.
To reach a longer lifespan of the solution, specific care should be given on the maintenance and monitoring aspects.
Another way to validate the effectiveness of installed solution is the implementation of a monitoring system and comparing these values to threshold levels.
The combination of good monitoring plan and maintenance systems allows to identify possible issues in the early stages and consequently to intervene promptly repairing the failures.
Photo: OAL Austria
Notes: The results of the calculation and checks phase have to be analysed in detail
To reach a longer lifespan of the solution, specific care should be given on the maintenance and monitoring aspects.
Another way to validate the effectiveness of installed solution is the implementation of a monitoring system, and comparing these values to threshold levels.
For this reason, durability aspects should be studied already during the design stages, providing a maintenance plan, describing the schedule and type of inspections and maintenance interventions.
The combination of good monitoring plan and maintenance systems allows to identify possible issues in the early stages and consequently to intervene promptly repairing the failures.

## Slide 12
Takeaways: Engineering approach to design NbS
EU funded project GA no. 776848
The engineering approach defined for the NbS is conceptually no different from others engineering problems
NbS design approach consists of:
  Problem definition
  Identification of the input parameters
  Solution behaviour modelling
  Calculations and checks
  Analysis and assessment of calculation results
To be able to comply with codes and standards and fulfil the market demands an engineering approach is a key aspect in the adoption of NbS.
12
Next up: NbS design process & implementation
Notes: The engineering approach defined for the NbS is conceptually no different from others engineering problems
NbS design approach consist of :
  Problem definition
  Identification of the input parameters
  Solution behaviour modelling
  Calculations and checks
  Analysis and assessment of calculation results
To be able to comply with codes and standards and fulfil the market demands an engineering approach is a key aspect in the adoption of NbS.

## Slide 13
EU funded project GA no. 776848
Examples of Nature-based Solutions in OPERANDUM
13
Deep rooting plants, bioswales, bioretention, green rooftops, grazing of the foreland
Natural water retention measures and water storage management
Sealing streams and channels, optimized forest management, snow accumulation control, drainage trenches, live fascines and brush layers, live pole draining, live crib walls and slope grids.
Constructed wetlands, overland flow area, sedimentation ponds and pits, peak flow control structures, submerged dams, riparian buffer zones, continuous cover forestry and a decision support protocol.
Artificial dune, marine sea grasses
Flooding
Coastal Erosion
Nutrient and sediment loading
Drought
Landslide
Example 1: OAL Italy
Example 2: OAL Ireland
Example 3: OAL Greece
Example 4: OAL Austria
Notes: Nature-based Solutions to hydro-meteorological hazards that have been implemented in OPERANDUM Open Air Laboratories
We will now look at examples on:
  NbS for coastal erosion from OAL Italy
  NbS for flooding from OAL Ireland & OAL Greece
  NbS for landslides from OAL Austria

## Slide 14
EU funded project GA no. 776848
Example 1: Artificial dune (OAL Italy)
14
Definition of the engineering problem
To reduce coastal erosion impacting on a protected area, by means of a passive erosion protection system, consisting in a vegetated embankment realized using natural materials.
2. Identification of the required input parameters
Topographical conditions, meteocean conditions, bathymetric conditions, geotechnical parameters, seismic parameters, vegetation conditions, anthropic variables, soil thrust, wave loads, anthropic loads, seismic actions, etc.
3. Model of the solution behaviour, in terms of engineering/calculations
Slope stability, structural strength of materials, geotechnical stability of the bulkhead.
4. Detailed calculations and check Use of tools such as Excel spreadsheets, specialistic software (e.g. SLIDE, Paratie Plus)
5. Calculation results and interpretation
Definition of final geometric features and position of the dune, maintenance and monitoring plan, expected behaviour of the beach protected by the dune, etc.
Notes: Definition of the engineering problem
To reduce coastal erosion impacting on a protected area, by means of a passive erosion protection system, consisting in a vegetated embankment realized using natural materials.
2. Identification of the required input parameters
Topographical conditions, meteocean conditions, bathymetric conditions, geotechnical parameters, seismic parameters, vegetation conditions, anthropic variables, soil thrust, wave loads, anthropic loads, seismic actions, etc.
3. Model of the solution behaviour, in terms of engineering/calculations
Slope stability, structural strength of materials, geotechnical stability of the bulkhead.
4. Detailed calculations and check Use of tools such as Excel spreadsheets, specialistic software (e.g. SLIDE, Paratie Plus)
5. Calculation results and interpretation
Definition of final geometric features and position of the dune, maintenance and monitoring plan, expected behaviour of the beach protected by the dune, etc.

## Slide 15
EU funded project GA no. 776848
Example 1: Artificial dune (OAL Italy)
15
Model of the solution behaviour (using inputs identified in Step 2)
Slope stability, structural strength of materials, geotechnical stability of the bulkhead
Detailed calculations and check Use of tools such as Excel spreadsheets, specialistic software (e.g. SLIDE, Paratie Plus)
Notes: Model of the solution behaviour (using inputs identified in Step 2)
  Includes Slope stability, structural strength of materials, geotechnical stability of the bulkhead of the design of the artificial dune
Detailed calculations and check
  Use of tools such as Excel spreadsheets, specialistic software (e.g. SLIDE, Paratie Plus)

## Slide 16
EU funded project GA no. 776848
Example 1: Artificial dune (OAL Italy)
16
Step 5: Calculation results and interpretation
Definition of final geometric features and position of the dune, maintenance and monitoring plan,
expected behaviour of the beach protected by the dune, etc.
Patent filed: Coastal protection barrier, Geotube
Artificial dune ‘Lido di Volano’
Notes: Step 5: Calculation results and interpretation
  Definition of final geometric features and position of the dune, maintenance and monitoring plan, expected behaviour of the beach protected by the dune, etc.
  A patent was filed for the NbS design, in particular for the Coastal protection barrier, and Geotube for this barrier

## Slide 17
EU funded project GA no. 776848
Example 1: Artificial dune (OAL Italy)
17
Notes: Photos of the construction of the NbS

## Slide 18
EU funded project GA no. 776848
Example 1: Complimentary seagrass belt to support artificial dune (OAL Italy)
18
Integrated efficiency of the dune and seagrass were also investigated with simulations for both present (2010-2019) and future scenario (2040-2049)
Notes: In addition, Integrated efficiency of the dune and seagrass were also investigated with simulations for both present (2010-2019) and future scenario (2040-2049)
Seagrass has the potential to decrease the energy of the waves and the storm surge
The plan is to have a coastal strip occupied by seagrass parallel to the coast, at about 3-5 meters depth
In this region the seagrass will have an effect on the formulation of the currents and the waves.

## Slide 19
EU funded project GA no. 776848
Example 2: Smart IoT Green Roof (OAL Ireland)
19
1. Definition of the engineering problem
Reduction of rainfall-fed runoff to control floods in an urban environment using green roofs.
Enhancement of the green roof NbS with technology to have a hybrid NbS in the form of a smart IoT green roof.
2. Identification of the required input parameters
Meteorological variables (rainfall, temperature, wind speed, solar radiation, humidity), types and nature of vegetation used, soil moisture content.
All the parameters are monitored and visualised in real time with smart IoT technology.
3. Model of the solution behaviour, in terms of engineering/calculations
Estimation of reduction in runoff due to green roofs using modelling as well as monitoring approaches.
The modelling approach requires a relationship between rainfall, runoff, soil moisture content and relative humidity, while the monitoring approach will measure the runoff with and without the green roofs for comparison.
Notes: 1. Definition of the engineering problem
Reduction of rainfall-fed runoff to control floods in an urban environment using green roofs. Enhancement of the green roof NbS with technology to have a hybrid NbS in the form of a smart IoT green roof.
2. Identification of the required input parameters
Meteorological variables (rainfall, temperature, wind speed, solar radiation, humidity), types and nature of vegetation used, soil moisture content. All the parameters are monitored and visualised in real time with smart IoT technology.
3. Model of the solution behaviour, in terms of engineering/calculations
Estimation of reduction in runoff due to green roofs using modelling as well as monitoring approaches. The modelling approach requires a relationship between rainfall, runoff, soil moisture content and relative humidity, while the monitoring approach will measure the runoff with and without the green roofs for comparison.
The area of OAL Ireland in Dublin is indicated on the map. In this area, a lot of tech companies have offices. The area is surrounded by River Dodder in the west and River Liffey in the north, while the Irish sea covers the eastern boundary.

## Slide 20
EU funded project GA no. 776848
Example 2: Smart IoT Green Roof (OAL Ireland)
20
4. Detailed calculations and check
Runoff from a storm event is equal to the amount of rainfall without the losses.
The primary loss is evaporation/evapotranspiration.
In situations where the green roof is absent, evapotranspiration won't be present, while presence of green roof will contribute to considerable evapotranspiration.
5. Calculation results and interpretation
Based on the modelling, the percentage of runoff reduction from a building can be estimated.
Accuracy of the model can be evaluated using monitored data.
Notes: 4. Detailed calculations and check
Runoff from a storm event is equal to the amount of rainfall without the losses.
The primary loss is evaporation/evapotranspiration.
In situations where the green roof is absent, evapotranspiration won't be present, while presence of green roof will contribute to considerable evapotranspiration.
5. Calculation results and interpretation
Based on the modelling, the percentage of runoff reduction from a building can be estimated.
Accuracy of the model can be evaluated using monitored data.
In this case, surface runoff and groundwater discharge was measured at 2 potential sites

## Slide 21
EU funded project GA no. 776848
Example 2: Smart IoT Green Roof (OAL Ireland)
21
Notes: A green roof was implemented to reduce surface runoff and groundwater discharge - the roof absorbs rainwater – and provides benefits such as providing insulation and temperature control, habitat promotion and enhancement of the aesthetics of the landscape.
In order to build a green roof the following structure is needed with different elements and layers (see slide)
The sensors on the roof will measure the following variables:
  Rainfall
  Temperature
  Humidity
  Solar radiation
  Wind speed and direction
  Soil moisture
  River level and flow
  Vapor and barometric pressure
  Soil temperature and conductivity

## Slide 22
EU funded project GA no. 776848
Example 3: Retention basins (OAL Greece)
22
Notes: See video

## Slide 23
EU funded project GA no. 776848
Example 4: Sealing of leaky streams (OAL Austria)
23
1. Definition of the engineering problem
The OAL landslide activity has been analyzed in detail, evaluating that the main driver of the landslide is the presence of incoming groundwater at the lower part of the slope.
2. Identification of the required input parameters
Hydraulic conductivity, discharge, initial water level, regolith depth, slope angle, specific storage, soil water content and characteristic curve.
3. Model of the solution behaviour, in terms of engineering/calculations
For representing the governing infiltration processes at the NbS-site a 1D pore pressure diffusion model was applied. These two options were exploited to reproduce the conditions with and without the implemented nature-based solution (bio-degradable multi-component clay liner as an impermeable layer).
The model allows to estimate the proportion of water prevented from deep seepage and hence, the improvements due to the NbS compared to the original conditions.
4. Detailed calculations and check
The dynamic model was applied in the experiment OAL site for the duration of one day with hourly outputs of pore pressure distributions over the considered depth.
5. Calculation results and interpretation
The comparison of the original conditions at the experiment site in OAL-AT and the conditions after implementing a prototype of the bio-degradable multi-component clay liner generally show the expected results.
However, the model is based on assumptions considering homogeneous, anisotropic material characteristics and does not account for preferential flow. In the light of ongoing investigations and monitoring activities a more accurate comparison may be achieved.

## Slide 24
EU funded project GA no. 776848
Example 4: Sealing of leaky streams (OAL Austria)
24
Selected slope profile, interpreted sliding surface and groundwater table
Sensitivity analysis indicating the influence of cohesion, friction angle,
specific weight and groundwater level on the utilisation degree
Notes: Selected slope profile, interpreted sliding surface and groundwater table (left)
Sensitivity analysis indicating the influence of cohesion, friction angle, specific weight and groundwater level on the utilisation degree (right)
These models show that further reduction of the groundwater level reduces the utilization degree, would increase slope stability
For this reason, the intervention of sealing leaky streams was implemented, as these would decrease the groundwater level

## Slide 25
EU funded project GA no. 776848
Example 4: Sealing of leaky streams (OAL Austria)
26
Notes: The selected options were repeatedly discussed and decided on with the involved stakeholders:
Nature-based sealing of leaky streams and channels
  Infiltration of surface water in leaky streams contributes to groundwater recharge, the main driver of the landslide. Common engineering practices and mitigation measures typically include synthetic materials prevailing in the subsurface.
  In OAL-Austria nature-based alternatives are tested including a fully bio-degradable clay liner. The supporting fleece material vanishes over time, but the impermeable clay layer persists and guarantees the desired effects over long time spans.
Optimization of the forest management with regard to the hydrological effects on the landslide. Currently, the forest in OAL Austria is mostly composed of spruce (Picea abies) with varying density and age distribution. Simulation scenarios are developed for comparing the hydrological effects of the current forest conditions and optimized conditions concerning stand structure and species compositions.
  It is expected that the hydrological effects of an optimized forest management can help decreasing the hydrological driver of the landslide.
Preliminary monitoring results (e.g. distribution of snow cover in early 2019) revealed that the use of snow fences may not yield the desired effects due to minor wind drift effects, as observed. Drainage trenches along forest roads have been renewed in 2019, further improvement could follow if required.

## Slide 26
Take home messages: NbS Selection and Engineering
EU funded project GA no. 776848
The application of the engineering approach to NbS is quite diverse, and the workflow for designing NbS illustrated in Part I can be applied to very different solutions. Moreover:
  Approaches from academic literature can be adapted to the NbS design by changing some parameters.
  Tests, data collection and monitoring can robustly support the NbS engineering.
  Non-traditional engineering solutions can also benefit from an NbS engineering approach.
  In the engineering of NbS it is important to be creative and think outside the box.
An engineering approach will facilitate the actual implementation of the solution you are fostering in the next stages (e.g. permitting, design, bid, construction).
The application of an engineering approach is something needed by the market to accelerate the adoption of NbS. Even if you are not directly involved in actual engineering activities it is important to understand how the engineering process is working.
27

## Slide 27
EU funded project GA no. 776848
Further reading
OPERANDUM
Spyrou et al. (2018) Deliverable 5.2a: Multi-impacts assessment for OAL and NBS. H2020 OPERANDUM project. Link.
GeoIKP Best Practices. H2020 OPERANDUM project. Link.
OAL Italy (Artificial dune)
Bishop A.W., 1955, The use of the Slip Circle in the Stability Analysis of Slopes, Géotechnique, Volume 5, Issue 1, 01 March 1955 , pages 7 –17.
Boccotti, P., 1997. Idraulica marittima. UTET.
DM 17/01/2018 “Norme Tecniche per le Costruzioni”;
EN 1997-1, 2004, Eurocode 7: Geotechnical design - Part 1: General rules (The European Union Per Regulation 305/2011, Directive 98/34/EC, Directive 2004/18/EC);
Istruzioni per l’applicazione delle Norme tecniche per le costruzioni di cui al DM 17/01/2018 – Circolare 21 gennaio 2019 n°7.
Grisogono B. and Belušić D., 2009, A review of recent advances in understanding the meso- and microscale properties of the severe Bora wind. Tellus A, 61 (2009), pp. 1-16.
Lancellotta R., 2004, Geotecnica, Zanichelli, Bologna.
Lionello et al., 2012,. Severe marine storms in the Northern Adriatic: Characteristics and trends. Physics and Chemistry of the Earth, Parts A/B/C. 40. 93-105. 10.1016/j.pce.2010.10.002.
Mendoza E.T. and Jimenez J.A., 2004. Factors controlling vulnerability to storm impacts along the Catalonian coast. Proceedings International Conference of Coastal Engineering, Lisbon, pp. 3087-3099.
Mononobe N., 1929, Earthquake-proof construction of masonry dams, Proc. of World Engineering Conference, vol.9, p.275.
Okabe S., 1926, General theory of earth pressure, Journal of Japanese Society of Civil Engineering, Vol 12 No.1.
Pasarić Z., Belušić D., Chiggiato J., Orographic effects on meteorological fields over the Adriatic from different models. J. Marine Syst., 78 (2009), pp. S90-S100.
Rankine W.J.M., 1857, On the stability of loose earth, Philosophical transactions, Royal Society, London.
Rapporto IdroMeteoClima Emilia-Romagna, 2019, Arpae in press.
Spencer, E., 1967, A method of analysis of the stability of embankments assuming parallel inter-slice forces, Geotechnique, 17(1), 11–26.
Vesic A., 1975, Bearing capacity of shallow foundations, Foundation Engineering Handbook, New York.
27

## Slide 28
EU funded project GA no. 776848
Further reading
OAL Austria (Sealing of leaky streams)
Iverson R.M., 2000, Landslide triggering by rain infiltration: Water Resources Research, 36(7), 1897–1910.
Savage W.Z., Godt J.W., and Baum R.L., 2004, Modelling time-dependent aerial slope stability, in Lacerda, W.A., Erlich, M., Fontoura, S.A.B., and Sayao, A.S.F., eds., Landslides—Evaluation and stabilization, Proceedings of the 9th International Symposium on Landslides: London, A.A. Balkema Publishers, 1, 23–36.
Srivastava R., and Yeh T.-C. J., 1991, Analytical solutions for one-dimensional, transient infiltration toward the water table in homogeneous and layered soils: Water Resources Research, 27, 753–762.
Van Genuchten M. T., 1980, A closed‐form equation for predicting the hydraulic conductivity of unsaturated soils. Soil science society of America journal, 44(5), 892-898.
Zieher et al., 2017, Water content dynamics at plot scale - comparison of time-lapse electrical resistivity tomography monitoring and pore pressure modelling, Journal of Hydrology. 544, 195 - 209.
28
OAL Greece (Retention basins)
Acharya, M., 2018, Analytical Approach to Design Vegetative Crib Walls. Geotech Geol , Volume 36, p. 483–496.
Balzan et al., 2020, Building capacity for mainstreaming nature-based solutions into environmental policy and landscape planning. Research Ideas and Outcomes 6: e58970.
Bella et al., 2017. An Innovative Bio-Engineering Retaining Structure for Supporting Unstable Soil. Journal of Rock Mechanics and Geotechnical Engineering, Volume 9, pp. 247-259.
Chrisanthou, V., 2015, "Rivers of Hydraulics and Technical Works". s.l.:Hellenic Academic Libraries.
Cohen-Shacham E, Walters G, Janzen C, Maginnis S (2016) Nature-based solutions to address global societal challenges. IUCN.
Dadson, S., 2017, A restatement of the natural science evidence concerning catchment-based ‘natural’ flood management in the UK.
Debele et al., 2019, Nature-based solutions for hydro-meteorological hazards: Revised concepts, classification schemes and databases. Environmental Research, volume 179 part B.
DHI MIKE HYDRO RIVER User Manual; Danish Hydraulic Institute: Copenhagen, 2020.
DHI. MIKE SHE User Manual; Danish Hydraulic Institute: Copenhagen, Denmark, 2020.
Dikau, R., 1989, The application of a digital relief model to landform analysis in geomorphology. In: Raper JF (ed) Three Dimensional Applications in Geographical Information Systems, Taylor and Francis, London, 51-77 p.
ERGOSE, 2003, Environmental Impact Study, measures to prevent flood damage in Spercheios river basin, September 2003.
European Environment Agency (EEA), 2020, Copernicus Land Monitoring Service. CORINE Land Cover 2012, Version 2020_20u1.
Hargreaves, G. H., & Samani, Z. A., 1985, Reference Crop Evapotranspiration from Temperature. Applied Engineering in Agriculture, 1(2), 96–99.
HCMR, 2015. Development of an integrated management system for basin, coastal and marine zones. Results of the annual evaluation of ecological quality of each water body [in Greek]. Hellenic Centre for Marine Research, Anavyssos
Hersbach et al., 2020, The ERA5 global reanalysis. Q J R Meteorol Soc. 2020; 146: 1999– 2049. https://doi.org/10.1002/qj.3803
IPCC, 2018, Impacts, Adaptation, and Vulnerability. Part A: Global and Sectoral Aspects. Contribution of Working Group II to the Fifth Assessment Report of the Intergovernmental Panel on Climate Change (2018), 1-34.
Jacob et al., 2014,EURO-CORDEX: new high-resolution climate change projections for European impact research, Reg Environ Change (2014) 14:563–578.

## Slide 29
Next steps
EU funded project GA no. 776848
29
Unit 1: NbS Concepts and Approaches
Unit 2: Good Practices from Open Air Laboratories
Unit 3: Stakeholder Engagement and Co-Creation
Unit 4: Assessing Risks in Socio-Ecological Systems
Unit 5: NbS Selection and Engineering
Unit 6: NbS Modelling and Monitoring
Unit 7: NbS Policy Context and Permitting Paths
Unit 8: Promoting NbS Uptake and Public Acceptance
Unit 9: Replication and Business Uptake
Unit 10: GeoIKP – NbS Platform

## Slide 30
EU funded project GA no. 776848
Training 5: NbS Selection and Engineering
Thank you!
Find us on: