## Slide 1: INTEGRATED RENEWABLE ENERGY FINANCE OPTIMISATION FOR MINI-GRID POWER SUPPLY TO 15 NEIGHBOURHOOD CLIENTS IN TSUMKWE, NAMIBIA
Kemi Jegede
jkemigift@gmail.com
Energy Modelling Platform for Africa (EMP-A)
2023

## Slide 2: Context and Aim
Chart: 
| South Africa | Namibia | Zambia | Zimbabwe
 | 57.1 | 28.7 | 7.3 | 6.3
Energy supply composition of Namibia
Context
Solar irradiation of 3000 kWh/m2 (2nd highest in the world)
Low population density (2nd lowest in the world)
About 50% of the Namibian population is unelectrified (30 000 households), consisting of 70-80% of the rural population
Community main economy is cropping farming
Aim
Ascertain project financial viability of Mini-grid in Tsumkwe
Increase of power quality and reliability from the production of energy close to demand
Eliminate dependency on the already strained main energy network
Reduced loss from energy transport
Environmental, health and security considerations
Can employ a wide range of technologies
Ideal for isolated communities with low energy demand
Notes: Namibia is rich natural resources and favorable climate
Environmental benefits
Eliminate dependency on the already strained main energy network
Reduced loss from energy transport
Increase of power quality and reliability from the production of energy close to demand
Can employ a wide range of technologies
Ideal for isolated communities with low energy demand
About 50% of the Namibian population is unelectrified (30 000 households), consisting of 70-80% of the rural population

## Slide 3: Project Description and Financing
Notes: What is your project? Describe it briefly.
Insert the key financial data / assumptions you used. Make sure to explain financial concepts, if any, on the presentation day.
Make sure to include only the important details, we do not want to overcrowd this slide.

## Slide 4: Project Description and Financing
Type of grid | Hybrid mini-grid solar-diesel-biomass (with lithium battery storage
Technologies | PV Unit, lithium batteries, steam turbine, biodigester, diesel generator
Location | Tsumkwe, Namibia
Construction period | 2024-2026
Duration of plant | 20 years
Inflation rate | 2% USD/ 6% NAD (Steady rate)
Generated amount | 0,1 GWh/year
Fuel cost (diesel and biomass) | 0,1 Million NAD/year
Discount rate | 10%
Plant size | 30 kW
Electricity price | NAD 2/kWh
Estimated cost | 0,2 Million USD
Notes: What is your project? Describe it briefly.
Insert the key financial data / assumptions you used. Make sure to explain financial concepts, if any, on the presentation day.
Make sure to include only the important details, we do not want to overcrowd this slide.

## Slide 5: Sensitivity Analysis
Parameters changed | Parameters studied | Assumptions
Sale price 2 -10 N$/kWh | Profitability (IRR & NPV) Dividends % return on equity | 5 values: increments of 0,2 One parameter changed at a time
Investment 0,05 – 0,6 million $ | Profitability (IRR & NPV) Dividends % return on equity | 7 values: 0,05; 0,1; 0,2; 0,3; 0,4; 0,5; 0,6 One parameter changed at a time
Notes: We need to simplify and understand the representation of reality
And how if can evolve

## Slide 6: Results
Chart: Sale Price (NAD/kWh)
| 2 | 4 | 6 | 8 | 10
NPV | -1.03 | 1.31 | 3.73 | 6.15 | 8.57
IRR | 0 | 18.6 | 32.8 | 46 | 57.8
Sensitivity of electricity sale price on NPV and IRR
Chart: Dividends (Million NAD)
| 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047
2D | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
4D | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.1302 | 0.2138 | 0.2637 | 0.3154 | 0.369 | 0.4246 | 0.4729 | 0.5229 | 0.5752 | 0.6301 | 0.6877 | 0.7481 | 0.8115 | 0.8781 | 0.9482 | 1.6279
6D | 0 | 0 | 0 | 0.0358 | 0.2569 | 0.3093 | 0.3635 | 0.421 | 0.4843 | 0.5517 | 0.6219 | 0.6951 | 0.7715 | 0.8512 | 0.9251 | 1.0022 | 1.0833 | 1.1686 | 1.2585 | 1.3532 | 1.4529 | 1.558 | 1.6689 | 2.3918
8D | 0 | 0 | 0 | 0.274 | 0.5094 | 0.5769 | 0.6472 | 0.7217 | 0.8031 | 0.8896 | 0.98 | 1.0747 | 1.1739 | 1.2778 | 1.3773 | 1.4815 | 1.5914 | 1.7072 | 1.8294 | 1.9583 | 2.0944 | 2.238 | 2.3896 | 3.1558
10D | 0 | 0 | 0 | 0.5122 | 0.7619 | 0.8446 | 0.9309 | 1.0224 | 1.1219 | 1.2275 | 1.3382 | 1.4544 | 1.5763 | 1.7044 | 1.8295 | 1.9608 | 2.0994 | 2.2458 | 2.4003 | 2.5634 | 2.7358 | 2.9179 | 3.1103 | 3.9197
2%R | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
4%R | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 18.3 | 30 | 37 | 44.3 | 51.8 | 59.6 | 66.4 | 73.4 | 80.7 | 88.4 | 96.5 | 104.9 | 113.8 | 123.2 | 133 | 228.4
6%R | 0 | 0 | 0 | 5 | 36 | 43.4 | 51 | 59.1 | 67.9 | 77.4 | 87.2 | 97.5 | 108.2 | 119.4 | 129.8 | 140.6 | 152 | 164 | 176.6 | 189.8 | 203.8 | 218.6 | 234.1 | 335.6
8%R | 0 | 0 | 0 | 38.4 | 71.5 | 80.9 | 90.8 | 101.2 | 112.7 | 124.8 | 137.5 | 150.8 | 164.7 | 179.3 | 193.2 | 207.8 | 223.3 | 239.5 | 256.6 | 274.7 | 293.8 | 314 | 335.2 | 442.7
10%R | 0 | 0 | 0 | 71.9 | 106.9 | 118.5 | 130.6 | 143.4 | 157.4 | 172.2 | 187.7 | 204 | 221.1 | 239.1 | 256.7 | 275.1 | 294.5 | 315.1 | 336.7 | 359.6 | 383.8 | 409.4 | 436.3 | 549.9
Sensitivity of electricity sale price on dividends and percentage return on equity
Notes: We need to simplify and understand the representation of reality
And how if can evolve

## Slide 7: Results
Sensitivity of investments on NPV and IRR
Chart: PLANT CAPEX (Million USD)
| 0.05 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6
NPV | 0.436 | -0.01 | -1.03 | -2.16 | -3.29 | -4.42 | -5.55
Base case
Chart: Dividends (Million NAD)
| 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047
0.05D | 0 | 0 | 0 | 0.0719 | 0.1069 | 0.1185 | 0.1306 | 0.1434 | 0.1574 | 0.1722 | 0.1877 | 0.204 | 0.2211 | 0.2391 | 0.2567 | 0.2751 | 0.2945 | 0.3151 | 0.3367 | 0.3596 | 0.3838 | 0.4094 | 0.4363 | 0.5499
0.1D | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0285 | 0.101 | 0.1174 | 0.1345 | 0.1522 | 0.1708 | 0.1902 | 0.2104 | 0.2315 | 0.2536 | 0.2767 | 0.3009 | 0.8318
0.2D | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0.3D | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0.4D | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0.5D | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0.6D | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0.05%R | 0 | 0.1 | 0 | 4 | 8.4 | 10.3 | 12.3 | 14.2 | 15.9 | 17.5 | 19.2 | 21 | 22.9 | 24.8 | 26.8 | 29 | 31.2 | 33.6 | 36.1 | 38.7 | 41.4 | 44.3 | 47.4 | 114.4
0.1%R | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 4 | 14.2 | 16.5 | 18.9 | 21.4 | 24 | 26.7 | 29.5 | 32.5 | 35.6 | 38.8 | 42.2 | 116.7
0.2%R | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0.3%R | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0.4%R | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Sensitivity of investments on dividends and percentage return on equity
Base case
Notes: We need to simplify and understand the representation of reality
And how if can evolve

## Slide 8: Conclusions and Policy Insights
Main policy insights
Base case model not profitable
Plant is too small to cover overheads
To make the plant profitable the following must be done:
          Increase production to 150 GWh/year and above (increase capacity factor) while keeping CAPEX fixed
Reduce the production cost to 0,05 million USD and below
Increase electricity sale price to 4 NAD/kWh and above
Reduce interest on loans
Interdependency/nonlinearity of parameters
Government actions and costs
Low interest loans
Community subsidy of up to 50% for local consumption use (2 NAD/kWh)
Future work
Expand the size of the hybrid plant to include the whole community (reduces overheads)
Use differential electricity rates for residential, industry and service providers
Consider other power conversion technologies in the hybrid system
Notes: List the main policy insights obtained from your model. Your conclusion should address your research question.
Your policy insights should describe what actions your government should take to address the challenges your country faces, and the cost of this intervention.
Give an example of future work, such as improvements to the model, data gathering, or use in teaching/capacity building.

## Slide 9: QUESTIONS?
Email: jkemigift@gmail.com
LinkedIn: https://www.linkedin.com/in/jegede-kemi-99526592/