## Slide 1
Antonio Aguilar-Garrido1, Mario Paniagua-López1,2, Ana Romero-Freire1, Manuel Sierra-Aragón1, Francisco Javier Martínez-Garzón1, and Francisco José Martín-Peinado1
1 Departamento de Edafología y Química Agrícola. Facultad de Ciencias. Universidad de Granada. Granada, Spain.
2 Departamento de Microbiología del Suelo y Sistemas Simbióticos, Estación Experimental del Zaidín, Consejo Superior de Investigaciones Científicas (EEZ-CSIC). Granada, Spain.
SSS7.3. Multidisciplinary approach on soil management and rehabilitation at different scales: materials for a toxic-free environment
RTI 2018-094327-B-I00 / FPU-18/02901
BIOLOGICAL ASSESSMENT OF IN-SITU REHABILITATION OF POLLUTED SOILS BY WASTE-DERIVED TECHNOSOLS
Notes: Hello to everyone,
I’m Antonio Aguilar Garrido from the Department of Soil Science of the University of Granada.
First of all, I would like to thank the session conveners for giving me the opportunity to present this study, which is part of my doctoral thesis and is entitled “Biological assessment of in-situ rehabilitation of polluted soils by waste-derived Technosols.”
25’’

## Slide 2
1. INTRODUCTION
2. AIMS
3. MATERIAL AND METHODS
4. RESULTS AND DISCUSSION
5. CONCLUSIONS
6. REFERENCES
Erosion by wind and water
Organic carbon loss
Pollution
Acidification
Salinization
Biodiversity loss
Surface effects
Nutrient status
Compaction
Moisture conditions
IMPACTS OF SOIL POLLUTION ON SOIL ECOSYSTEM SERVICES (FAO AND UNEP, 2021)
SOIL THREATS – Status of the World’s Soil Resources (FAO and ITPS, 2015)
3rd
4th
5th
9th
9th
7th
8th
Soil pollution’s rank among threats to soil functions
(Adapted from Rodríguez-Eugenio et al., 2018)
Notes: Soil pollution is a serious environmental problem, as it is one of the major threats worldwide, with strong repercussions on the ecosystem services that soils provide.

## Slide 3
1. INTRODUCTION
2. AIMS
3. MATERIAL AND METHODS
4. RESULTS AND DISCUSSION
5. CONCLUSIONS
6. REFERENCES
Main pollutants in soils (FAO and UNEP, 2021)
Main anthropogenic sources of metal(loid)s (Alloway, 2013)
Industrial areas
Mine tailings
Leaded gasoline and paints
Fertilizers
Animal manure / Sewage sludge
Atmospheric deposition
Pesticides
Wastewater irrigation
Coal combustion residues
Spillage of petrochemical
Mine tailings
Notes: There are several pollutants in soils, but here we refer to metal(loid)s. For which, metal mining is one of the main sources.

## Slide 4
1. INTRODUCTION
2. AIMS
3. MATERIAL AND METHODS
4. RESULTS AND DISCUSSION
5. CONCLUSIONS
6. REFERENCES
Author: A. Aguilar-Garrido
MINING OF SULPHIDE ORES
AZNALCÓLLAR MINE | SP
© Universidad de Granada
AZNALCÓLLAR DISASTER (SPAIN, 1998)
Author: F.J. Martín Peinado
April 1998
Author: A. Aguilar-Garrido
April 2022
Notes: In particular, mining of sulphide ores, such as the Aznalcóllar mine in Spain. Where took place one of the largest mining accident, with repercussions even today after more than 20 years.

## Slide 5
1. INTRODUCTION
2. AIMS
3. MATERIAL AND METHODS
4. RESULTS AND DISCUSSION
5. CONCLUSIONS
6. REFERENCES
Zn
As
Cd
Pb
Se
As
Fe
Cu
Pb
Pb
Hg
Fe
Zn
Zn
Cd
U
Sb
Tl
Au
As
Se
Fe
Pb
Fe
Zn
Tl
WASTE-DERIVED TECHNOSOLS
To evaluate, at short term, the effectiveness of two designed Technosols to rehabilitate these residually polluted soils
Measurements of soil enzymatic activity
Recovery of natural vegetation
Notes: This study aims to evaluate, at short term, the effectiveness of two designed Technosols to remediate these affected soils. In particular, the remediation process was assessed focusing on measurements of soil enzymatic activity and the recovery of natural vegetation.

## Slide 6
1. INTRODUCTION
2. AIMS
3. MATERIAL AND METHODS
4. RESULTS AND DISCUSSION
5. CONCLUSIONS
6. REFERENCES
Technosol | PS | IO | MS | OL | VC
T4 | 60 | 2 | 20 | 18 | -
T6 | 60 | 2 | 20 | - | 18
Composition (%): Ex-situ polluted soil + Mining/Urban/Agricultural wastes
TWO TECHNOSOLS (T4 and T6)
PS: Ex-situ polluted soil by metal(oid)s
Author: A. Aguilar-Garrido
IO: Sludge rich in iron oxyhydroxides
Author: A. Aguilar-Garrido
MS: Sludge from marble cutting and polishing
Author: A. Aguilar-Garrido
OL: Solid olive-mill by-product
Author: A. Aguilar-Garrido
VC: Vermicompost from pruning and gardening
Author: A. Aguilar-Garrido
Notes: Both Technosols were composed of ex-situ polluted soil and two mining wastes (sludge rich in iron oxyhydroxides and a marble sludge); together with an agro-industrial waste (solid olive-mill by-product) in T4, and an urban waste (vermicompost from gardening) in T6.

## Slide 7
Composition (%): Ex-situ polluted soil + Mining/Urban/Agricultural wastes
Author: A. Aguilar-Garrido
1. INTRODUCTION
2. AIMS
3. MATERIAL AND METHODS
4. RESULTS AND DISCUSSION
5. CONCLUSIONS
6. REFERENCES
TWO TECHNOSOLS (T4 and T6)
Manual mixing
Author: A. Aguilar-Garrido
Container filling
Author: A. Aguilar-Garrido
Watering and incubation for 2 months
Author: A. Aguilar-Garrido
Notes: All these component were manually mixed on site, then, containers were filled with the Technosols, where they were incubated for x months.

## Slide 8
1. INTRODUCTION
2. AIMS
3. MATERIAL AND METHODS
4. RESULTS AND DISCUSSION
5. CONCLUSIONS
6. REFERENCES
Experimental set-up
TWO TECHNOSOLS (T4 and T6)
EXPERIMENTAL PLOT “EL VICARIO” (SEVILLE, SPAIN)
TECHNOSOL
(25 cm)
POLLUTED SOIL
(~ 5 cm)
Author: A. Aguilar-Garrido
T4
T6
Replica 1
Replica 2
Replica 3
Author: A. Aguilar-Garrido
SEED BANK
(~ 2.5 cm)
Notes: About 25 cm of the Technosols were surface applied in situ on polluted soils in triplicate. On top of Technosols, a small layer of recovered soil was also placed as a seed bank.

## Slide 9
1. INTRODUCTION
2. AIMS
3. MATERIAL AND METHODS
4. RESULTS AND DISCUSSION
5. CONCLUSIONS
6. REFERENCES
Experimental monitoring
TWO TECHNOSOLS (T4 and T6)
2 TIMES
t0 = 0 months (Apr. 2021)
t1 = 12 months (Apr. 2022)
Sampling
TECHNOSOL
(T4 and T6) (depth: < 25 cm)
TREATED POLLUTED SOIL
(T4-PS and T6-PS) (depth: 25 - 30 cm)
Variables measured
Soil properties
  pH 1:2.5, EC 1:5, OC (Tyurin, 1951), CaCO3 (Barahona, 1984), CEC (SCS-USDA, 1972)
Metal(loid)s concentrations (As, Cd, Cu, Ni, Pb, Sb, Zn)
  Total (X‐ray fluorescence with NITON XL3t‐980 GOLDD+) and water-soluble (Sposito et al., 1982; PerkinElmer Avio® 500 ICP-OES)
Soil enzymatic activities
  Dehydrogenase (Tabatabai, 1994), acid phosphatase (Eivazi and Tabatabai, 1977), cellulase (Hope and Burns, 1987), and protease (Ladd and Butler, 1972)
Vegetation recovery
  Cover, specific richness, and diversity index Shannon-Wiever
Notes: After one year of application, Technosols and treated polluted soils were characterised (soil properties, total and water-soluble concentrations of metal(loid)s, and soil enzyme activities) and compared to initial conditions. Vegetation was also monitored by measuring cover, specific richness and diversity index.

## Slide 10
Slight increase in CEC
1. INTRODUCTION
2. AIMS
3. MATERIAL AND METHODS
4. RESULTS AND DISCUSSION
5. CONCLUSIONS
6. REFERENCES
 |  |  | T4 |  |  | T4-PS |  |  | T6 |  |  | T6-PS |  | 
 |  |  | t0 | t1 |  | t0 | t1 |  | t0 | t1 |  | t0 | t1 | 
 | pH1:2.5 (H2O) |  | 7.03 ± 0.07 aB | 7.56 ± 0.02 bB |  | 3.60 ± 0.13 aA | 7.04 ± 0.16 bA |  | 7.12 ± 0.08 aB | 7.48 ± 0.04 bB |  | 3.60 ± 0.23 aA | 7.26 ± 0.04 bA | 
 | EC1:5 (dS m-1) |  | 3.34 ± 0.19 bB | 2.79 ± 0.08 aA |  | 2.88 ± 0.05 A | 2.96 ± 0.04B |  | 3.05 ± 0.13 b | 2.78 ± 0.04 a |  | 2.82 ± 0.15 | 2.87 ± 0.16 | 
 | OC (%) |  | 2.76 ± 0.36 B | 2.66 ± 0.12 B |  | 0.45 ± 0.26 aA | 0.87 ± 0.15 bA |  | 2.29 ± 0.09 B | 2.26 ± 0.22 B |  | 0.59 ± 0.19 aA | 1.12 ± 0.34 bA | 
 | CaCO3 (%) |  | 21.60 ± 1.27 B | 22.13 ± 2.09 B |  | 0.68 ± 0.04 aA | 4.69 ± 1.68 bA |  | 20.39 ± 0.99 aB | 22.68 ± 0.72 bB |  | 0.62 ± 0.14 aA | 9.35 ± 3.71 bA | 
 | CEC (cmol(+) kg-1) |  | 12.72 ± 0.61 B | 14.06 ± 0.92 B |  | 7.99 ± 1.16 aA | 10.96 ± 1.73 bA |  | 11.74 ± 0.40 aB | 15.07 ± 2.70 bB |  | 6.96 ± 0.37 aA | 11.20 ± 0.84 bA | 
SOIL PROPERTIES
Effects of Technosol treatment on polluted soils
Strongly acidic pH (<4) neutralisation
2-fold increase in OC
Addition of CaCO3
Technosols
Neutral pH
High OC content (T4 ~ 2.7%, T6 ~ 2.3%)
High CaCO3 content (> 20%)
Medium CEC
Notes: Technosols showed optimal conditions to rehabilitate the polluted soils and recover the non-existent natural vegetation. In fact, the treatment with Technosols reversed the adverse conditions in the polluted soils. - Neutralised the acid pH - Doubled the OC content and, consequently, also slightly increased the cation exchange capacity. - Incorporated carbonates, related to acid neutralisation

## Slide 11
1. INTRODUCTION
2. AIMS
3. MATERIAL AND METHODS
4. RESULTS AND DISCUSSION
5. CONCLUSIONS
6. REFERENCES
 |  |  | T4 |  |  | T4-PS |  |  | T6 |  |  | T6-PS |  | 
 | mg kg-1 |  | t0 | t1 |  | t0 | t1 |  | t0 | t1 |  | t0 | t1 | 
 | AsT |  | 215.17 ± 7.71 A | 213.05 ± 22.95 A |  | 274.11 ± 19.89 B | 275.17 ± 33.92 B |  | 187.01 ± 8.26 A | 193.94 ± 7.95 A |  | 288.70 ± 27.44 bB | 229.56 ± 14.68 aB | 
 | CdT |  | < LOD | < LOD |  | < LOD | < LOD |  | < LOD | < LOD |  | < LOD | < LOD | 
 | CuT |  | 95.29 ± 5.37 B | 93.73 ± 3.30 |  | 81.46 ± 1.53 aA | 93.32 ± 7.78 b |  | 75.06 ± 3.51 a | 86.73 ± 3.37 b |  | 84.90 ± 9.43 | 84.38 ± 1.18 | 
 | NiT |  | 31.33 ± 3.82 A | 30.78 ± 3.08 A |  | 35.75 ± 0.60 aB | 45.01 ± 3.78 bB |  | 30.24 ± 4.30 a | 38.77 ± 2.98 b |  | 35.96 ± 3.14 | 37.86 ± 2.95 | 
 | PbT |  | 477.69 ± 9.06 A | 458.31 ± 41.95 |  | 548.85 ± 17.31 B | 553.24 ± 60.70 |  | 422.93 ± 33.44 A | 426.48 ± 31.60 A |  | 553.59 ± 77.81 B | 509.34 ± 24.68 B | 
 | SbT |  | 20.61 ± 2.78 | 24.75 ± 6.41 |  | 24.87 ± 3.98 | 37.49 ± 7.35 |  | 16.26 ± 1.54 a A | 22.71 ± 4.12 b |  | 22.79 ± 4.79 B | 27.01 ± 9.21 | 
 | ZnT |  | 168.11 ± 16.77 | 165.02 ± 9.73 |  | 144.86 ± 26.26 | 165.25 ± 37.83 |  | 156.89 ± 12.88 B | 180.72 ± 14.28 |  | 128.95 ± 27.04 aA | 165.99 ± 22.83 b | 
TOTAL CONCENTRATIONS OF METAL(LOID)S
 | NGR | 
 | (BOJA, 2015) | 
 | 36 | 
 | 25 | 
 | 595 | 
 | 1530 | 
 | 275 | 
 | 90 | 
 | 10000 | 
High total concentrations of potentially harmful elements (PHE)
... both in polluted soil and Technosols
Potentially polluted by As and Pb
Technosol | PS | IO | MS | OL | VC
T4 | 60 | 2 | 20 | 18 | -
T6 | 60 | 2 | 20 | - | 18
Notes: Looking at the total concentration of metal(loid)s, we observed that there were high concentrations of several potentially harmful elements in both the polluted soil and the Technosols. In fact, as regional regulatory levels were exceeded, they could be considered potentially polluted by As and Pb.

## Slide 12
1. INTRODUCTION
2. AIMS
3. MATERIAL AND METHODS
4. RESULTS AND DISCUSSION
5. CONCLUSIONS
6. REFERENCES
 |  |  | T4 |  |  | T4-PS |  |  | T6 |  |  | T6-PS |  | 
 | mg kg-1 |  | t0 | t1 |  | t0 | t1 |  | t0 | t1 |  | t0 | t1 | 
 | AsW |  | 0.26 ± 0.03 a | 0.39 ± 0.01 bB |  | 0.27 ± 0.04 | 0.21 ± 0.03 A |  | 0.47 ± 0.06 B | 0.46 ± 0.03 B |  | 0.28 ± 0.03 bA | 0.18 ± 0.04 aA | 
 | CdW |  | 0.0056 ± 0.0008 bA | < LOD a |  | 0.2208 ± 0.0460 bB | < LOD a |  | 0.0091 ± 0.007 bA | < LOD a |  | 0.1730 ± 0.0563 bB | < LOD a | 
 | CuW |  | 0.42 ± 0.04 bA | 0.14 ± 0.06 aA |  | 3.90 ± 1.07 bB | 0.31 ± 0.04 aB |  | 0.25 ± 0.01 bA | 0.10 ± 0.03 aA |  | 3.62 ± 0.98 bB | 0.24 ± 0.09 aB | 
 | NiW |  | 0.046 ± 0.008 bA | < LOD a |  | 1.436 ± 0.275 bB | 0.008 ± 0.007 a |  | 0.026 ± 0.003 bA | < LOD a |  | 1.315 ± 0.253 bB | 0.010 ± 0.017 a | 
 | PbW |  | 0.0018 ± 0.0031 bA | < LOD a |  | 0.0177 ± 0.0096 bB | < LOD a |  | 0.0013 ± 0.0022 | < LOD |  | 0.0251 ± 0.0330 b | < LOD a | 
 | SbW |  | 0.132 ± 0.005 aB | 0.221 ± 0.028 b |  | 0.015 ± 0.005 aA | 0.168 ± 0.048 b |  | 0.158 ± 0.024 B | 0.153 ± 0.008 |  | 0.016 ± 0.004 aA | 0.146 ± 0.017 b | 
 | ZnW |  | 0.30 ± 0.06 bA | 0.07 ± 0.01 a |  | 40.73 ± 6.49 bB | 0.12 ± 0.12 a |  | 0.21 ± 0.04 bA | 0.05 ± 0.02 a |  | 32.36 ± 8.21 bB | 0.10 ± 0.05 a | 
WATER-SOLUBLE CONCENTRATIONS OF METAL(LOID)S
Significant reduction in solubility of most PHE
In Technosols (T4 and T6)
In polluted soils treated by Technosol (T4-PS and T6-PS) after 1 year
As and Sb, the opposite
Notes: Likewise, Technosols significantly reduced the considerable concentrations of several PHEs in the water-soluble fractions of the polluted soil. Directly in the Technosols, as well as in the polluted soil with one year of treatment.
With the notable exceptions of As and Pb, which, on the contrary, the treatment has caused their resolubilization (especially Sb).

## Slide 13
1. INTRODUCTION
2. AIMS
3. MATERIAL AND METHODS
4. RESULTS AND DISCUSSION
5. CONCLUSIONS
6. REFERENCES
SOIL ENZYMATIC ACTIVITIES
Chart: Dehydrogenase (µg TPF g soil-1 16 h-1)
| T4 | T4-PS | T6 | T6-PS
0 mth | 4.1567 | 1.32 | 10.0233 | 1.8752
12 mth | 85.56 | 4.5867 | 59.15 | 3.3167
Chart: Cellulase (µg glucose g soil-1 16h-1)
| T4 | T4-PS | T6 | T6-PS
0 mth | 0.17611 | 0.061763 | 0.3076 | 0.11327
12 mth | 0.64836 | 0.28155 | 0.5833 | 0.43944
Chart: Protease (µmol tyrosine g soil-1 2h-1)
| T4 | T4-PS | T6 | T6-PS
0 mth | 12.1018 | 2.1988 | 8.9805 | 2.4758
12 mth | 5.4693 | 3.6813 | 6.0336 | 2.891
Chart: Acid phosphatase (µmol ƿ-nitrophenol g soil-1 h-1)
| T4 | T4-PS | T6 | T6-PS
0 mth | 0.24245 | 0.28448 | 0.5444 | 0.25513
12 mth | 0.55005 | 0.31317 | 0.7867 | 0.26569
x 2
x 1.5
x 3.5
x 1.8
x 20
x 6
÷ 2
÷ 1.5
Notes: At initial time, microbiological activity increased slightly in Technosols compared to the polluted soil. But over time it was strongly stimulated.
For example, dehydrogenase activity increased by 20 in T4 and 6 in T6 compared to initial values.
Similarly, although not as pronounced as in the Technosols, an increase in microbiological activity with treatment was observed in the contaminated soil.

## Slide 14
Author: A. Aguilar-Garrido
Replica 2
1. INTRODUCTION
2. AIMS
3. MATERIAL AND METHODS
4. RESULTS AND DISCUSSION
5. CONCLUSIONS
6. REFERENCES
VEGETATION RECOVERY
Vegetation cover: 100% in T4 and T6
Author: A. Aguilar-Garrido
Replica 1
Author: A. Aguilar-Garrido
Replica 3
Notes: Furthermore, after one year, 100% vegetation cover was established with the application of both Technosols.

## Slide 15
1. INTRODUCTION
2. AIMS
3. MATERIAL AND METHODS
4. RESULTS AND DISCUSSION
5. CONCLUSIONS
6. REFERENCES
VEGETATION RECOVERY
Author: A. Aguilar-Garrido
Author: A. Aguilar-Garrido
Author: A. Aguilar-Garrido
Notes: Although with certain differences among Technosols.

## Slide 16
1. INTRODUCTION
2. AIMS
3. MATERIAL AND METHODS
4. RESULTS AND DISCUSSION
5. CONCLUSIONS
6. REFERENCES
VEGETATION RECOVERY
Chart: Specific richness
| T4 | T6
 | 13 | 9
Chart: Shannon-Wiever diversity index
| T4 | T6
 | 2.93 | 2.51
T4a
Spergularia rubra (L.) J. Presl & C. Presl. (51)
Anthemis arvensis L. (48)
Brassica oxyrrhina Willk. (Coss.) (33)
Vulpia membranacea (L.) Dumort. (32)
Trifolium arvense L. (28)
Lamarckia aurea (L.) Moench (20)
Echium plantagineum L. (8)
Ornithopus sativus subsp. isthmocarpus (Coss.) Dostál (3)
Trifolium campestre Schreb. (2)
Silene micropetala Lag. / Silene gallica L. (1)
Scorpiurus vermiculatus L. (1)
T4b
Brassica oxyrrhina Willk. (Coss.) (45)
Anthemis arvensis L. (38)
Trifolium arvense L. (32)
Vulpia membranacea (L.) Dumort. (25)
Echium plantagineum L. (21)
Lamarckia aurea (L.) Moench (9)
Hordeum leporinum Link (5)
Trifolium campestre Schreb. (4)
Ornithopus sativus subsp. isthmocarpus (Coss.) Dostál (2)
Leontodon longirostris (Finch & P. D. Sell) Talavera (1)
T4c
Trifolium arvense L. (84)
Vulpia membranacea (L.) Dumort. (56)
Anthemis arvensis L. (36)
Spergularia rubra (L.) J. Presl & C. Presl. (29)
Lamarckia aurea (L.) Moench (18)
Brassica oxyrrhina Willk. (Coss.) (9)
Trifolium campestre Schreb. (8)
Ornithopus sativus subsp. isthmocarpus (Coss.) Dostál (7)
Echium plantagineum L. (2)
Silene micropetala Lag. / Silene gallica L. (1)
T6a
Brassica oxyrrhina Willk. (Coss.) (98)
Anthemis arvensis L. (5)
Out of the census:
Lamarckia aurea (L.) Moench
Spergularia rubra (L.) J. Presl & C. Presl.
Chrysanthemum coronarium L.
Hirschfeldia incana (L.) Lagr.-Foss.
T6b
Echium plantagineum L. (46)
Anthemis arvensis L. (34)
Brassica oxyrrhina Willk. (Coss.) (27)
Vulpia membranacea (L.) Dumort. (15)
Trifolium arvense L. (7)
Hirschfeldia incana (L.) Lagr.-Foss. (7)
Hordeum murinum L. subsp. leporinum (Link) Arcang. (1)
T6c
Vulpia membranacea (L.) Dumort. (75)
Echium plantagineum L. (54)
Anthemis arvensis L. (38)
Lamarckia aurea (L.) Moench (10)
Chrysanthemum coronarium L. (8)
Trifolium arvense L. (7)
Bromus hordeaceus L. (6)
Notes: Greater biodiversity developed in T4 than in T6, with higher specific richness and diversity index.

## Slide 17
1. INTRODUCTION
2. AIMS
3. MATERIAL AND METHODS
4. RESULTS AND DISCUSSION
5. CONCLUSIONS
6. REFERENCES
Zn
As
Cd
Pb
Se
As
Fe
Cu
Pb
Pb
Hg
Fe
Zn
Zn
Cd
U
Sb
Tl
Au
As
Se
Fe
Pb
Fe
Zn
Tl
WASTE-DERIVED TECHNOSOLS
Improve soil properties
TECHNOSOLS WERE EFFECTIVE IN REHABILITATING THESE POLLUTED SOILS
Reduce PHE solubility (except As and Sb)
Stimulate microbiological activity
Promote the establishment of biodiverse natural vegetation
Notes: Therefore, these Technosols were effective in rehabilitating these polluted soils, as they improved soil properties, reduced PHEs mobility and bioavailability, and also promoted microbiological activity and establishment of biodiverse natural vegetation.

## Slide 18
1. INTRODUCTION
2. AIMS
3. MATERIAL AND METHODS
4. RESULTS AND DISCUSSION
5. CONCLUSIONS
6. REFERENCES
Alloway, B. J. (2013). Sources of Heavy Metals and Metalloids in Soils. In B. J. Alloway (Ed.), Heavy Metals in Soils (pp. 11-50). Dordrecht, Netherlands: Springer. https://doi.org/10.1007/978-94-007-4470-7
Barahona, E. (1984). Determinaciones analíticas en suelos: carbonatos totales y caliza activa. In Sociedad Española de la Ciencia del Suelo (SECS) (Ed.), I Congreso Nacional de la Ciencia del Suelo. Sociedad Española de la Ciencia del Suelo.
Eivazi, F., & Tabatabai, M. A. (1977). Phosphatases in soils. Soil Biology & Biochemistry, 9, 167–172.
Hope, C. F. A., & Burns, R. G. (1987). Activity, origins and location of cellulases in a silt loam soil. Biology and Fertility of Soils, 5, 164–170. https://doi.org/10.1007/BF00257653
FAO (Food and Agriculture Organization of the United Nations) and ITPS (Intergovernmental Technical Panel on Soils). (2015). Status of the world’s soil resources (SWSR) – Main report. Rome, Italy: Food and Agriculture Organization of the United Nations and Intergovernmental Technical Panel on Soils. http://www.fao.org/3/a-i5199e.pdf
FAO (Food and Agriculture Organization of the United Nations) and UNEP (United Nations Environment Programme). (2021). Global assessment of soil pollution: Report. Rome, Italy: Food and Agriculture Organization of the United Nations. https://doi.org/10.4060/cb4894en
Ladd, J. N., & Butler, J. H. A. (1972). Short-term assays of soil proteolytic enzyme activities using proteins and dipeptide derivatives as substrates. Soil Biology and Biochemistry, 4(1), 19–30. https://doi.org/10.1016/0038-0717(72)90038-7
Rodríguez-Eugenio, N., McLaughlin, M. J., & Pennock, D. (2018). Soil pollution: a hidden reality. Rome, Italy: Food and Agriculture Organization of the United Nations (FAO).
SCS (Soil Conservation Service) - USDA (United States Department of Agriculture). (1972). Soil Survey Manual. Methods and procedures for collecting soil samples. Soil Conservation Service, USDA.
Sposito, G., Lund, L. J., & Chang, A. C. (1982). Trace Metal Chemistry in Arid-zone Field Soils Amended with Sewage Sludge: I. Fractionation of Ni, Cu, Zn, Cd, and Pb in Solid Phases. Soil Science Society of America Journal, 46, 260–264. https://doi.org/10.2136/sssaj1982.03615995004600020009x
Tabatabai, M. A. (1994). Soil enzymes. In S. H. Mickelson & J. M. Bigham (Eds.), Methods of Soil Analysis, Part 2. Microbiological and Biochemical Properties - SSSA Book Series, no. 5. (pp. 775–833). Soil Science Society of America. https://doi.org/10.2136/sssabookser5.2.c37
Tyurin, I. V. (1951). Analytical procedure for a comparative study of soil humus. Trudy Poch. Inst. Dokuchaev., 33, 5–21.

## Slide 19
Antonio Aguilar-Garrido, Mario Paniagua-López, Ana Romero-Freire, Manuel Sierra-Aragón, Francisco Javier Martínez-Garzón, and Francisco José Martín-Peinado
BIOLOGICAL ASSESSMENT OF IN-SITU REHABILITATION OF POLLUTED SOILS BY WASTE-DERIVED TECHNOSOLS
Acknowledge to the Spanish Government for the foundation of this study with the National Research Project (RTI 2018-094327-B-I00, Ministry of Science and Innvotation) and the pre-doctoral contract of Antonio Aguilar-Garrido (FPU-18/02901, Ministry of Education), the Linking Landscape, Environment, Agriculture and Food of the Instituto Superior de Agronomia of the University of Lisbon for assistance and foundation of soil enzymatic analyses, the CSIC Associated I+D+I Unit “Soil Biorremediation” from the University of Granada, and the European Geosciences Union for the Roland Schlich Travel Support.
Notes: Thank you for your attention.

## Slide 20
Notes: Thank you for your attention.