## Slide 1: Hwekwete 20MW Grid Tied Solar Power Plant Financial Analysis
Trevor Ashala trevor@natfortenergy.com
Energy Modelling Platform for Africa (EMP-A)
2023
Flag or map of the country…

## Slide 2: Context and Aim
Zimbabwe is generating 1000MW with a daily peak load of 2500MW. The deficit has led to load shedding.
The major hinderance to financing of the projects are legacy debts, lack of long term finance, currency conversion issues and inflation.
Aim
To determine project profitability if we changed the inflation up to 50% , corporate tax to 20% and production of the plant decreasing by 20%.

## Slide 3
Capacity
Tax
Inflation
NPV:23756.8355
IRR: 13.46%
Project Base Scenario
Profit and Loss Analysis

## Slide 4: Project Description
Technology | SOLAR GRID TIED
Capacity | 20MW
Construction Period(Years) | 3
Start Year | 2023
First Year of Operation | 2026
Finish Year | 2051
Usd Inflation Rate % | 2
Zwl Inflation Rate % | 10
Tax percentage % | 15
Local Currency | Zimbabwean Dollar(ZWL)
Foreign Currency | United States Dollar(USD)

## Slide 5: Scenario Analysis
Using the Model for Financial Analysis of Electric Sector Expansion Plans (FINPLAN)
Number | Scenarios | Key Assumptions
1 | Increase the inflation to 50% | Central Government Fails to Contain Inflation to maintain Yearly Inflation to 10%
2 | Decrease the output of the Plant by 20% | Plant Equipment is Underperforming
3 | Increase of Corporate Tax to 20% from 15% | Government increase of base tax to fund consumer programs like road rehabilitation.
Number | Scenarios | Key Assumptions
1 | Increase the inflation to 50% | Central Government Fails to Contain Inflation to maintain Yearly Inflation to 10%
2 | Decrease the output of the Plant by 20% | Plant Equipment is Underperforming
3 | Increase of Corporate Tax to 20% from 15% | Government increase of base tax to fund consumer programs like road rehabilitation.

## Slide 6: Loan Repayment cost Changes Due to Inflation
Chart: Loan Repayment Changes Due to Inflation
| 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050 | 2051
Repayments: loans and bonds with 10% inflation | 0 | 0 | 0 | 485.4455 | 587.1949 | 710.271 | 859.1438 | 1039.2203 | 1257.0409 | 1520.5166 | 1839.2169 | 2224.7168 | 2691.0174 | 3255.0547 | 3937.3141 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Repayments: loans and bonds with 50% inflation | 0 | 368.7667 | 1640.9747 | 3236.389 | 4789.8557 | 7088.9865 | 10491.7 | 15527.716 | 22981.0197 | 34011.9092 | 50337.6256 | 74499.6858 | 110259.535 | 122456.1908 | 60277.3232 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
RESULTS
NPV:5015
IRR: 7.42%
1000 x INCREASE

## Slide 7: Effects of decrease of plant production
Chart: Effects of decrease of plant production by 20% on sales and dividends
| 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050 | 2051
Total sales revenues for 80% production | 0 | 0 | 0 | 1716.4177 | 1888.0594 | 2076.8654 | 2284.5519 | 2513.0071 | 2764.3078 | 3040.7386 | 3344.8125 | 3679.2937 | 4047.2231 | 4451.9454 | 4897.1399 | 5386.8539 | 5925.5393 | 6518.0932 | 7169.9026 | 7886.8928 | 8675.5821 | 9543.1403 | 10497.4544 | 11547.1998 | 12701.9198 | 13972.1117 | 15369.3229 | 16906.2552 | 18596.8807
Total sales revenues for 100% production | 0 | 0 | 0 | 2145.6652 | 2360.2317 | 2596.2549 | 2855.8803 | 3141.4684 | 3455.6152 | 3801.1767 | 4181.2944 | 4599.4238 | 5059.3662 | 5565.3029 | 6121.8331 | 6734.0165 | 7407.4181 | 8148.1599 | 8962.9759 | 9859.2735 | 10845.2008 | 11929.7209 | 13122.693 | 14434.9623 | 15878.4586 | 17466.3044 | 19212.9349 | 21134.2283 | 23247.6512
Dividend for 100% production | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1891.1178 | 6793.1066 | 7638.8196 | 8560.4539 | 9565.5982 | 11619.9242 | 12731.8051 | 13954.8238 | 15300.0892 | 16779.8201 | 19755.82
Dividends for 80% production | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2947.3161 | 5642.7932 | 7126.8657 | 7775.6076 | 8489.1736 | 9274.0408 | 10137.3339 | 15940.9957
33.5% decrease in revenue

## Slide 8: Increase of Corporate Tax to 20%
NPV:22058.29
IRR: 13.166
Chart: Effects of Increase of Tax
| 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050 | 2051
Profit/loss at 20% tax | 0 | -708.8 | -2239.824 | -2185.7329 | -2166.0733 | -2119.2574 | -2037.6584 | -1911.9261 | -1730.6236 | -1479.7901 | -1142.4135 | -697.7951 | -120.7836 | 619.1476 | 1559.0127 | 2743.6529 | 3895.8763 | 5270.4273 | 6343.6791 | 6793.1066 | 7638.8196 | 8560.4539 | 9565.5982 | 11619.9242 | 12731.8051 | 13954.8238 | 15300.0892 | 16779.8201 | 19755.82
Profit/loss at 15% tax | 0 | -432.952 | -1366.8705 | -1683.1653 | -1668.9555 | -1640.832 | -1595.628 | -1529.6103 | -1438.3876 | -1316.8043 | -1158.8194 | -957.3653 | -704.1864 | -389.6528 | -5.7987 | 455.657 | 1010.8276 | 1679.3199 | 2480.5559 | 3437.032 | 4574.7853 | 5198.1666 | 5642.7932 | 7126.8657 | 7775.6076 | 8489.1736 | 9274.0408 | 10137.3339 | 15940.9957
40% decrease in Profit

## Slide 9: NPV & IRR RESULTS
Scenario | NPV | IRR
Base Simulation | NPV:23756.8355 | IRR: 13.46%
20% Percent Decrease in Production | NPV:8822.87 | IRR: 9.545%
Increase of Tax to 20% | NPV:22058.29 | IRR: 13.166
Increase of Inflation to 50% | NPV:5015 | IRR: 7.42%

## Slide 10: Conclusions and Policy Insights
Conclusion | Policy Insights
increase on corporate tax from 15% to 20% decreases the net profit of a project | The government needs to create an enabling investment environment in the renewable sector by keeping the corporate tax on 15%
increase in inflation to 50% from 10% will increase the cost of loan repayments , overall decreasing the net profits of the project in real money | Government needs to put stability instruments in place to have a floating inflation that is close to 10% with an allowable deviation of +_5 % only
decrease in production to 80% due to plant equipment not being of standards. Pushes the start of paying out dividends by 2 years and decreases the Revenue collected by a factor of 22.5% | Government needs to put more regulation in the Renewable EPC Sector so as to get quality products that bring value on money invested

## Slide 11: Project Financing
Equity: from 2023 to 2026 the following amounts in LC are injected:2000, 4000 and 2000.No limit to dividends being paid out
Short term deposits: interest rate -1% over inflation.
Stand by facility: interest rate 4 % over inflation
Shareholders targeted return data: 11% approx. return rate. Disposal year 2055
Terms of project finance loan: 6% discount rate ,12 years average loan term ,1.4 security ratio for loan period, 25 years expected life, 1.6 security ratio for project life, 2026 first year of debt service