## Slide 1: The acceptability of wearables for atrial fibrillation screening: Interim analysis of the SAFER Wearables Study
Dr Peter H. Charlton
University of Cambridge
City, University of London
Photo by Luke Chesser on Unsplash
Recorded in preparation for the
2024 Computing in Cardiology Conference.

## Slide 2
7,000
Strokes prevented
Lives saved p.a.
2,000
425,000
Additional diagnoses
If atrial fibrillation was adequately treated in England:
Stroke Association, “State of the Nation,” 2017.
Public Health England, “Atrial fibrillation prevalence estimates in England …”, 2015.
Pexels, https://pixabay.com/photos/man-heartache-chest-pain-hurt-pain-1846050/ (Pixabay Licence)
Notes: Source: https://www.stroke.org.uk/professionals/atrial-fibrillation-information-and-resources ; “It's estimated that if AF was adequately treated, around 7,000 strokes would be prevented and over 2,000 lives saved every year in England alone.”

## Slide 3
Photo by Luke Chesser on Unsplash

## Slide 4
Kristof F et al., QRS detection in single-lead, telehealth electrocardiogram signals: Benchmarking open-source algorithms, PLOS Digital Health, 2024. https://doi.org/10.1371/journal.pdig.0000538 (CC BY 4.0)

## Slide 5
1. Background
2. Acceptability in older adults
Photo by Luke Chesser on Unsplash
3. Next Steps
Photo by Dario Valenzuela on Unsplash
Detecting atrial fibrillation in daily life

## Slide 6
3. Next Steps
1. Background
2. Acceptability in older adults
Photo by Luke Chesser on Unsplash
Photo by Dario Valenzuela on Unsplash
Detecting atrial fibrillation in daily life

## Slide 7
The Photoplethysmogram
Photoplethysmogram (PPG) Sensor
Wrist cross-section
Notes: If you have a fitness tracker or smart watch you may have seen sensors on its underside, perhaps emitting red or green light. These are PPG sensors. I’ll use a cross-section [click] of the wrist to illustrate how a PPG signal is generated and captured. In this example a [click] green LED is used to illuminate the wrist. Some of the light is attenuated in the tissues, and some is reflected back towards the sensor. The level of reflected light is recorded by a [click] light sensor (in yellow). Here is [click] an example of the resulting PPG signal.
[click] The cross-section shows the pulsatile flow of arterial blood into the wrist with each heart beat. On the right, the signal increases and decreases with each heart beat, as the volume of arterial blood, which absorbs light, increases and decreases. This forms pulse waves – one for each heart beat.

## Slide 8
Photoplethysmogram (heart rate = 100 bpm)
Slower heart rate (heart rate = 80 bpm)
Atrial fibrillation (heart rate = 140 bpm)
Photoplethysmogram (PPG) Sensor
Wrist cross-section
The Photoplethysmogram
Notes: [click] Heart rate: 100 bpm
[click] Heart rate: 60 bpm
[click] irregular rhythm
[click] irregular intervals
[click] varying pulse amplitudes
If you have a fitness tracker or smart watch you may have seen sensors on its underside, perhaps emitting red or green light. These are PPG sensors. I’ll use a cross-section [click] of the wrist to illustrate how a PPG signal is generated and captured. In this example a [click] green LED is used to illuminate the wrist. Some of the light is attenuated in the tissues, and some is reflected back towards the sensor. The level of reflected light is recorded by a [click] light sensor (in yellow). Here is [click] an example of the resulting PPG signal.
[click] The cross-section shows the pulsatile flow of arterial blood into the wrist with each heart beat. On the right, the signal increases and decreases with each heart beat, as the volume of arterial blood, which absorbs light, increases and decreases. This forms pulse waves – one for each heart beat.
[click] This PPG signal shows a heart rate of approximately 100 beats per minute. [click] Here is an example of a slower heart rate, still in sinus rhythm. Besides the heart rate, the signal is also greatly influenced by the [click] heart rhythm, since an irregular rhythm such as atrial fibrillation results in both [click] irregular beat-to-beat intervals and [click] varying pulse amplitudes. [click] Focusing in on a [click] single pulse wave [click]...

## Slide 9
Single-lead ECG

## Slide 10
Photo by Luke Chesser on Unsplash
Using photoplethysmography to prompt single-lead ECG

## Slide 11
3. Next Steps
1. Background
2. Acceptability in older adults
Photo by Luke Chesser on Unsplash
Photo by Dario Valenzuela on Unsplash
Detecting atrial fibrillation in daily life

## Slide 12
Aim: To identify factors influencing the acceptability of wearables in older adults.
Methods:
In 130 older adults, aged 65+, half of whom have AF
Devices delivered by mail, and instructions provided via leaflet and telephone call.
Asked to wear three devices for one week.
Two wrist-worn devices:
  PulseOn Arrhythmia Monitor: Continuous PPG. Vibrated 4 times per day and upon irregular pulse to prompt ECG recording.
  PulseOn OHR (Optical Heart Rate Tracker): Intermittent PPG
Reference ECG chest patch:
  Bittium Faros 180 chest patch: Continuous ECG
Questionnaire provided formal feedback
Informal feedback collected via telephone calls.
Progress:
21 out of 130 participants to date.
The SAFER Wearables Study, NCT04715555

## Slide 13
Results:
Recruitment and participation
75 potential participants invited
42 consented to take part (56%)
21 had taken part at the time of this analysis
Device removals
Removals:
5 (24%) removed Faros 180 due to skin irritation
4 (19%) removed PulseOn OHR (3 due to battery running out, 1 due to skin irritation)
1 (5%) removed PulseOn Arr due to night-time vibrations
The SAFER Wearables Study, NCT04715555

## Slide 14
Results:
Feedback
Most respondents would be happy to wear any device for a week:
The SAFER Wearables Study, NCT04715555

## Slide 15
Results:
Feedback
But the chest electrodes irritated participants, with 8 (38%) participants reporting irritation during telephone calls.
The SAFER Wearables Study, NCT04715555
“looked as though I'd been attacked with an octopus with a round ring”
"I forget that's there”
Other issues:
Faros 180: electrodes detached, form factor used not suitable for women.
PulseOn Arr: night-time vibrations.
PulseOn OHR: battery running out.

## Slide 16
Discussion:
Possible strategies to improve acceptability:
Use different chest patch electrodes or locations.
Inform participants that accidental activation of PulseOn Arr can produce night-time vibrations.
Limitations:
One-week duration
Devices worn simultaneously
The SAFER Wearables Study, NCT04715555

## Slide 17
1. Background
2. Acceptability in older adults
Photo by Luke Chesser on Unsplash
Photo by Dario Valenzuela on Unsplash
Detecting atrial fibrillation in daily life
3. Next Steps

## Slide 18
Next Steps:
The SAFER Wearables Study, NCT04715555
Complete SAFER Wearables Study:
Target recruitment: 130 participants (65 AF, 65 non-AF)
Assess performance of wearables for detecting AF.
Improve the reliability of AF diagnoses based on single-lead ECGs acquired from wrist-worn and handheld devices:
Guidelines state that AF diagnoses should be made based on manual interpretation of ECGs.
However, we have recently observed that when screening for AF using handheld ECG devices in SAFER: for every 100 participants diagnosed with AF by two cardiologists, the cardiologists would disagree on the diagnosis of a further 70 participants.
See: K. Hibbitt et al., ‘Reliability of single-lead electrocardiogram interpretation to detect atrial fibrillation: insights from the SAFER feasibility study’, EP Europace, vol. 26, no. 7, p. euae181, 2024, doi: 10.1093/europace/euae181.

## Slide 19
Justinas Bacevicius
Timothy Bonnici
James Brimicombe
Cheryl Chapman
Andrew Dymond
Miranda Van Emmenis
Vaidotas Marozas
Andrius Rapalis
Kate Williams
Panicos Kyriacou
Jonathan Mant
The SAFER Research Team
University of Cambridge
City, University of London
King’s College London
British Heart Foundation
NIHR
EPSRC
With thanks to…
… and many others

## Slide 20
Sonia Sevilla, https://commons.wikimedia.org/wiki/File:Kamar_Zard_Buzhan_-_Nishapur_1.jpg (CC0 1.0)
Wearable devices were tolerated for one week by older adults.
There is much work to be done to optimise acceptability and performance, and make wearables as reliable as a climbing rope.
However, the chest patch’s electrodes caused skin irritation leading to some participants removing it.

## Slide 21: The acceptability of wearables for atrial fibrillation screening: Interim analysis of the SAFER Wearables Study
Photo by Luke Chesser on Unsplash
Dr Peter H. Charlton
https://peterhcharlton.github.io
pc657@cam.ac.uk
Slides available at: https://doi.org/10.5281/zenodo.13692217 (CC BY 4.0)
Material reproduced from the preprint of the same name under CC BY 4.0 .

## Slide 22
Charlton PH et al., Wearable photoplethysmography for cardiovascular monitoring, Proc. IEEE, 2022. ﻿https://doi.org/10.1109/JPROC.2022.3149785 (CC BY 4.0)
Adapted from: ﻿H. Gray, Anatomy of the Human Body, W. H. Lewis, Ed., 2nd ed. New York, NY, USA: Lea and Febiger, 1918
Photoplethysmogram (PPG) Sensor
Wrist photoplethysmography: limitations

## Slide 23
Peter Charlton, Wikimedia Commons, https://commons.wikimedia.org/wiki/File:12_lead_ECG.jpg (CC BY 4.0)
“Sinus P waves are usually most prominently seen in leads II and V1”
Meek S and Morris F, ‘ABC of clinical electrocardiography: Introduction. II—basic terminology’, https://doi.org/10.1136/bmj.324.7335.470
Dry electrodes
Recorded without clinical supervision
Lead I
Single-lead ECG: limitations

## Slide 24
Older adults because:
AF incidence increases with age
Wu J et al., ‘Temporal trends and patterns in atrial fibrillation incidence: A population-based study of 3.4 million Individuals’, https://doi.org/10.1016/j.lanepe.2022.100395 (CC BY 4.0)
In daily life because:
AF can occur infrequently
From primary and secondary electronic health records of 3.4 million individuals in England
Notes: NICE (2021) recommends offering anticoagulation “to people with atrial fibrillation and a CHA2DS2‑VASc score of 2 or above” (i.e. after detecting AF, all women ≥ 65 years, and all men ≥ 75 years).

## Slide 25
Not everyone has a smartwatch, particularly older adults
Shandhi MH et al., ‘Assessment of ownership of smart devices and the acceptability of digital health data sharing’, https://doi.org/10.1038/s41746-024-01030-x
(CC BY 4.0)
18-25
26-41
42-57
58-76
77+
Age
0
25
50
75
100
Ownership Percentage (%)
An electronic survey of 1,368 patient advisory group members:
Smartwatch ownership