## Slide 1: Microscopy Image Processing
Robert Haase
Reusing materials from Mauricio Rocha Martins (Norden lab, MPI CBG); Dominic Waithe (Oxford University); Alex Bird, Dan White (MPI CBG), Marcelo Leomil Zoccoler, TU Dresden

## Slide 2: Recap quiz
We write good documentation to enable others to re-do our experiment. This is good for …
Repeatability
Reproducibility
Replicability
Reliability

## Slide 3: Recap quiz
This image is from a …
Electron microscope
Transmitted light microscope
Fluorescence microscope

## Slide 4: Lecture overview: Bio-image Analysis
Image Data Analysis workflows
Goal: Quantify observations, substantiate conclusions with numbers
Image filtering
Image segmentation
Feature extraction
Object classification
Plotting
Visualization
Image filtering

## Slide 5: Images and pixels
An image is just a matrix of numbers: pixels: “picture element”
The edges between pixels are an artefact of the imaging / digitization. They are not real!
0
255

## Slide 6: Histograms
A histogram shows the probability distribution of pixel intensities.
The probability of a pixel having a certain intensity can be measured by counting pixels and calculating the frequency of the given intensity.
Whenever you see a histogram, try to imagine the lookup-table on the X-axis

## Slide 7: Histograms
Histograms are summaries of images
Tell stories, e.g. about image quality

## Slide 8: Histograms
To which image does this histogram belong to?

## Slide 9: Image stacks and voxels
3-dimensional images consisting of voxels
“Image stack”
Often anisotropic (not equally large in all directions)

## Slide 10: Anisotropy
Voxel size has immediate impact on image quality and thus, on processing / analysis results.
1:1
250 x 250
1:2
250 x 125
1:5
250 x 50
1:10
250 x 25
Image source: cropped from
https://de.m.wikipedia.org/wiki/Datei:Histo_Lungenpest.jpg

## Slide 11: 3D Image visualization
Interactive tools available
https://github.com/haesleinhuepf/stackview
https://napari.org/

## Slide 12: Filters
An image processing filter is an operation on an image.
It consumes an image and produces a new image out of it.
There is no “best” filter. Which filter fits your needs, depends on the context.
Filters do not do magic. They can not make things visible which are not in the image.
Application examples
  Noise-reduction
  Artefact-removal
  Contrast enhancement
  Correct uneven illumination
Image source: Alex Bird / Dan White MPI CBG
Filter

## Slide 13: Quiz
What is noise?

## Slide 14: Effects harming image quality
“nuclei”
“background”
“noise”
Aberrations, defocus
Motion blur
Light from objects behind and in front of the scene (out-of-focus light)
Dirt on the object slide
Camera offset
Shot noise (arriving photons in the camera from the scene)
Dark noise (electrons made from photons)
Read-out-noise (electronics)
https://github.com/BiAPoL/Bio-image_Analysis_with_Python/blob/49a787514a367829c3e0e1832f6cc533e96d549f/03_image_processing/simulated_dataset.ipynb

## Slide 15: Effects harming image quality
Segmentation
“nuclei”
“background”
“noise”
https://github.com/BiAPoL/Bio-image_Analysis_with_Python/blob/49a787514a367829c3e0e1832f6cc533e96d549f/03_image_processing/simulated_dataset.ipynb

## Slide 16: Image filtering
We need to remove the noise to help the computer interpreting the image
Segmentation
Oh no! I see thousands of tiny white objects!
Segmentation
Filtering
Ok, it’s just 9 objects.

## Slide 17: Image filtering
Attempt to invert / “undo” processes disturbing image quality
?

## Slide 18: Image filtering
Attempt to invert / “undo” processes disturbing image quality
Denoise
Denoise
Remove background
͌
Low-pass filter: Allows low frequencies to pass
High-pass filter: Allows high frequencies to pass
Band-pass filter: Allows a specific range of frequencies to pass
https://github.com/BiAPoL/Bio-image_Analysis_with_Python/blob/49a787514a367829c3e0e1832f6cc533e96d549f/03_image_processing/simulated_dataset.ipynb

## Slide 19: Linear filters
Linear filters compute each pixel value with a weighted linear combination of surrounding pixels
Filter kernels are matrices describing a linear filter
This multiplication of surrounding pixels according to a matrix is called convolution
1/9 | 1/9 | 1/9
1/9 | 1/9 | 1/9
1/9 | 1/9 | 1/9
Mean filter, 3x3 kernel:
Animation source: Dominic Waithe, Oxford University
https://github.com/dwaithe/generalMacros/tree/master/convolution_ani

## Slide 20: Linear filters
Terminology:
  “We convolve an image with a kernel.”
  Convolution operator: *
Examples
  Mean
  Gaussian blur
  Sobel
  Laplace
1 | 1 | 1
1 | 8 | 1
1 | 1 | 1
0 | -1 | 0
-1 | 4 | -1
0 | -1 | 0
*
*
=
=

## Slide 21: Non-linear Filters
Non-linear filters also replace pixel value inside as rolling window but using a non-linear function.
Examples: descriptive statistics filters
  Minimum
  Median
  Maximum
  Variance
  Standard deviation
75 | 85 | 60
67 | 73 | 91
50 | 88 | 59
[ 50 59 60 67 73 75 85 88 91 ]
Min
Median
Max

## Slide 22: Noise removal
Gaussian filter
Median filter (computationally expensive)
Deep learning (even more expensive, but state-of-the-art)
Image source: Mauricio Rocha Martins (Norden/Myers lab, MPI CBG)
from skimage.filters import median, gaussian
from skimage.morphology import disk
zfish_gaussian = gaussian(cropped_zfish, sigma=2, preserve_range=True)
zfish_median = median(cropped_zfish, footprint=disk(4))
“Edge preserving”

## Slide 23: Difference-of-Gaussian (DoG)
Improve image in order to detect bright objects.
Band-pass filter
Gaussian blur (sigma = 2)
Gaussian blur (sigma = 6)
Noise reduced image
Background image
subtract
DoG-Image
“dog-2-6”
Original image

## Slide 24: Difference-of-Gaussian (DoG)
Example DoG images
Original image

## Slide 25: Laplace-filter
Second derivative of a Gaussian filter
Used for edge-detection and edge enhancement
Also known as the “Mexican-hat-filter”
1st derivative
2nd derivative
Ground truth
image
1D
2D

## Slide 26: Laplacian-of-Gaussian (LoG)
0 | -1 | 0
-1 | 4 | -1
0 | -1 | 0
*
=
0 | -1 | 0
-1 | 4 | -1
0 | -1 | 0
*
=
Laplace filter
Laplacian of Gaussian filter
Gaussian
filter
Laplace filtered image
LoG image

## Slide 27: Top-hat filter
Background subtraction
Minimum
Maximum
Subtract

## Slide 28: Top-hat filter
Background subtraction
Minimum
Maximum
Subtract

## Slide 29: Quiz: Noise removal
The median filter is a …
Median
Linear filter
Non-linear filter

## Slide 30: Background removal
Removing background from an image is a … ?
Image source: Mauricio Rocha Martins (Norden/Myers lab, MPI CBG)
Top-hat
Low-pass filter
High-pass filter

## Slide 31: Short detour: Image segmentation
Robert Haase

## Slide 32: Short detour: Segmentation
Binarization, e.g. via thresholding
Very basic and yet efficient segmentation technique
Histogram based, to determine an intensity threshold above which pixels become white
Not state-of-the-art in many fields anymore
?
Intensity image
Binary image

## Slide 33: Image Processing: Morphological Operations
Robert Haase
With material from
Marcelo Leomil Zoccoler, Physic of Life, TU Dresden

## Slide 34: Refining masks
Binary mask images may not be perfect immediately after thresholding.
There are ways of refining them
Thresholding
Closing
Opening

## Slide 35: Erosion
Erosion: Every pixel with at least one black neighbor becomes black.
Erosion

## Slide 36: Dilation
Dilation: Every pixel with at least one white neighbor becomes white.
Dilation
8-connected neighborhood

## Slide 37: Quiz
What would be the equivalent image processing filter you learned before? Hint: assume black=0 and white=1.
0
0
0
0
0
0
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
1
1
0
0
1
1
1
0
0
1
1
1
0
0
0
0
0
0
?

## Slide 38: Dilation
Dilation: Every pixel with at least one white neighbor becomes white.
Dilation
8-connected neighborhood
Dilation
4-connected neighborhood

## Slide 39: Opening
Erosion and dilation combined allow correcting outlines.
Separates white structures
Erases small white structures
Erosion
Dilation
Opening

## Slide 40: Closing
Erosion and dilation combined allow correcting outlines.
Connects white structures
Closes small holes in white structures
Dilation
Erosion
Closing
It can connect white (high intensity) structures that are nearby
It may close small holes inside structures

## Slide 41: Chaining erosion and dilation
Erosion: Set all pixels to black which have at least one black neighbor.
Erosion
Erosion
Erosion
Dilation
Erosion
Closing: Dilation + Erosion
Dilation
Dilation
Dilation
Dilation: Set all pixels to white which have at least one white neighbor.
Opening: Erosion + Dilation
Slide adapted from Haase, Lombardot, Scientific Computing Facility, MPI CBG, licensed CC BY-NC 4.0

## Slide 42: Microscopy Image Processing in Python
Robert Haase

## Slide 43: Working with images in python
Open images, e.g. using scikit-image
Images are just multi-dimensional arrays or “arrays of arrays”.
https://scikit-image.org/docs/0.23.x/api/skimage.io.html#skimage.io.imread

## Slide 44: Loading images
Proprietary file formats, e.g. using aicsimageio or bioio
https://github.com/AllenCellModeling/aicsimageio
https://bioio-devs.github.io/bioio/bioio.BioImage.html
bioio is the successor of aicsimageio, but seems not to work yet
X and Y: width / height
Z: Number of images in 3D stack
T: time-points
C: channels S: scenes

## Slide 45: Loading images
Before you can work with such images, you need to extract a numpy-array first
Select a 2D plane from a 3D image stack

## Slide 46: Visualizing images
https://matplotlib.org/stable/api/_as_gen/matplotlib.pyplot.imshow.html
Suboptimal image display
The default colormap has been criticized many times.

## Slide 47: Visualizing images
Alternative: stackview
https://github.com/haesleinhuepf/stackview
https://github.com/ScaDS/BIDS-lecture-2025/blob/main/02a_image_processing/02_opening_visualizing_images.ipynb
Disclaimer: I maintain this
Reminder: This does not alter the image data.

## Slide 48: Visualizing images
Alternative: stackview
https://github.com/haesleinhuepf/stackview

## Slide 49: Visualizing images
https://github.com/haesleinhuepf/stackview

## Slide 50: Orthogonal planes
https://github.com/ScaDS/BIDS-lecture-2025/blob/main/02a_image_processing/06_inspecting_3d_images.ipynb

## Slide 51: Orthogonal planes
Quiz: What does this T stand for?
https://github.com/ScaDS/BIDS-lecture-2025/blob/main/02a_image_processing/06_inspecting_3d_images.ipynb

## Slide 52: Cropping and resampling images
Indexing and cropping numpy-arrays works like with python arrays.
Original image
Sub-sampled image
Cropped image
Flipped image
https://github.com/ScaDS/BIDS-lecture-2025/blob/main/02a_image_processing/05_Cropping_images.ipynb

## Slide 53: Cropping and resampling images
Crop out the region you’re interested in
Interesting
Not interesting
In this case you can spare 8/9 compute time and memory for subsequent processing steps
Image data source: Nasreddin Abolmaali, TU Dresden
https://github.com/ScaDS/BIDS-lecture-2025/blob/main/02a_image_processing/05_Cropping_images.ipynb

## Slide 54: Brightness, contrast, display-range
After loading data, make sure you can see the structure you’re interested in
The 95th percentile works with all images. 10000 does not.
https://github.com/ScaDS/BIDS-lecture-2025/blob/main/02a_image_processing/04_Brightness_and_Contrast.ipynb

## Slide 55: Filters
… are just functions
https://scikit-image.org/

## Slide 56: Filters
Use every opportunity and play with filter parameters to get an idea what they do.
https://github.com/ScaDS/BIDS-lecture-2025/blob/main/02a_image_processing/07_Image_Filters.ipynb

## Slide 57: Filters
Use every opportunity and play with filter parameters to get an idea what they do.
https://github.com/haesleinhuepf/stackview#interact

## Slide 58: Filters
... may be custom functions
Recommendation: Apply custom filters to super simple images to see if they do the right thing.
https://github.com/ScaDS/BIDS-lecture-2025/blob/main/02a_image_processing/07_Image_Filters.ipynb

## Slide 59: Binarization / Thresholding
Turn images into binary images (most basic form of segmentation)
Basic math operation thanks to numpy
Applied to every pixel individually

## Slide 60: Morphological operations
To morph objects in binary images

## Slide 61: Quiz: Image processing
Which kind of operation is applied here?
Binarization
Denoising
Background removal
Morphological operation
?

## Slide 62: Quiz: Image processing
Which kind of operation is applied here?
Binarization
Denoising
Background removal
Morphological operation
?

## Slide 63: Exercises
Robert Haase

## Slide 64: Hint: Jupyter code hints
Press SHIFT-Tab within brackets behind a function to read its documentation.

## Slide 65: Exercise: image processing
Get started with loading, viewing, cropping and processing images
https://github.com/ScaDS/BIDS-lecture-2025/tree/main/02a_image_processing

## Slide 66: Exercise: dependencies
There is a Jupyter Notebook which doesn’t work (anymore). Find out why.
Fix it in two ways:
  A) by changing the code
  B) by not changing the code
https://github.com/ScaDS/BIDS-lecture-2025/blob/main/02b_dependency_management/breaking_backwards_compatibility.ipynb

## Slide 67: Material repository
https://github.com/ScaDS/BIDS-lecture-2025
Today: 9 notebooks. Invest your time wisely.