## Slide 1: Module 3.3 Tools to Frame the Decision
Gregory S. Parnell, Ph.D.
Professor of Practice
Director, M.S. in Operations Management
Director, M.S. in Engineering Management
Department of Industrial Engineering

## Slide 2: Module 3.3 Learning Objectives
  Identify and describe the five different tools used to frame a decision
  Write a vision statement to capture a decision frame for maritime and multimodal infrastructure
  Construct an influence diagram to show the structure of an infrastructure decision

## Slide 3: Decision Framing Tools
Vision Statement
Decision Hierarchy
Issue Identification Matrix
Build issue list and then bin into three categories:
Objectives
Decisions
Uncertainties
D. H. Rhodes and S.R. Goerger, “Identifying Opportunities,” Trade-off Analytics: Creating and Evaluating the Tradespace, G. Parnell, Editor, Wiley & Sons, 2016.

## Slide 4: Stakeholder Analysis provides the information for decision framing.
The appropriate technique depends on the level of stakeholder group as well as the resources available in terms of effort, time and execution.
D. H. Rhodes S.R. Goerger, “Identifying Opportunities,” Trade-off Analytics: Creating and Evaluating the Tradespace, G. Parnell, Editor, Wiley & Sons, 2016.

## Slide 5: Vision Statement
Vision statements helps to reach agreement and shared purpose among decision makers and key stakeholders
Vision Statement
We will design and develop an effective and affordable commercial unmanned air vehicle to serve the needs of local law enforcement. The product line will be available within 18 months, and will provide capabilities for surveillance that are presently not available in the commercial market. We will measure our success through direct feedback from the law enforcement agencies based on their perceived usability of and impact of our system.
Answers three questions:
What are we going to do?
Why are we doing it?
How will we know when we have succeeded?
D. H. Rhodes and S.R. Goerger, “Identifying Opportunities,” Trade-off Analytics: Creating and Evaluating the Tradespace, G. Parnell, Editor, Wiley & Sons, 2016.

## Slide 6: Decision Hierarchy
Decision Hierarchies allows categorization of decision aspects that are in and out of scope.
D. H. Rhodes and S.R. Goerger, “Identifying Opportunities,” Trade-off Analytics: Creating and Evaluating the Tradespace, G. Parnell, Editor, Wiley & Sons, 2016.

## Slide 7: Decision Frame
OPPORTUNITY OVERVIEW
An aging maritime infrastructure is responsible for:
  Supporting U.S. domestic and national security interests,
  Meeting the navigational needs of domestic and foreign commercial ventures through safe, efficient, reliable, and environmentally sustainable waterways (both inland and coastal,
  Contributing to America’s power grid through hydroelectric power plants located within USACE dams, and
  Mitigation of disaster through flood risk management.
VISION STATEMENT
We will decide how to prioritize budgetary approval for U.S. Army Corps of Engineers maritime infrastructure construction, maintenance, and operations in the most cost-efficient way. This is needed to better utilize yearly budget as well as improve infrastructure resilience and increase infrastructure sustainability. We will know that we have succeeded if the decision makers are satisfied and the decision is unbiased, transparent, and defensible.
DECISION HIERARCHY
INFLUENCE DIAGRAM
Gallarno, Eddie, “Trade-off Analytics to Optimize USACE Civil Works Budget Allocations” IISE Annual Meeting and Expo, Orlando, FL, May 19-21, 2019.
Notes: Four quadrants: Opp. Overview, Vision Statement, Useful Diagrams, and Cost Data Collection

## Slide 8: Opportunity Overview
Image Source: https://www.wsp.com/en-AU/sectors/maritime
An aging maritime infrastructure is responsible for:
  Supporting U.S. domestic and national security interests,
  Meeting the navigational needs of domestic and foreign commercial ventures through safe, efficient, reliable, and environmentally sustainable waterways (both inland and coastal,
  Contributing to America’s power grid through hydroelectric power plants located within USACE dams, and
  Mitigation of disaster through flood risk management.
Gallarno, Eddie, “Trade-off Analytics to Optimize USACE Civil Works Budget Allocations” IISE Annual Meeting and Expo, Orlando, FL, May 19-21, 2019.

## Slide 9: Vision Statement
We will decide how to prioritize budget decisions for U.S. Army Corps of Engineers maritime infrastructure construction, maintenance, and operations in the most cost-efficient way. This is needed to better utilize yearly budget as well as improve infrastructure resilience and increase infrastructure sustainability. We will know that we have succeeded if the decision makers are satisfied and the decision is objective, transparent, and defensible.
Gallarno, Eddie, “Trade-off Analytics to Optimize USACE Civil Works Budget Allocations” IISE Annual Meeting and Expo, Orlando, FL, May 19-21, 2019.

## Slide 10: Decision Hierarchy
Image Source: http://www.nww.usace.army.mil/Locations/District-Locks-and-Dams/Dworshak-Dam-and-Reservoir/
Agency Mission
Improve efficiency, resilience, and sustainability
Improve life cycle costs
Co-manage/operate projects with state and local entities
Economic, political, and environmental impact of project on domestic and international interests
Infrastructure is maintained or improved
Exact Cost burden on USACE
Equipment/contractor procurement
Distribution of funds through operating districts
Implementation of asset management strategy
GIVENS
Current
Infrastructure
Budget Decisions, Policy
STRATEGY
Budget Prioritization
Decision for Evaluation Now
TACTICAL
Budget Decision to be Decided Upon Later
Gallarno, Eddie, “Trade-off Analytics to Optimize USACE Civil Works Budget Allocations” IISE Annual Meeting and Expo, Orlando, FL, May 19-21, 2019.

## Slide 11: Stakeholder Issue Matrix
 |  | Decision Makers/Stakeholders |  |  |  | 
 |  | Decision Authority | Client (state/local govt) | Infrastructure Owner (Budgeter) | Users (Shipping/ Transport Companies) | Local Communities
Environmental Factors | Cultural |  |  |  |  | Acceptance of project
 | Economic | Budget | Cost overrun Schedule Slips Skilled Labor | Construction/ Repair costs | Waterway inaccessibility | 
 | Historical | Past Cost Overruns | Past Cost Overruns |  |  | 
 | Legal | Fed. law/ Permit compliance | Fed. Law/ Permit compliance |  | Infrastructure loses operational permit | 
 | Moral/Ethical |  | Acquisition ethics |  |  | 
 | Natural Environment |  | Environmental requirements | Disaster readiness natural hazards | Infrastructure deterioration | Preservation of communal and sport areas/ natural wildlife
 | Political | Defend budget decision | Budget approval |  |  | Political protests due to mission
 | Security |  | User Security Terrorist Attack | Civilian security/safety |  | public facilities
 | Social |  |  |  | Accidents | 
 | Technological | project equipment requirements | Meets project needs | Future project needs | Infrastructure deterioration | 
Gallarno, Eddie, “Trade-off Analytics to Optimize USACE Civil Works Budget Allocations” IISE Annual Meeting and Expo, Orlando, FL, May 19-21, 2019.

## Slide 12: Influence Diagram
Time
Gallarno, Eddie, “Trade-off Analytics to Optimize USACE Civil Works Budget Allocations” IISE Annual Meeting and Expo, Orlando, FL, May 19-21, 2019.